## Slide 1: Validation Progress and Plans for ENDF/B-VIII.1β1 at ORNL
B.J. Marshall and T.M. Greene
Mini-CSEWG
Livermore, CA
April 27, 2023

## Slide 2: Outline
ORNL definition of ENDF/B-VIII.1β1
keff results for CE calculations with VALID
Preliminary RCA result
Future plans for additional validation

## Slide 3: ORNL Definition of 8.1-beta1
  neutrons : commit 9611a57, tag = version.VIII.1-Beta1
  gammas : commit dd78fe0, <no tags>, phase2 (unused!)
  thermal_scatt : no beta1, attempt was made to predict
    phase1
      *ZrHx*
      H-H2O
      Si
      Mg
      H-Mesitylene
      H-Toluene
    ORNL_TSL_EVALUATIONS
      C8H8
      CH2
      C5O2H8
    phase2
      Everything not listed above
ENDF/B-VIII.1-beta1 (as of Apr. 4th, 2023)

## Slide 4: VALID benchmarks
VALID suite at ORNL has been expanded in recent years to include more ICSBEP benchmarks
More categories of experiments are covered, though some of them have very few cases
Deuterium- and polyethylene-moderated systems have been added, expanding validation basis for moderators beyond light water

## Slide 5: HEU Results
Category | Number of Cases | ENDF/B-VIII.0 |  | ENDF/B-VIII.1β1 | 
 |  | C/E | σ | C/E | σ
HMF | 91 | 1.00016 | 0.00026 | 1.00026 | 0.00026
HMI | 6 | 1.00079 | 0.00042 | 0.99956 | 0.00042
HMF/HMI (ZEUS) | 8 | 1.00320 | 0.00101 | 1.00192 | 0.00101
HST (1H) | 57 | 0.99904 | 0.00075 | 0.99996 | 0.00075
HST/I (2H) | 6 | 0.98936 | 0.00182 | 0.99161 | 0.00183
HCT (2H) | 9 | 1.00184 | 0.00230 | 1.00282 | 0.00231
HST/HCT (2H) | 15 | 0.99685 | 0.00156 | 0.99834 | 0.00157

## Slide 6: HMF results

## Slide 7: LEU and IEU results
LCT results may be degraded slightly (-0.00043 ± 0.00027)
LST results potentially improved (0.00075 ± 0.00117)
IST results may be slightly improved (-0.00060 ± 0.00109)
Category | Number of Cases | ENDF/B-VIII.0 |  | ENDF/B-VIII.1β1 | 
 |  | C/E | σ | C/E | σ
LCT | 144 | 0.99911 | 0.00019 | 0.99868 | 0.00019
LST | 19 | 0.99845 | 0.00083 | 0.99920 | 0.00083
IST | 59 | 1.00120 | 0.00077 | 1.00060 | 0.00077

## Slide 8: LCT results plot

## Slide 9: MIX results
Degraded performance in both MCT and MST experiments
MCT: -0.00311 ± 0.00082
MST: -0.00177 ± 0.00222
Category | Number of Cases | ENDF/B-VIII.0 |  | ENDF/B-VIII.1β1 | 
 |  | C/E | σ | C/E | σ
MCT | 49 | 0.99555 | 0.00058 | 0.99244 | 0.00058
MST | 10 | 0.99354 | 0.00157 | 0.99177 | 0.00157

## Slide 10: MCT results plot

## Slide 11: PU results
Little change in fast, intermediate, or mixed systems
Slight improvement in thermal systems (0.00134 ± 0.00072)
Category | Number of Cases | ENDF/B-VIII.0 |  | ENDF/B-VIII.1β1 | 
 |  | C/E | σ | C/E | σ
PMF | 25 | 1.00011 | 0.00045 | 0.99997 | 0.00045
PST | 92 | 0.99836 | 0.00051 | 0.99970 | 0.00051
PMM | 5 | 1.00422 | 0.00108 | 1.00408 | 0.00108

## Slide 12: PST results plot

## Slide 13: 233U results
Generally better performance for mixed and intermediate solution systems
Thermal solutions significantly more reactive, with similar magnitude bias
Category | Number of Cases | ENDF/B-VIII.0 |  | ENDF/B-VIII.1β1 | 
 |  | C/E | σ | C/E | σ
UCT | 3 | 0.99818 | 0.00140 | 1.00368 | 0.00140
UMF | 10 | 0.99860 | 0.00051 | 0.99874 | 0.00051
USI | 29 | 0.97945 | 0.00123 | 0.98761 | 0.00124
USM | 8 | 0.97546 | 0.00214 | 0.98411 | 0.00216
UST | 140 | 0.99750 | 0.00052 | 1.00281 | 0.00053

## Slide 14: 233U solutions trend with neutron spectrum

## Slide 15: VALID summary
Performance of ENDF/B-VIII.1β1 is improved for 233U and PST systems
  Trend in 233U solutions not greatly improved, but overall level is better
Small performance decrement in LCT systems
Cumulative χ2/DF metric is better for ENDF/B-VIII.1β1 than for ENDF/B-VIII.0 for VALID benchmarks
  2.85 for ENDF/B-VIII.0 vs 2.63 for ENDF/B-VIII.1β1
  Driven by improvement in 233U cases
More analysis on-going to provide more detailed feedback

## Slide 16: Preliminary RCA assessment for GKN sample
These results are relative to ENDF/B-VII.1
Small improvement in performance!
  ENDF/B-VII.1 <C/E> = 1.04891
  ENDF/B-VIII.1 <C/E> = 1.04203
Marked improvement for U-235
ENDF/B-VIII.0 will be included in further testing

## Slide 17: Future validation plans
Depletion validation
  (More) RCA samples
  Decay heat
Shielding validation
  Benchmarks in SCALE validation report
  Transmission testing
Reactor physics validation
  Core reactivity trajectory
  CASL/VERA test suite
  Advanced reactor test cases

## Slide 18: Acknowledgment
This presentation was supported by the Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration for the Department of Energy.

## Slide 19: Questions?