INTT HV GUI
Joseph Bertaux
Purdue University

---
Overview
INTT will supply power to the ROC boards and Ladders using WIENER MPOD modules

---
Overview
- INTT’s High-Voltage GUI will be a graphical front-end for monitoring
  - Implemented with PySimpleGUI
  - Calls SNMP commands send and retrieve information from MPOD modules

---
Example
There is a tab for each layer of the INTT (currently only two tabs in example)
Each ladder is a row
Each sensor can be assigned an MPOD channel (multiple can be the same—no constrictions on how the IP and Channel are assigned to a sensor

---
Progress
- Can communicate with the MPOD module in Si Lab
- Need to set up on OPC0
- Need to be able to print currents on order of 10^-7 or 10^-8 A (unless our operating range is higher than uA)
- Implement additional features as needed