## Slide 1: ML QA Data Analysis/Clustering
2023 USMDP Collaboration Meeting
Presenting work of intern Alberto Plebani
Co-supervised by Reed Teyber (LBNL), Emanuela Barzi (FNAL)
With inputs from Maxim Marchevsky, Diego Arbelaez

## Slide 2: Background - Inter-Layer Quench Antennas
A suite of diagnostics have been implemented in subscale magnets (lead by Maxim Marchevsky)
One diagnostic is the inter-layer Quench antennas
  Integrated into magnet yielding sensitive measurements
  Dipole bucked (left-right)
  Elements every 30 degrees
Dataset contains 4 magnets, 8 thermal cycles
  Recorded at 25 kHz along ramp through quench

## Slide 3: Background – The Common quench
Many quenches across subscale magnets look remarkably similar
  A characteristic frequency ~ 1kHz that we associate with current redistribution phenomena
    Corroborated by high-resolution cable quench simulations by Ruben Keizer (Twente/CERN)
  We impose this experience on our approach
In other words, for quench antennas:
  Mechanical activity has many “shapes and sizes”
  Current redistribution (i.e. quench) can have clear signatures
  Where along ramp do we see redistribution?
  What does this mean?

## Slide 4: Outline
Summer internship work of Alberto Plebani
  Co-supervised by myself and Emanuela Barzi
  Presenting today on his behalf
“Birds eye view” - charge to student
  Take continuous ramp data, extract all ramp events + quench
    Single antenna element only
  Find features that characterize the events
  K-means to cluster data
    What are the cluster centroids?
    What ramp events get clustered / show similarities with the quench?

## Slide 5: Extract ramp events
Threshold to identify events
  Explored filtering, various selection, et cetera
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)
9 ramps, quench events shown
Some quenches from other magnet locations

## Slide 6: Define Features
Many, many features explored
  Maximum antenna voltage
  Maximum voltage integral
  Signal Widths / shape
  Proxies for frequency content
    Dominant frequency
    Measure of 1 kHz content
  Many more explored
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 7: Preliminary Results
K-means clustering – 3 centroids
  Iteratively find centroids to minimize distance from centroids to each event
  3 features, no dimensionality reduction (presented today)
Quench
events
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)
High Amp. -> “1kHz”

## Slide 8: Cluster 2
25 randomly selected “cluster 2” events
  Large amplitude, correlated with ~ 1kHz – includes many quenches
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 9: Cluster 1
25 randomly selected “cluster 1” events
  Long, low-amplitude events
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 10: Cluster 0
25 randomly selected “cluster 0” events
  Small, fast-decay events
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 11: Ramp Activity
Presented on Monday
Several “cluster 2” events along ramp show similarities with quench events
  Suggests disturbances that cause redistribution during ramps – ”small quenches that recover”
  Not yet done – analyze trends where this occurs
Ramp event
– not a quench
Low pass filter
- Looks like a quench!
High pass filter
Typical Quench
Cluster “associated” with redistribution
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 12: Concluding Remarks (1/2)
Methods employed today are great starting point - but moving forward…
  Should use more antennas, more ramps, more features, implement dimensionality reduction,…
  More sophisticated clustering techniques e.g. NN-based
  Could consider manually labeled events and use supervised techniques
Excellent work over very short amount of time by Alberto Plebani
  Collaboration with Emanuela Barzi (FNAL) and myself (LBNL)
Wish internship was longer – student left as interesting results started being generated
  Needs a focused effort – from either myself or a new student
Yet, a very nice outcome from experience!
  Student presented this work during applications and was just offered a Ph.D. position at Cambridge (ATLAS)!
Alberto Plebani, Co-supervised by Reed Teyber (LBNL) and Emanuela Barzi (FNAL)

## Slide 13: Concluding Remarks (2/2)
Quench antennas are historically a diagnostic – ”to be analyzed later”
But, if we know what frequency range to look for, and the antenna amplitudes of a quench are “unique”….
  Could be interesting to build a real-time quench detection system!
  Microcontrollers these days can do spectral analysis, linear algebra, basic machine learning (TensorFlow Lite),…

## Slide 14: Backup Slides

## Slide 15: Signal Processing
Rate of change of magnetic flux induces antenna voltage
Integral of induced antenna voltage gives net change in flux
  Displacement of a wire from position a to b through dipole field gives constant, path-independent integrated voltage [V-S]
Quench antennas are sensitive to mechanics and current redistribution– how to isolate quench location?
  Integral removes periodic content (mechanics / vibration)
  Quench location - antenna with largest norm of [V-s] up to constant magnet voltage (red vertical line)
The signal shown here (location and frequency) is remarkably prevalent in all subscale magnet tests
  Low frequency (~ 1 kHz) “stationary” signal
~ 1 kHz

## Slide 16: K-means clustering
We have to tell K-means how many clusters to look for
  Example on right – clustering hand-written digits, would expect 10 clusters
  Need to repeat clustering analysis for many # of clusters
    Look for “performance” vs. number of clusters
  3 chosen here
Example from scikit-learn
From Alberto
# Clusters

## Slide 17: Dimensionality Reduction
K-means clustering
  A simple but powerful technique to create labels for unlabeled data
  Iteratively find new centroids to minimize Euclidean distance from centroids to each ramp event
  Too many features -> run into issues with dimensionality
Principal Component Analysis
  Singular Value Decomposition-like
  Find new orthogonal axis, reduced in number, that minimizes “data loss”
Center and Scale
  For each feature, center (subtract mean over all ramp events) and divide by standard deviation
  Failure to do this - clustering will be dominated by the single feature with largest magnitudes
“New” features (3)
Original Features (7)