## Slide 1: RHIC/AGS Annual User’s Meeting ePIC Readout Electronics
Fernando Barbosa (JLab), L3 CAM
Jeff Landgraff (BNL), L3 CAM
Jin Huang (BNL)
ePIC Electronics & DAQ WG Conveners
2 August 2023
BNL, Upton, NY

## Slide 2: Outline
Requirements and Design Philosophy
Streaming Readout Architecture
  Readout Chain – Functions and Nomenclature
Readout Channels
  eRD109 Proposals
  Summary of Electronics Developments
  ePIC Full Readout Chain
Summary

## Slide 3: Requirements and Design Philosophy
Front-End Boards custom designed for each detector, populated with ASICs/COTS, operate in large magnetic fields.
ASICs/COTS process analog signals and digitization tailored to each type of detector technology, data reduction (e.g., zero suppression) desirable.
Maximize synergies in electronics and minimize cabling.
Electronics, including digitizers, close to the detector as much as possible and where applicable.
Prefer to limit FPGA use inside detector volume.
Serviceability as a design criteria.
Triggerless operation of the electronics as default; triggered operation for calibration, test, de-bugging.
Meet current US standards per NEC, UL, FCC, NEMA.

## Slide 4: EIC Streaming Readout Architecture
Data
Configuration & Control
Power
Detector
FEB
(Front End Board)
RDO
(Readout Board)
DAM + Computing (Data Aggregation Module)
Storage
ASIC
FPGA
Power Supply System
(HV, LV, Bias)
Cooling Systems
Fiber
LVDS ~ 20-30 m*
Analog ~ 20m
Fiber
L ~ 100 m
fiber
Monitoring
BW: O(100 Tbps)
BW: O(10 Tbps)
Goal: O(100 Gbps)
FEB
FEB
RDO
Switch / Server / Link-Exchange: Readout
Switch / Server: Processing
Switch / Server: Buffer
Total
w/ Jin and Kai
Bunch Crossing ~ 10.2 ns/98.5 MHz
Event Rate ~ 2 us/500 kHz
Low occupancy.
Jitter ~ 5 ps
Front-End Electronics
DAQ
GTU
(Global Timing Unit)
*LVDS – ANSI/TIA/EIA-644A standard. Maximum cable length dependent on data rate.

## Slide 5: EIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
-Multi-Channel Sensor
-MAPS
-AC-LGAD
-MPGD
-MCP-PMT
-SiPM
-LAPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA

## Slide 6: ePIC Readout Channels (w/ Project P6 updates) – Refinements are on-going, e.g. Astropix, Timepix.
Detector System | Channels | Nominal Readout Technology | eRD109 Initiatives
Si Tracking: 3 vertex layers, 3 sagitta layers, 4 backward disks, 5 forward disks | 7 m^2 32 B pixels 5,200 MAPS sensors | MAPS – ITS-3 | 
MPGD tracking: 3 layers | 100k | Strips | SALSA
Calorimeters: (in P6) Forward: LFHCAL pECAL Barrel: HCAL ECAL Backward: ECAL nHCAL | 31640 19000 1536 5760 3256 3240 | SiPM | Discrete/HGCROC
Far Forward: B0: 3 MAPS layers 1 or 2 AC-LGAD layer 2 Roman Pots 2 Off Momentum ZDC: Crystal Calorimeter 32 Silicon pad layer 4 silicon pixel layers 2 boxes scintillator | 3x20cmx20cm (300M pixel) 300k or 600k 1M (4 x 135k layers each) 650k (4 x 80k layers each) 400 11520 160k 72 | MAPS – ITS-3 AC-LGAG AC-LGAD AC-LGAD APD Si PMT/SiPM | EICROC EICROC EICROC Discrete/HGCROC HGCROC Discrete/HGCROC
Far Backward: Low Q Tagger 1 Low Q Tagger 2 2 Calorimeters | 1.3M 480k 700 | AC-LGAD AC-LGAD PMT/SiPM | EICROC EICROC Discrete/HGCROC
PID-TOF Barrel TOF CTTL Hadron Endcap TOF FTTL | 3M-50M | AC-LGAD | EICROC
PID-Cherenkov: dRICH pfRICH DIRC | 5376 69632 69362 | SiPM HRPPD HRPPD | ALCOR EICROC EICROC

## Slide 7: eRD109 Status
 | Detector/Technology | Discrete/ASIC | Group | Awarded
A | Calorimeter | Discrete | IUCF | April 2023
B | Calorimeter | HGCROC | ORNL | April 2023
C | dRICH | ALCOR | INFN | April 2023
D | AC-LGAD | EICROC | Omega/IN2P3 | See below
 |  | FCFD | FNAL | June 2023
 |  | Barrel L-M Serv. Hybrid | ORNL | April 2023
 |  | 3rd Party Evaluation | UCSC | Pending Legal
E | MPGD/µRWell | SALSA | CEA | May 2023
 |  |  | USP | May 2023
FY23 - Contract awards have taken much longer than expected.
IN2P3 and OMEGA have committed considerable resources to the design of the ROC ASICs to meet the EIC streaming readout needs.
 | Detector/Technology | Discrete/ASIC | Group
A | Calorimeter | Discrete | IUCF
B | Calorimeter | HGCROC | ORNL
C | dRICH | ALCOR | INFN –BO, TO
D | AC-LGAD | EICROC | Omega/IN2P3/ IJCLab/CEA/IRFU
 |  | Barrel L-M Serv. Hybrid | ORNL
 |  | High Precision Clock Dist. | BNL/Rice/UIC/ORNL
E | MPGD/µRWell | SALSA | CEA/IRFU
 |  |  | USP
FY24 – Proposed and subject to DAC review 28-31 August 2023.

## Slide 8: ePIC Readout Electronics – Present Assessment
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD
 | MAPS | AC-LGAD, HRPPD | SiPM/PMT | MPGD
Tracking | 32 B |  |  | 100k
Calorimeters | 50M |  | 67k | 
Far Forward | 300M | 2.3M | 500 | 
Far Backward |  | 1.8M | 700 | 
PID |  | 3M-50M + 140k | 300k | 
TOTAL | 32 B | 7.1M-54M | 370k | 100k
ASIC | ITS-3 | EICROC | Discrete/COTS HGCROC3 ALCOR-EIC | SALSA
eRD109
HRPPD
EICROC and HGCROC families of ASICs have similar interfaces and follow similar developments at IN2P3/OMEGA/IRFU/IJCLab.
Commitment by IN2P3 and OMEGA narrows the ASIC field, favors convergence:

## Slide 9: Summary of Electronics Developments
Based on ALICE ALPIDE - 62 nm CMOS.
Tr < 2 us, 40 nW/pixel, 1.2 Gbps serial link
Radiation Tolerant.
MAPS – ITS-3 (Monolithic Active Pixel Sensor)
Adapter PCBs
FEB PCBs
Calorimeters – SiPMs – a) Discrete/COTS/ASIC (IU), b) HGCROCv3 (ORNL)
32 ch, Waveform, 12/14-bit
Cabling, Power, Cooling, Packaging.
72 ch, Charge (ADC+TOT), Time (TOA,25 ps)
Large Dynamic range, 2xGbps links, 20 mW/ch
40 MHz, SRO with FPGA
Radiation Tolerant

## Slide 10: ROC ASIC Developments
Triggerless, to be checked w/existing chip.
40 MHz operation from external clock with BX 98.5 MHz.
1280 Mbps @ 40 MHz.
Proposed HGCROC (based on H2GCROC3) – ePIROC?
No Change
Modify trig, mem, CLK dist.
Triggered Tests,
N. Novitzky
Proposed EICROC
Different input structure, similar interfaces as HGCROC.
A few variants possible (direct attach BGA, interposer, IC package, # Pixels) to fit detectors.
HGCROC
  1D, 72 ch.
  Cdin: 5-50 pF
  Dynamic Range: 1-10 pC
  Timing: 100-120 ps
  Power: 10-15 mW/ch
EICROC
  2D, 32x32, 1024 ch
  Cdin: 1-5 pF
  Dynamic Range: 1-50 fC
  Timing: 15-20ps
  Power: < 1 mW/ch

## Slide 11
dRICH – SiPM – ALCOR (INFN)
MPGD – SALSA (CEA-Saclay, U. Sao Paulo)
64-Ch, 110/65 nm CMOS, SiPM readout.
Amplification, conditioning, digitization.
Triggerless and triggered operation.
25 ps TDCs, 5 MHz input.
4 or 8x 640 Mbps LVDS links.
64-Ch, 65 nm CMOS.
Peaking time: 50 – 500 ns
Inputs: >200 pF; Dual polarity
Rates: ~100’s kHz)
ADC: 12 bits, 5 – 50 MSPS.
Extensive data processing capabilities.
Triggerless and triggered operation.
Power: 15 mW/Ch
Several 1 Gbps links.
Updated design from SAMPA v5
Migration to 65 nm CMOS.

## Slide 12
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD |  | RDOs / Fibers | DAM | Data Volume Estimate (Gb/s) | Data Volume To Tape (Gb/s)
 | MAPS | AC-LGAD | SiPM/PMT | MPGD | LAPPD |  |  |  | 
Tracking | 32 B |  |  | 100k |  | 415 | 11 | 15 | 15
Calorimeters | 88M* |  | 67k |  |  | 305 | 11 | 15 | 15
Far Forward | 300M | 2.3M | 500 |  |  | 174 | 5 | 1 | 1
Far Backward |  | 1.8M | 700 |  |  | 113 | 4 | 100 | 2
PID |  | 3M-50M | 300k |  | 150k | 1070 | 41 | 1856 | 45
TOTAL | 32 B | 7.1M-54M | 370k | 100k | 150k | 1662 | 72 | 1987 | 78
ePIC Full Readout Chain - Refinements are on-going.
RDO – Readout Board – Interface between FEBs and DAMs with:
    Aggregation, data formatting & readout, configuration & control, clock & timing.
    Data transport via fibers.
    A few design variants are planned.
DAM – Data Aggregation Module – Interface between DAMs and Computing:
    Aggregation, computing, configuration & control, clock & timing, software trigger.
    One design for ePIC.
Data volume to tape estimated to be less than 100 Gbps.

## Slide 13: Other current activities:
Location/partitioning of electronics under consideration: space, power, radiation, cabling – overall performance:
RDO/Timing subgroup – GTU/DAM/RDO clock timing validation tests (~5 ps).
by Irakli M.
On-detector for dRICH
by Jo S., Jeff L.

## Slide 14: Summary
ePIC is actively developing a streaming readout architecture, benefiting from resources within its large collaboration and to meet the physics goals of the EIC.
Developing the readout electronics by building upon previous developments, with design re-use as a guiding principle.
Engaging the community and benefiting from in-kind contributions.
Significant Progress:
  Readout architecture and nomenclature completed.
  Active design initiatives:
      ASICs/Discrete circuitry
      Full chain Interface standards (FEBs/RDOs/DAMs)
      Clock timing and distribution (GTU).
      DAQ Computing & Streaming Models.
Please join:
  • Mailing Lists – https://lists.bnl.gov/mailman/listinfo • Indico Agenda - https://indico.bnl.gov/category/402/ • Wiki - https://wiki.bnl.gov/EPIC