## Slide 1: Barrel HCAL SiPMs
J. Lajoie, C. Hughes

## Slide 2: The Barrel HCAL Scintillating Tiles
Scintillating Tile (shown unwrapped)
Tile Retainer Clip
Light block, SiPM mount and SiPM
(S12572-015P-02)
7680 total
Calibration Fiber

## Slide 3: Questions
What is the dynamic range one needs to cover?
  sPHENIX planned on 25 MeV – 50 GeV per tower (5 scintillator tiles) @200 GeV
    5 MeV – 10 GeV per tile, or 1 – 2000 (2.5 – 5000) pixels @ 200 (500) PE/GeV
    Should look at 18x275 GeV jets at h ~ 1 to verify range, suspect OK
What is the impact of radiation damage of the SiPMs on your system?
  Expected to be negligible, at outer radius of detector. No degradation anticipated in 3 (5) years of sPHENIX operation (HI).
  Is there a standard “per N years of operation” to estimate dose?
What specs have you already determined and how? What needs still be determined
  Based on existing design, we have a fixed physical package (3x3mm)
  Designed for 40000 pixels @ 15mm. Reduced pixel count might work but needs study
How do your SiPM specs impact the readout electronics, especially the FEEs.
  Plan to use HGCROC, piggy-back on ORNL HGCROC development for LFHCAL