## Slide 1: Opportunities at the Isotope Program
July 17, 2023
Cathy S. Cutler

## Slide 2: DOE Isotope Program Mission
Produce and/or distribute radioactive and stable isotopes that are in short supply; includes by-products, surplus materials and related isotope services
Maintain and upgrade the infrastructure required to produce and supply priority isotope products and related service
Conduct R&D on new and improved isotope production and processing techniques which can make available priority isotopes for research and application. Develop workforce.
Ensure robust domestic supply chains. Reduce U.S. dependency on foreign supply to ensure National Preparedness.
Isotopes are forms of the same element that contain equal numbers of protons but different numbers of neutrons in their nuclei, and hence differ in relative atomic mass but not in chemical properties; in particular, a radioactive form of an element.

## Slide 3
Applications – Accelerator Isotopes
Sr-82/Rb-82:
Generator- cardiac imaging
Ge-68/Ga-68:
Generator-
cancer imaging
Si-32: Environmental applications
Na-22: Source for PET imaging
Cd-109: X-ray fluorescence source
Notes: Focusing initially on accelerator isotope products, LANL and BNL are engaged in the routine production of Ge-68 for Ga-68 generator applications (cancer imaging) and Sr-82 for cardiac imaging application. Both sites produce a variety of other products like Cd-109 (for X-ray….), Na-22 (a calibration source for PET imaging) and Si-32 (for environmental imaging) to name a few. The accelerator sites are also engaged in active R&D campaigns to make new isotopes available for applications development in the areas of fundamental R&D, medical research, and national security applications
Ge-68 (271 day)/Ga-68 (68 min)
Sr-82 (25 day)/Rb-82 (75 sec)
Si-32 (approx 170 years)
Cd-109 (461 days)
Na-22 (2.6 years)

## Slide 4: Brookhaven Linac Isotope Producer
Proton beam
Cooling water
Target basket
106 MeV
97 MeV
30 MeV (C-slot)
68 MeV
RbCl 1
RbCl 2
degrader
BLIP target stack
BLIP schematics

## Slide 5: Opportunities for isotope Production and R&D
232Th(p,2p6n)225Ac
68Zn(p,2p)67Cu
natRb(p,xn)82Sr
82Sr - API for Bracco’s Cardiogen-82® generator
75As(p,4n)72Se
natGa(p,xn)68Ge
86Sr(p,n)86Y
186W(p,n)186Re
192Os(p,2np)189Re
45Sc(p,2n)44Ti
48Ti(p,2p)47Sc
Notes: Capable of producing high energy protons (up to 200 MeV)
High current (up to ~173 µA)
New raster magnet installed to more uniformly distribute the beam

## Slide 7: High Specific Activity 72As –
Imaging Isotope 72As (T1/2= 26 h)
Positron energy comparison
No-carrier added As-72 can be obtained from 72Se/72As generator
Accelerator production of 72Se from natRbBr(p,x) at high energy and 75As(p,4n) at intermediate energy has been reported
We are interested in 75As(p,4n) production route for which excitation functions up to 45 MeV have been reported
Isotope | 89Zr (3.27 d) | 68Ga (67.7 m) | 124I (4.18 d) | 72As (26 h)
Mean Eβ+, keV | 396 (22.7%) | 829.5 (88.9%) | 870 (22.7%) | 1170 (87.8%)
(p,n)
(p,4n)

## Slide 8: Measurements of 75As(p,x)
Irradiation conditions:
Target material: GaAs foil, d×h=2.5×0.00254 cm
Beam current: ~30 µA, focused beam
Irradiation time: 2 h
Incident energy: 117 MeV incident, lower points achieved by degradation with Al degraders
Aluminum foil used for beam monitoring
Work done by Dr. Anthony DeGraffenreid

## Slide 9: Excitation functions for Se-75 and Se-72 production from As

## Slide 10: TRi-Laboratory Effort in Nuclear Data (TREND)
Collaboration of BNL, LANL, LBNL
Formed to address a lack of nuclear data for predicting yields for desired isotopes as well as contaminants that are co-produced
Measured cross sections provide valuable data for isotope production, but also are important inputs into nuclear physics models for predicting cross sections across the chart of nuclides
Official Use Only

## Slide 11: Large scale production of 72Se at 105-103.5 MeV
Melting Point/ Decomposition
Aluminum arsenide (mp—1740 °C)
Gallium arsenide (mp—1240 °C)
Arsenic metal (sublimation—615 °C)
Thermal Conductivity and Density
Aluminum arsenide—84 W/mK; 3.81 g/cm3
Gallium arsenide—55 W/mK; 5.32 g/cm3
Arsenic metal—50.2 W/mK; 5.73 g/cm3

## Slide 13: Opportunities in MIRP- Separations
Process of purifying radioisotope of interest from bulk target materials.
Chemical differences
Atomic weight of the isotope
Radioanalytical techniques
ICP
Gamma Spectroscopy

## Slide 14: Opportunities within MIRP - Separations
Solvent Extraction
Isolation of 73Se from 16O irradiated Co targets
Radiochim. Acta 2012, 100, 865-870.
J. Radioanal. Nucl. Chem. 2002, 251, 159-162
Column Chromatography
72Se isolation from arsenic targets

## Slide 15: DGA membranes for Ac-225 purification (Part of a 2020 DOE Early Career Research Award)
1
Christine Duval
Asst. Professor, PI
Collaborators
Cathy S. Cutler, PhD
Jasmine Hatcher-Lamarre, PhD
Pavithra H.A. Kankanamalage, PhD
Megan Sibley
Post Doc
(now at ORNL)
Tuli Banik
Grad Student
Alexa Ford
Undergrad
Tim Yen
Undergrad
Maura Sepesy
Grad Student
@Duval_Lab
Official Use Only
Notes: Add a bullet point here that Ac-225 is successful but the supply is limited.

## Slide 16: Goal: reduce separation time from hours to minutes
Our approach is to use membrane adsorbers due to their potential for:
  High product capture at high flowrates – minimize product loss to decay
  Small bed volumes (sharp elution curves) – minimizing concentrative process steps
  Unlike resins, membranes can be stacked without appreciate rise in pressure drop
6
Sibley et al. “DGA-functionalized membranes for Ac-225 purification.” In preparation.
Notes: Tie this to improving from the drawbacks of resins

## Slide 17: Comparing Ac-225 resin & membrane data
Chart: [HNO3], M
| 4 | 6 | 10
 | 0.041969 | 0.013676 | 0.0015678
Figure 3: 1.25 mg membrane, 1 mL solution, 418 kBq Ac-225 (160 pg Ac-225) [2]
Figure 4: 50 mg resin, 1 mL solution, 5.9 kBq Ac-225 (3 pg Ac-225) [1]
[1] Radchenko et al. “Radiometric evaluation of diglycolamides resins for the chromatographic separation of actinium from fission product lanthanides.” Talanta. 2017, 175 (318-324)
[2] Sibley et al. “DGA-functionalized membranes for Ac-225 purification.” In preparation.
DGA resin
DGA membrane
16
Cannot directly compare the absolute value of the Kd because the measurements were made at different mass to volume ratios and with different initial concentrations of Ac-225 – but the trends are consistent with DGA resins

## Slide 18: Opportunities within MIRP - Generator Development
  A device that allows for the production of a short-lived radioisotope (daughter) following the decay of a long-lived radioisotope (parent)
    Easily transportable
  It allows for the use of shorter-lived radioisotopes without the need for a production facility (i.e. cyclotron) within a close proximity.
  Uses adsorbent material which has strong affinity for the parent nuclide and allows for simple removal of daughter nuclide
    Ion exchange resin
    Alumina
    zirconia

## Slide 19: Opportunities within MIRP - Radiolabeling and Preclinical Studies
Gastric Cancer Cell Uptake
18.5 times uptake in cells!!!
Free 72As
72As-Trastuzumab
1st images of indirectly labeled 72As-mAb!!

## Slide 20: Other modes of Isotope production
TR-19 Cyclotron
Provides protons- 13 - 19 meV
Beam current 200 µA
Supports gas, liquid, and solid targets

## Slide 21: Target Development for EBCO cyclotron
Isabella Pasha
Najah Curtis

## Slide 22: NCSS at BNL
An intensive six-week Summer School in Nuclear and Radiochemistry for undergraduates. NCSS 2023 started this Monday.
Sponsored by the Division of Nuclear Chemistry and Technology of the American Chemical Society (ACS DNC&T) and funding by the U.S. Department of Energy.
Provide fundamental training in nuclear and radiochemistry principles, particularly to physical science and engineering students from institutions that do not have such programs.
Stimulate interest in physical science and engineering undergraduates in graduate studies in fields founded in nuclear and radiochemistry.
Generate awareness and acceptance of nuclear technologies and application in society among participants.
12 students selected for each site primarily from institutions that do not offer nuclear studies
~48% of NCSS students continue to graduate studies in nuclear science.

## Slide 23: Presentation Summary
Various opportunities to engage with the isotope program
Visiting Faculty program, SULI program GEM, SURP
Projects on targetry, nuclear data, engineering, separations, radiolabeling, automation, modeling
NCSS for undergraduate's deep dive into radiochemistry and nuclear chemistry
Continue efforts to reach out and collaborate to provide access to unique facilities
Official Use Only