## Slide 1: Impedance Modeling And Collective Effects in ESR
Alexei Blednykh
EIC Accelerator Design Weekly Meeting
Jun 7, 2023
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 2: Overview
Electron Storage Ring (HSR)
  Impedance Budget
Summary
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 3: Calculation of the Pseudo-Green Function
An important part of wakefield simulation is determining the accuracy and numerical resolution required for a particular component.
Codes typically calculate the wakefield from a Gaussian bunch of rms length , so that the numerical mesh needs to be small enough.
To resolve the short-range wakefield accurately, the mesh size requires to be:
  in GdfidL. Parallel computing. Linux based.
  in ECHO 3D. Indirect integration method. No option for parallel computing yet.
The wakefield is used as a pseudo-Green function in tracking simulations to determine the collective effects impact on the beam dynamics.
The wakefield should be calculated with a source current whose length is
The requirements above drive the computer power resources.
RF heating and/or low frequency modes can be calculated using a source current .
Review Article, A. Blednykh, G. Bassi, V. Smaluk, and R. Lindberg, “Impedance modeling and its application to the analysis of the collective effects”, Phys. Rev. Accel. Beams 24, 104801 (2021).
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 4: ESR Beam Intensity
 | 5 GeV | 10 GeV | 18 GeV
Num. of electrons per bunch, | 1.7x1011 |  | 1.6x1010
Bunch Charge, | 27.6 nC |  | 2.5 nC
Number of Bunches, | 1160 | 1160 | 290
Single Bunch Current, | 2.2 mA |  | 0.2 mA
Bunch Length, | 22.7 ps | 25.4 ps | 30 ps
Peak Bunch Current, | 484 A | 433 A | 34 A
Average Current, | 2.5 A | 2.5 A | 0.23 A
 | 5 GeV | 10 GeV | 18 GeV
 | 1.7x1011 |  | 1.6x1010
 | 27.6 nC |  | 2.5 nC
 | 1160 | 1160 | 290
 | 2.2 mA |  | 0.2 mA
 | 22.7 ps | 25.4 ps | 30 ps
 | 484 A | 433 A | 34 A
 | 2.5 A | 2.5 A | 0.23 A
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 5: ESR Horizontal In-Vacuum Collimator
Computer Resources Usage
mesh fdtd
mesh fdtd
mesh ww
Available NSLS-II Computer Resources
23 x 24 CPU’s & 23 x 750 GB RAM
GdfidL Algorithms
  Finite Difference Time Domain (-fdtd)
  Moving Window (-windowwake)
Detailed conceptual design in C. Hetzel’s talk
The total length is 910mm, with a ~370mm taper length.
The middle section has a rectangular profile
Longitudinal short-range wakefield W(s)
Top View of the Tapered Transition
Transition
Collimator
20
Codes benchmarking: G. Wang, M. Blaskiewicz, A. Blednykh and M. Sangroula, IPAC2021 Proceeding, WEPAB032
D. Hidas
G. Wang
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 6: ESR Vertical Collimator (WyD)
V/pC/m for a 7mm bunch length
kV/pC for j=3
M. Valette, A. Drees, C. Hetzel, J. Belong, G. Wang, M. Blaskiewicz
Contribution of three VCLMs is ~30% of the present total vertical impedance budget.
20um STEPSIZE - GdfidL
At open position
If the minimum gap will be smaller as designed (12 mm).
Damage of jaws. The material choice is work in progress
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 7: IR Chamber Design
The electron beam pipe was extended all the way to the center of the detector chamber
An opening on the side of the electron beam pipe is large enough for the forward moving collision particles
has been reduced to the impedance of the horizontal oval slot.
Final photon absorber is outside of the central detector pipe.
Beam–Induced heating for the US side of the IR chamber is @ Iave=2.5A within M=1160 and =7mm
Next step is impedance optimization for proton beam with =60mm.
1.4m long Beryllium section
Horizontal Oval Slot (US)
Tapered Transition (DS)
60mm
40mm
C. Hetzel
- A. Blednykh, E. C. Aschenauer, M. Blaskiewicz, C. Hetzel, M. Sangroula, G. Wang, H. Witte, IPAC2021 Proceeding, WEPAB032
- H. Witte et al., These PAC2021 Proceedings, WEPAB002
60mm
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 8: Flange Joints
Longitudinal wakefield
Total: ~2000
Slot regime
1.5mm
0.25mm
()
()
Factor of 10!
Option A
Option B
Option A is a reasonable choice
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 9: ESR BPM Button (Normal Conducting)
CST beam induced heating simulations for a 7mm bunch length at =2.5 A within M=1160 bunches.
Water circulated via cooling channels at the rate of 6 GPM.
Maximum temperature of 73 deg. C was found at the surface of the BPM button.
The loss factor was optimized by a choice of the button shape (Cone-Shaped).
BPM Button diameter is 7 mm, gap is 250 um, elliptical chamber 80 mm x 36 mm
ESR BPM Button Assembly
M. Sangroula
Real Part of the long. impedance
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 10: Bellows Design Adapted for ESR CHM Profile
SKEKB Comb Type
Sirius Comb Type
NSLS-II Conventional
C. Hetzel
ESR bellows is based on the NSLS-II conventional design
Water cooling channels are integrated to mitigate beam-induced heating
ESR Bellows
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 11: Sirius Comb Type Bellows Adapted for ESR
y
x
x & y motion is limited by the space between the RF fingers.
RF flexible spring and small finger height eliminate capacitance effect at low-frequency (LF)
is smaller for longer bunches. Enough room for the water cooling channels.
Beam Induced Heating - OK
Significant Contribution at HF
for a 7mm bunch length
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 12: ESR Asymmetric 591 MHz RF Cavity
J. Guo
D. Holmes
G. Wang
W. Xu
C. Hetzel
C. Montag
R. Rimmer
E. Daly
A. Zaltsman
150mm beampipe chamber
T of SiC is 240 C for L=150mm
T drops down to 150 C for L=200mm
  ESR 591 MHz Cavities (HOM).
    Limiting space in IP10 for 17 cavities, tapered transitions, quadrupoles, correctors, BPMs, … .
    Asymmetric design with a 150 mm beam pipe diameter with integrated HOM
    Beam induced heating of HOM absorber.
Two Back-To Back Cavities & Tapered Transition
x 9
x 9
Installation of the RF cavities and number of tapered transitions
Protection from Synch. Rad.
Beam pipe between the cavities needs to be reduced from 150mm to 70mm to accommodate APS magnets
Two Back-To-Back Cavities
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 13: ESR – Impedance Budget
Components | Abbreviation | Number | Status
Bellows | BLW | 350 | ✓ x2 (NEG)
Collimator Ramp1 | CLM | 16 | ✓
Horizontal In-Vacuum Collimator | HIVC | 3 | TBD
Vertical In-Vacuum Collimator | VIVC | 3 | TBD
Crab Cavity | CRBCVT | 2 | ✓
Beam Position Monitor2 | BPM | 494 | ✓
Gate Valve2 | GV | 30 | ✓
Stripline Kicker2 | SK | 18 | ✓
Main RF Cavity2 | CVT | 23 | ✓
Tapered Transition in RF Section | TPRD | 9? | TBD
Multipole Chamber Absorber | MPABS | 292 | ✓
Dipole Chamber Absorber | DPABS | 250 | ✓
Flange Joints | FLNG | 1500 | TBD
Resistive Wall | RW | - | ✓
Coherent Synchrotron Radiation | CSR | - | ✓
1 - SKEKB design
2 - NSLS-II design
✓ - Included into the total W(s)
The strong resonance peak at 14GHz corresponds to 494 BPM.
FFT of the total longitudinal wakefield at 5GeV
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 14: Microwave Instability Threshold at 5GeV
Energy, |  | 5 | 10
Average Current, |  | 2.5 | 
Revolution Period, |  | 12.79 | 
Momentum Compaction, |  | 1.33x10-3 | 
Harmonic Number, |  | 7560 | 
Energy Loss, |  | 0.95 | 3.52
RF Voltage, |  | 12 | 24
RF Acceptance |  | 1.156 | 1.089
Synchrotron Tune, |  | 0.062 | 0.062
Damping Time, |  | 134, 67 | 134, 67
Energy Spread, |  | 5.15x10-4 | 5.8x10-4
Bunch Length, |  | 6.8 | 7.6
 |  | 5 | 10
 |  | 2.5 | 
 |  | 12.79 | 
 |  | 1.33x10-3 | 
 |  | 7560 | 
 |  | 0.95 | 3.52
 |  | 12 | 24
RF Acceptance |  | 1.156 | 1.089
 |  | 0.062 | 0.062
 |  | 134, 67 | 134, 67
 |  | 5.15x10-4 | 5.8x10-4
 |  | 6.8 | 7.6
NSLS-II, APS, … need less than 1M macroparticles & 1 kick per turn for numerical simulations.
EIC requires, at least, 8M macroparticles and 8 wakefield elements per turn, C>3times longer, momentum compaction 5 times larger, … .
Energy spread and bunch length as a function of single-bunch current
Microwave instability threshold is
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 15: Transverse Mode Coupling Instability at 5GeV Lattice
V/pC/m
The TMCI at zero chromaticity
Total Dipole Vertical Wakefield
Chromaticity 0/0
Particle tracking simulations with ELEGANT
& are not included
At 2.2 mA, should no exceed
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 16: TMCI Threshold vs. Chromaticity
Stabilizing effect of positive chromaticity and bunch–by–bunch feed back system increase the TMCI threshold in NSLS-II.
NSLS-II sb current is limited by the vacuum activity at .
NSLS-II ()
EIC ()
Experimental data
APS-U ()
Two-Mode approximation valid when
R. Lindberg, Phys. Rev. Accel. Beams 19, 124402
5GeV lattice
w/o &
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 17: Summary
Work on Impedance Budget for ESR and HSR is continued. RCS is next.
The Collective Effects Simulations have been performed for ESR w/ up-to-date Impedance Budget. The instability thresholds are above the required single-bunch current of 2.2 mA. HSR is next.
The crab cavities in the ESR and HSR can lead to very strong transverse coupled-bunch instabilities.
Transverse Bunch-by Bunch Feedback is required during injection and ramping in the HSR to suppress the instabilities.
The proton beam is stable during store due to large synchrotron tune and beam-beam tune spread.
Beam – Beam Simulation w/ the total longitudinal Wakefield is work in progress.
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 18: ESR Individual Component Contribution to the Total Longitudinal Wakefield (=0.3mm)
Bellows, Ramp Collimators and Gate Valves are the first few largest sources
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL

## Slide 19: ESR Individual Component Contribution to the Total Vertical Dipole Wakefield (=2mm)
Bellows, BPM and Gate Valves are the first few largest sources.
A. Blednykh Accel Phys EIC Accelerator Design Weekly Meeting, 7 June 2023, BNL