## Slide 1
Nov 29, 2023
D. Ratner
SLAC National Accelerator Laboratory
Anomaly Detection for an X-ray Free-Electon Laser

## Slide 2
Outline
Introduction and motivation for X-ray Free-Electron Lasers
RF station faults / Coincident anomaly detection
Cathode quantum efficiency degradation / Ghost imaging
Teaser on collider application (beam shape reconstruction)

## Slide 3
Introduction to XFELs
Suga et al.
Photosystem II
Shock waves in extreme conditions
Milathianaki et al.
Si
Ekeberg et al.,
Single particle imaging (Mimivirus)
X-ray free-electron lasers: Accelerator driven x-ray sources to study ultrafast, ultrasmall scale phenomena
Linac Coherent Light Source (LCLS)

## Slide 4: Motivation
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Failure prediction at accelerators:
Failures cause downtime, degrade performance
1000s of subsystems  frequent failures
200k variables to monitor at LCLS  impossible to do manually
Big data, but nearly none of it labeled

## Slide 5: Case Study 1: RF Station Faults
SLAC Linear Accelerator and 280 Overpass
SLAC RF Stations
Case study: RF station faults
RF stations provide power for acceleration
Most common fault at LCLS (1000s/year)
Degrades performance even if no downtime
Years of data, only dozens labeled

## Slide 6: Case Study 1: RF Station Faults
Existing solution #1: Thresholding on subsystem amplitudes
Readbacks of station power condensed to “status bit” for each of 80 stations
Status bit ‘0’ if healthy, and flips to ‘1’ if RF amplitude changes more than 2%
Status bit has multiple problems:
Too simplistic (only looks for sudden drops)
Too permissive (misses subtle faults)
Too noisy (lots of false positives)
7 example measurements
Time (min)
0
5
RF station amplitude for 1 station
70% of alarms are false
(i.e. poor precision)
RF station diagram
Recall = TP/(TP+FN) Precision = TP/(TP+FP)
TP = true positive, FP = false positive, FN = false negative

## Slide 7: Case Study 1: RF Station Faults
Operators watch for a drop in X-ray power here
After observing a drop, search for RF stations with warning/fail status
Existing solution #2: Manual, beam-based anomaly detection
Many missed events
(recall ~ 1%)

## Slide 8: Case Study 1: RF Station Faults
New approach: Beam-based algorithm inspired by operators
Highway 280
Algorithm #1 looks for subsystem anomalies
RF stations
Beam position monitors
Algorithm #2 looks at final beam quality
Simultaneous anomalies trigger alarm
Question: How do we train these algorithms with no labels?
Key insight: A ‘good’ pair of algorithms will be self-consistent

## Slide 9: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
Subsystem
Beam quality
Algorithm 1
Algorithm 2
Prediction
Unknown
machine state
Red stars = consistent
black stars = inconsistent
More red = higher recall;
less black = higher precision
Subsystem (s)
Quality (q)
Anomaly
confidence
Anomaly
confidence
FP rate = product of black star rates
TP rate = red star rate – FP rate
Prediction
Self-Consistency
metric
 Unsupervised precision/recall

## Slide 10: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
We estimate unlabeled version of recall/precision from coincidence
Estimates can be differentiable  can train neural networks!
i.e. a loss function, not just a metric
Formally the loss function is defined for NN outputs :
: Estimated anomaly rate
: Weighting factor (recall vs. precision)
: red star rate
: estimated FP rate

## Slide 11: CoAD for RF Station Faults
RF Station data
Beam Data
Estimated precision/recall
Implementation for RF station task:
Network 1
Network 2
Unsupervised loss function
Anomaly confidence
Anomaly confidence

## Slide 12: Case Study 1: Performance in the control room
 | Precision | Recall (events)
Manual recording by operator | NA | 6
Status bit | 0.31 | 385
Coincident Detection | 0.88 | 504
6x fewer false positives vs. status bit
100x more anomalies vs. manual recording
30% more anomalies vs. status bit
Summary of predictions on 4 months of data
Ryan Humble, Finn O’Shea, Zhe Zhang
Live deployment in LCLS control room!
BPMs
RF
Amplitude

## Slide 13: Case Study 2: Ghost imaging
Radiation, a
Target, x
b = [ 5037,
4783,
4891, … ]
Bucket measures total transmission
Raster scan
Ghost imaging
Reconstructed Target, x*
=
b
x
a
Exploit natural (passive) variation in beam!
What is ghost imaging?

## Slide 14: Case Study 2: GI for Quantum Efficiency Map
photocathode quantum efficiency
Day 1
Day 3
K. Kabra, et al., Phys. Rev. Accel. Beams 23, 022803 (2020)
Cathode QE reconstruction at LCLS
Laser photon hits cathode to produce electron beam
Quantum efficiency (QE): probability of a photon producing an electron
QE map directly impacts electron beam emittance (“quality”)
Current mapping are both low resolution and invasive
4 years later finally in progress… camera controls are not synchronous!
Cathode
target
Cathode laser
Electron charge

## Slide 15: Ghost imaging: Collider example
I1
I2
=
L
d
As function of offset, d
Infer beam shape from luminosity and beam offset jitter
Can GI resolve transverse beam shapes at an interaction point from offset and luminosity jitter?
LHC Motivation:
Improve focusing at the IP
Provide experiments with probability distributions for every crossing
Possibly of interest to EIC?
D. Ratner, A. Chao, K. Li, IPAC2021, WEXA05

## Slide 16: Ghost imaging: Collider example
Can GI resolve transverse beam shapes at an interaction point from offset and luminosity jitter?
 Synchronous acquisition critical
Simulation example works…
…but synchronous BPM/Lumi data not available at LHC
LHC Motivation:
Improve focusing at the IP
Provide experiments with probability distributions for every crossing
Possibly of interest to EIC?
D. Ratner, A. Chao, K. Li, IPAC2021, WEXA05

## Slide 17
Conclusion
Summary:
Turning the corner on deployment of AI methods (anomaly detection, tuning, etc.)
Several examples of AI methods outperforming classical methods (SLAC and elsewhere)
But…
Implementing AI methods for online controls puts new stresses on control systems  the earlier you establish AI-ready systems the better
Synchronous acquisition, high data rates, easy access to GPUs for deployment
Alex Chao, William Colocho, Eric Darve, Matt Gibbs, Ryan Humble, Michael Kagan, Kevin Li, Jason Liang, Finn O’Shea, Jake Rudolph, Eloise Yang, Zhe Zhang
Thanks for listening!
And thanks to everyone who worked on these projects!

## Slide 18
Backup
Notes: Histogram of the events based on the change in RF amplitude. Orange were labeled anomalous by our algorithm. A simple threshold at ~5 would have significant differences (about 20%) from our NN prediction. Based on visual inspection and correlation efficiency, we believe the NN is mostly correct (~10% errors).

## Slide 19: Coincident Anomaly Detection (CoAD)
Consider two algorithms making predictions on two streams of data
Key insight #1: We estimate unlabeled version of recall/precision from coincidence
Key insight #2: Estimates can be differentiable  can train neural networks!
i.e. a loss function, not just a metric
Formally the loss function is defined for NN outputs :
: Estimated anomaly rate
: Weighting factor (recall vs. precision)
: red star rate
: estimated FP rate

## Slide 20: Ghost Imaging Concept
Riddle: How can I take a picture with a spectrometer?
Answer: Have a friend with a flashlight
Ghost imaging / Single pixel camera / Compressive Sensing

## Slide 21: Case Study 2: Resilient VAE for general fault detection
Auto-encoder for unsupervised anomaly detection
Accelerator diagnostics
Input
Latent space
Output
Accelerator diagnostics
Time (~1 minute)
Diagnostics
Reconstruction error
|Output – Input|
Ryan Humble

## Slide 22: Case Study 2: Resilient VAE for general fault detection
Auto-encoder for unsupervised anomaly detection
Ryan Humble
Time (~1 minute)
Diagnostics
Reconstruction error
|Output – Input|
Klystron fault
Beam scraping
BPM Charge
“Resilient VAE” avoids need for a normal training set
Work in progress…