## Slide 1: Towards construction of a novel nm resolution MeV-STEM for imaging thick biological samples
10/04/2023
Xi Yang
on behalf of BNL UEM team
in collaboration with Cornell university

## Slide 2: Outline
Introduction
  Review of scientific case for conventional TEM/STEM and UED
  Promise of MeV- microscopy
History of MeV- microscopy
Review of the state-of-art in the field
Physics & engineering challenges & solutions in reaching nm resolution
  Ultrabright MeV electron source
  Interaction of MeV-electrons to sample
  Detector & instrumental stability
Conclusion

## Slide 3
D. A. Muller, Nat. Mater. 8, 263 (2009)
Adapted from H. H. Rose (2009)
Transmission electron microscopy
Soil bacterium
Cryo-TEM
An intact virus to fight against covid-19
Yao, H. et al. Cell 183, 730 (2020)
Intact virus applied to EM grids
    Imaging tool for materials science, chemistry, physics, biology, and industry
    Atomic resolution with aberration correction
    I

## Slide 4: Ultrafast science enabled by MeV UED
Ultrafast hydrogen bond strengthening in liquid water(Nature. 596, 531(2021)).
Phase switch with a single flash of light (Sci. Adv. 4, eaau5501 (2018)).
Courtesy of Xiaozhe Shen
Toward real space imaging enabled by MeV Microscopy
Resolving ultrafast phase transitions (Science 360 1451–1455 (2018))
Concurrent probing electron-lattice dephasing (BNL)
SLAC
High repetition rate electron scattering beamline (HiRES) LBNL
F. Ji, et al., Commun. Phys. 2, 54 (2019)
Li et al., Phys. Rev. B 101, 100304(R) (2020)
fs-resolved imaging of grain boundary dynamics in energy-filtered ultrafast electron microscopy (UNIST)
(Sci. Adv. 9, eadd5375 (2023))

## Slide 5: Promise of MeV Microscopy
    Life science application: 3D image intact thick bio-samples
    studying cell-biology and microbiology in cellular context
    No need of cryo-FIB (focused ion beam) slicing thick cells
    Limit to 10-20 lamellae/day, “blindly” select target
    Speed up discovery
    I
S.G. Wolf, et al., Cellular Imaging, Springer
3 MeV STEM/UEM
300 keV
Top and side views of a eukaryotic cell.
Nucleus
cryo-scanning transmission e- tomograph
cryo-electron tomograph
Benefit of increasing electron energy to MeV
Signal for 3 MeV-UEM
Signal for 3 MeV-STEM
300 keV-STEM
300 keV-UEM
Why MeV? Phase contrast (TEM) & amplitude contrast (STEM)
300 keV
  Single-elastic drop <1% after 1-µm ice layer
  Inelastic drop <1% after 4-µm
3 MeV
  Single-elastic drop <1% after 2-µm ice layer
  Inelastic stays 63% after 10-mm
Top
Side

## Slide 6
Graphite
Fe
Dry-ice
(CO2)
LiOH
Amorphous ice
Graphite, Fe, LiOH and Dry ice (CO2) with size of ~ 3 nm in-plane and 6 nm thick are embedded in amorphous ice.
The product of Cs and l is kept constant, we choose Cs=0.5 mm for 200 KeV and Cs=2.5 mm for 2 MeV.
D0=5 nm. Here .
200 KeV
2 MeV
graphite
Fe
LiOH
CO2
Benefit from increasing electron beam energy to MeV
UEM Imaging at different beam energies
Nanoparticle in amorphous ice
10nm
10nm
10nm
3nm
3 nm
6 nm
BNL capability: Electrons and sample interaction simulation by Lijun Wu’s multislice wave optics code
e-

## Slide 7: State of art MeV UEM/UED: world-wide efforts
UCLA
SLAC
LBNL
BNL
Diamond
DESY
PKU
THU
OSAKA
SJTU
KAERI
Appl. Phys. Lett. 112, 113102 (2018)
Spatial resolution ~50 nm
SJTU
Single shot
Nano-particle
Microscopy 67, 291 (2018)
Temporal resolution 180 fs
OSAKA
UCLA
PRL 118, 154802 (2017)
BNL
Wait for beam testing
Beam
RUEDI
RUEDI
proposed UK National User Facility
halfway through design stage

## Slide 8: Critical parameters and components for MeV UEM/STEM
Beam requirement for single-shot UEM / raster STEM
Number of electrons /shot (freq)
Imaging area 100
Beam divergence
t - resolution ment
Energy spread 10-4
More challenging for STEM
  10 pm nor. emittance with current of 0.1-1 nA
  Both need flattened longitudinal phase space for
  energy spread
Four main building blocks of MeV UEM
  High brightness photoinjector
    Photocathode, high gradient rf gun, drive laser
  Bright beam transportation
    Condenser, aperture, imaging lens system
  Electrons and sample interaction
    Time-resolved applications, life science (e.g., bio-samples with up to 10 μm thickness)
  Detector
    Scintillating, single electron counting
is the reverse of that of a TEM column from sample to detector
Reciprocity: STEM column from e- source to sample

## Slide 9: High brightness photoinjector
Two types of photoinjectors
  DC gun (up to 10 MV/m)
  RF gun (higher gradient up to 250 MV/m)
    Normal conducting
    Superconducting
    I
Laser shaping affects tran. & long. dynamics
  Uniformly filled ellipsoidal
  Linear self-field
I. V. Bazarovet al., PRL 102, 104801 (2009)
D. Filippetto et al., PRAB 17, 024201 (2014)
J. Rosenzweig et al., PRAB 22, 023403 (2019)
O.J. Luiten, et al., Phys. Rev. Lett. 93(9), 094802 (2004)
P. Musumeci al., PRL 100, 244801 (2008)
Qian and Vogel, IPAC21
electron bunch
Emittance is preserved during beam transportation with an initial ellipsoidal profile
High field  High brightness

## Slide 10: Challenges of MeV UEM/STEM
QE > 10-5
1. Reduce beam emittance to < 10 / 0.01 nm for UEM/STEM
Δr = Csα3; Δr = CcαΔE/E;
    Reduce thermal emittance (minimize MTE & spot size & cool cathode)
    Reduce space charge induced emittance growth
    I
0.25 μm/mm rms emittance is close to the limit set by e- finite T=300 k
0.12 μm/mm rms emittance when T=90 k
L. Cultrera et al., Phys. Rev. ST – Acc. Beams 18 (2015) 113401
H. Lee et al., Rev. Sci. Instrum. 86 (2015) 073309
Choose low emittance photocathode (e.g., alkali antimonide)
Cool the cathode to cool the electrons & increase Ez
Notes: 𝑅_12=0
𝐶_𝑐=𝑇_126
𝐶_𝑠=𝑈_1222

## Slide 11: Challenges of MeV UEM/STEM
2. Reduce beam energy spread to < 10-4
    Remove quadratic energy chirp with a harmonic cavity (single shot)
    Remove off-energy electrons with a monochromator (single- and multi- shot)
    Excellent RF and Low-level RF system
    I
Li and Musumeci, Phys. Rev. Applied, 2, 024003 (2014)
Reduce beam energy spread
with a harmonic cavity
Reduce beam energy spread
with a MeV-monochromator
Yang, et al., Sci. Rep. 10, 16171 (2020)

## Slide 12: Challenges of MeV UEM/STEM
3. High beam density and space charge effect
    Rose theorem: >100 electrons/pixel to make a useful image
    Single shot UEM: B6D 102-103 A/(keV*μm2*rad2)
    Ultimate beam density (e-/nm3) limited by space charge (SC) effect
    Spatial resolution also limited by stochastic space charge effect
    Single-electron per bucket avoids SC effect enable MeV-STEM
    I
Li and Musumeci, Phys. Rev. Applied, 2, 024003 (2014)
Qian and Vogel, IPAC21
No SC
With SC and IBS

## Slide 13: Challenges of MeV UEM/STEM
4. Build low-aberration strong lenses for MeV UEM at BNL
    Novel approach: compact low-cost imaging lens based on PMQ quintuplets.
    Minimum aberrations: strong lens with the highest achievable gradient and shortest focal length.
    Tunability of the magnification: +/- 5% by adjusting drift spaces between magnets and trim quadrupole.
Wan, W., Chen, F. & Zhu, Y., Ultramicroscopy. 194 143-153 (2018).
Diffraction
Spherical
Chromatic
Focal length f and main aberrations Cs and Cc
Q5 Q3
Q4 Q2Q1
Trim-Q
Beam

## Slide 14: Challenges of MeV UEM/STEM
    Illustration of 5 electron categories
    I0 = Inoscat + I1el + Iel,plural + Iinel + Iout
    I
5. Electron sample interaction
Why MeV? Critical angle decreases with the increase of beam energy
Mean energy loss: <∆E> (t/λi)(). t (thickness), λi (MFP), (=40 eV, single inelastic energy loss for amorphous ice)
I0
Sample
Inoscat
Iel,plural
TEM
I1el
STEM
Iinel
Iout
0 1 2 3 ……… n
Energy loss
θ0
Signal (a.u.)
thicker
Single elastic
(TEM)
(STEM)
STEM signal

## Slide 15
For thick samples (e.g., t > 1.2 um), mean energy loss is almost linearly proportional to the sample thickness
Left plot is electron energy loss spectrum (EELS) at 2, 3, 4 um thick samples
Right plot is peak position as a function of sample thickness, which fits well with the linear relationship
Chromatic aberration affect gets worse for thick sample  e.g., energy filter + TEM
Energy loss data taken with beam energy 200 keV at CFN
Sample is a wedged silicon
Courtesy Sooyeon, Yimei and Lijun

## Slide 16: MEV STEM to visualize intact thick cells
Requirement
Beam size and converging angle on sample determines resolution.
To achieve nanoscale resolution with up to 10 µm sample thickness:
Electron dose: 200 e-/nm2 / μs
Probe on sample: 2-5 nm
Beam convergence angle: 1 mrad
Beam flux: 200 - 5,000 e-/ μs
Scanning accuracy: 1 nm
E | dsam | α | I | ∆E/E | ∆xcen | ϵgeo
MeV | nm | mrad | nA |  | nm | pm·rad
3.0 | 2 | 1 | 0.1-1 | <10-4 | 1 | 2
Photocathode (e.g., alkali antimonide)
In transmission mode, there is a micron laser size and MTE 35 meV
Beam emittance of nm
    Solution: combination of high penetration inelastic signal and lens-less between sample and detector
    makes MeV-STEM an appropriate microscope for 10 μm or thicker bio-samples with nm resolution
H. Lee, L. Cultrera, and I. Bazarov, Appl. Phys. Lett. 108, 124105 (2016).
H. Lee, et al., Rev. Sci. Instrum. 89, 083303 (2018).
J. Maxson, et al.
Notes: Combine with slide 5

## Slide 17: Challenges of implementing MeV STEM
Reduce beam emittance to ~ 2 pm with current of 30 – 750 pA
Photocathodes & beam dynamics need to improve brightness by >1000
Probe size: ; divergence: ; emittance:
    Reduce laser spot size and MTE from photocathode
    Increase QE 10-5
    Beam dynamics come hand in hand with improved emittance
      Apply aperture to increase both transverse and longitudinal brightness
    I
    Preliminarily MeV-STEM column design (reversal of TEM column)
    Assume 2 μm spot at cathode
    Dose rate 200 to 5k e-/μs
    I
J. Maxson and A. Bartnik
Detector collection angles
5-6 m

## Slide 18: Challenges of implementing MeV STEM
Design lowest aberration strongest lenses for MeV STEM
Probe size: and divergence:
    STEM column
      Focus the beam onto the sample with a few nanometers
      Freedom of varying the probe beam size
    Variation of aperture and magnetic field of trim quadrupoles can change the beam size from 2 nm - 60 µm (to find ROI)
    I
    The final probe beam size in RMS (green)
    The theoretically minimum resolution (purple)
 | f (cm) | Cs,x (cm) | Cs,y (cm) | Cs,xy (cm) | Cc,x (cm) | Cc,y (cm)
Probe forming Lens (SRF) | 1.00 | 16.2 | 15.0 | 35.3 | 1.78 | 1.44
probe forming Lens (DC) | 1.00 | 16.2 | 15.0 | 35.3 | 1.80 | 1.46

## Slide 19: Summary
Accelerator based MeV UEM/STEM hold great potential to solve the challenges in probing matter at ultrafast-temporal ultrasmall-spatial scales and studying life science
Expect better performance than low-energy UEM/STEM for thick samples
Several MeV UED user facilities are being built and deliver high impact results
MeV UEM efforts are ramping up
MeV STEM developments are just in the beginning
A great complement to XFELs
Inter-discipline collaboration generates creative idea

## Slide 20: Acknowledgements
Special thanks to
  Cornell: Jared Maxson and Adam Bartnik
  SLAC: Xiaozhe Shen
BNL UED/UEM Team
Xi Yang, Victor Smaluk, Timur Shaftan, Liguo Wang, Sean McSweeney, Lihua Yu, Ganesh Tiwari, Yoshiteru Hidaka, Guimei Wang, Lewis Doom, Jim Rose, David Bergman, Michael Fulkerson, George Ganetis, Bernard Kosciuk, Danny Padrazo, Belkacem Bacha, Charles Spataro, King Wilson, Mikhail Fedurin, Marcus Babzien, Robert Malone, Karl Kusche, Christian Cullen, Junjie Li, Lijun Wu, Yimei Zhu, Luca Cultrera, Qun Liu, Weishi Wan

## Slide 21
Thank you!