## Slide 1: Potential applications and requirements of photoelectron sources for metrology
Gil Delgado
VP of Adv Tech

## Slide 2
Nova is a leading innovator and a key provider of metrology solutions for advanced process control used in semiconductor manufacturing

## Slide 3
KEY Facts
1993 | Date Founded | Dually Traded
>1100 | Employees
>5000 | Active Systems
>200 | Customer Sites
R&D | Israel, USA, Germany
Presence | Israel HQ , Global Offices

## Slide 4
Current chip manufacturing:
Over 1,000 process steps are needed to make transistors and connections! Ideally you want to monitor every step.
Specialized materials and processes use
up to 62 different elements
etch
dev
Litho
etch
dep
etch
dep
CMP
Semiconductor Process
Front End of Line

## Slide 5
Process Control:
Metrology
is essential for Chip Manufacturing success
Importance of Inline Process Control
~ 100,000, 300 mm wafers per month are produced by an advanced fab
Cost of a single wafer for standard process ~ $15,000
$ 15,000 X 100,000 = $1.5 B
Cost per wafer x Wafers per month
Wafer metrology tools are used to carefully control the film properties, dimensions, and potential defect levels in order to optimize the manufacturing process of these devices. Using lab tools can take a long time to resolve issues.

## Slide 6: Memory – 3D NAND Process Challenges
Dimensional
Full profile – per deck and in total
Logic under Memory cell
Bottom parameters
Tiers and liner thickness
Tilt and Overlay between decks
Material
Dielectric composition & thickness control
Channel Poly Si crystallinity & grain size
Channel sidewall
Chemical residues
Stress management
From Single Deck to Multi Deck
Triple Deck
3
7,8,9
1
3
2
5
4
> 400 Tiers
> 20um thickness
Logic under Memory
Single Deck
Overlay
Slit
TCD
Slit
MCD
Slit
BCD
3
6
3D NAND

## Slide 7: Memory – 3D DRAM Process Challenges
Dimensional
High-Aspect Ratio capacitor holes & supporters
Bottom gate parameters
Tight contact holes
Lateral selective etches for thinner capacitors
Material
Dielectric composition & thickness control
Higher dielectric constants
Material residues
2D DRAM
2D scaling is not enough
Move to 3D DRAM-
Same path as NAND
Capacitor
Bit Line
Word Line
1,6
1,3
2
5,6,7
4
Moving from 2D DRAM to 3D DRAM
3D DRAM

## Slide 8: Logic Architecture - Process Challenges
Dimensional
Multiple nanosheets – shapes, spacing & thickness
Thin deposition surrounding nanosheets
Buried structures
Local topography variations
Material
Si / SiGe uniformity
SiGe residues
Stress & strain on multiple nanosheets
Doping control
<10nm
4
Adding a dielectric wall between NFet and PFet
True 3D
NFet over PFet
Forksheet
Logic Architecture Evolution – Increased Complexity
1,2,5,6,7
3
Nanosheet
Complementary FET
2D Materials
2D Atomic Channel
Source: Nova, American Chemical Society
Growing dimensional and material complexity

## Slide 9: Interconnect - Process Challenges
Dimensional
HAR Cu nano-TSV profile control
Topography for Wafer-to-Wafer bonding
Voids & Delamination
Surface roughness
Material
Via Pitch and CD too narrow for plated copper
Cobalt etch - Single damascene
Cu fill - Buried Power Rails
Cu, Ru & Co interconnects plating
New Architecture
Backside Power Delivery Network & Hybrid-Bonding with Nano-TSVs
2,4
1,3,5
7,8
Source: Intel
New architectures are also being adapted in the Back-End or interconnect of wafer manufacturing.

## Slide 10
Smaller Dimensions, and Depth Pitch Pose Challenges in For Metrology
Metrology technologies need to have depth and sensitivity to these
small defects
Some Examples:
1) 3D NAND
Impact of defects magnified
Non uniform layers
Source: https://semiengineering.com/3d-nand-flash-wars-begin/

## Slide 11
Electron penetration depth->LE
~ 10’s um
Depending on
LE and material
Electron Beams Have Many Capabilities to Address Many of The Needs For Metrology and Inspection
Adapted from Wikipedia

## Slide 12
Secondary electrons
Good for topographic imaging
Auger Electrons
Surface Sensitive
Compositional Info
X-rays
Film analysis
Thickness and composition
Cathodoluminescence
Electrical Info
Backscattered electrons
Atomic Number and topography info
X-rays Fluorescence
Film analysis
Thickness and composition
Topographic 3D Imagining
Electron Beams Have Many Capabilities to Address Many of the Needs For Metrology and Inspection
Adapted from Wikipedia

## Slide 13
Smaller Dimensions, and Depth Pitch Pose Challenges in For Metrology
Example 2: TSVs (Through-silicon vias )
E-beam have the resolution and penetration depth for TSVs metrology
Photocathodes can be an important technology for TSVs metrology
TSVs are vertical interconnects that enable 3D stacking and integration of chips. They allow high-density interconnections between stacked chips.
Important Metrology of TSVs: Geometry (diameter, depth, sidewall angle), defects (voids, incomplete filling), and insulating liner integrity.
As TSV dimensions continue to shrink, new and improved metrology/tools are needed to ensure reliability and enable further 3D integration
Open defect between TSV and metal via
Open defect between bump and upper die
Short between fine
Void formation in TSV
Source: Jacobs et al, 2020_IEEE TRANSACTIONS ON COMPONENTS, PACKAGING AND MANUFACTURING TECHNOLOGY, VOL. 10, NO. 9, SEPTEMBER 2020
J. Wang Applied Sciences Volume 13 Issue 14 10.3390/app13148301

## Slide 14
Example 3: TSVs
TSV dielectric defects can generate leakage current between TSV and substrate (i.e., short defects). These short defects can be detected and localized by sensing the electron-induced TSV current.
Ebeams have depth and resolution for these small structures.
Figure shows the schematics of a 3-D SoC chip with two silicon wafers
Source: Jacobs et al, 2020_IEEE TRANSACTIONS ON COMPONENTS, PACKAGING AND MANUFACTURING TECHNOLOGY, VOL. 10, NO. 9, SEPTEMBER 2020
J. Wang Applied Sciences Volume 13 Issue 14 10.3390/app13148301
Smaller Dimensions, and Depth Pitch Pose Challenges in For Metrology
Electron beams can generate in-situ electrical beam-induced current that can be used to localize dielectric shorts between TSV and substrate

## Slide 15: E-Beam Source Requirements for Metrology
 | Units | Schottky TFE | Photo-cathode
 | eV | ≥ 0.7 | 0.3
Temp | K | 1800 | 294
Stability |  | <1% | <1%
 | A / m2 | ~30x107 | >30x107
Multibeam |  | >20 | > 20
Cost |  | Cost prohibited | 
 | Units | Schottky TFE | Photo-cathode
 | eV | ≥ 0.7 | 0.3
Temp | K | 1800 | 294
Stability |  | <1% | <1%
 | A / m2 | ~30x107 | >30x107
Multibeam |  | >20 | > 20
Cost |  | Cost prohibited | 
Photocathodes have some clear advantages over state-of-the-art electron sources.
Electron Source
  Energy Spread < 0.3 eV
  High Brightness > 108A / (V m2 sr)
  Focus to high current densities
  Spot Size: <100 nm2
    (or smaller for in device testing)
  Stability: <1%
  Long Lifetime

## Slide 16
Example: Etec Systems
Generated a linear array of 32 ebeams
Produced 86 nm spots
Long term stability: 1%
Energy Spread < 0.3 eV
1 mm
Prototype raster multibeam lithography tool
S. T. Coyle, J. Maldonado, et al, Journal of Vacuum Science & Technology B 20, 2657 (2002)
Ebeams were magnified and focused onto a YAG screen.
Today photocathodes with high-end electron optics can focus e-beam to spot size < 10 nm
Multibeam Photocathode System can address throughput issues
Photocathodes can become an important technology for semiconductor metrology.

## Slide 17: Metrology Future Needs
Conventional metrology is challenged to characterize the tiny features, dimensions and material composition with the required sensitivity.
Lab metrology is slow, expensive, and, often destructive. Fabs need inline metrology systems
As device structures become more complicated and require more process steps, process control becomes more critical.
  Many critical defects and metrology needs can not be addressed by optical means regardless of inspection time
  Electron beam inspection and metrology is expected to become an important part of the metrology process control
  Electron beam source technology is a limiting factor for adoption