## Slide 1
fECal Discussion, 06.05.23 O.Tsai
Brief reports form fECal consortia.
Discussion of next steps for 0’s order mechanical design.

## Slide 2
Update on global design refinement with full ePIC simulations:
Effect of material upfront of Ecal, i.e. readout on the back vs front – no difference.
Pixel size for SiPMs – 15-20 um, same SiPMs for entire fECal
Outer radius – (interplay between barrel and fECla) R out ~ 1.7m, reduction of n channels from 19k to ~15k
What left:
Effect of radiation damages – need for cooling of SiPMs next to the beam pipe.
Granularity at insert area – (only affect FEE design).
With next few simulation campaign I don’t expect any new impacts on mechanical design.
Mechanical design may have small impact on simulations (collar near the beam pipe_.

## Slide 3
Update on fECal module design
No changes, installation block is the same ~ 10 x 10 x 17 cm WScFi + 13 cm light guides + readout.
Components:
W Powder – Fudan’s type
Fibers Kuraray or Luxium (final sample from Luxium will be at UCLA end of June, confirmed today).
Meshes (after checks with Fudan) updated quotes from FOTOFAB on May 15’th.
Epoxy – DE NEEF (instead of Epotek 301-1) for modules, Epotek 301-1 for TiO2 diffuser layer only. DeNeef tested at UCLA and Fudan, workability same as Epotek.
Light Guides - new design, maximizing light collection efficiency. Investigations in few directions how to produce these (machine, cast, injection). No definitive yet.
Test Run for 2023
Late fall, waiting from FNAL announcement. Readout scheme for test run defined.

## Slide 4
Workforce (at present):
UCLA/Fudan – working on block production technique
Indiana – FEE/readout
UCR – SiPMs (mostly for insert for a moment)
UCLA/BNL – structural tests (just about to start, small WScFI blocks first, then installation block (arrived from Indiana today)).
eRD106 funds still not available, long delay at BNL. Now delay at UCLA and UCR sides, but promised that accounts finally will be set any moment now…

## Slide 5
Ecal installation block weight ~ 18 kg., transverse dimensions 10 cm x 10 cm
Ecal installation block will be glued to ‘Strong Back’, which is ~ 1 cm thick Aluminum plate with two tapped holes.
Mounting Brackets – steel ~ 8 mm x 8 mm
Mounting Brackets probably need to be adjustable
ECal blocks will be installed from bottom to top, layer by layer.
Each Ecal block rest on top of a bracket from previous layer and bolted to mounting bracket at the top of the block.
A spring loaded pin in bottom bracket may be needed.
Seismic analysis
For BNL it is 0.25g horizontal.

## Slide 6
Discussion of next steps toward 0’s order mechanical model.
Area near beam pipe.
Collar – should it be considered as a support/safety structure around beam pipe?
Or after structural tests we find that it can be as thin as possible and serves only as a part of fECal enclosure.
My view, we should consider it as a support/safety structure.

## Slide 7
2. Filling of fECal area to ~ 1.7 radius – number of blocks
3. Define integration envelope at outer radius, i.e. space for cooling/cables.
4. But before that need to decide of utilities routing.
5. That will have impact on steel ring around fECal
Probably preferably is to route all utilities and cables ‘inside’ and have openings below beam pipe to rout them to platforms.

## Slide 8
ECal attached to HCal via mounting plate
Mounting plate is a solid ~1 cm thick steel plate with mounting holes to:
1. Attach Mounting plate to Hcal blocks
2. Attach Ecal mounting brackets to Mounting plate (next slide)
3. Provide support for ECAL enclosure hardware.
ECal Blocks positioning accuracy ~ 100 mkm
Ecal Enclosure
All cables utilities coming out to racks.