## Slide 1: Modular RICH Detector Simulation – Rayleigh Scattering inside Aerogel
Cheuk-Ping Wong
Georgia State University
04-01-2016

## Slide 2: Overview
Transmission of aerogel with updated material definitions
  Aerogel thickness : 3cm3.3cm
  Rayleigh scattering length : rescaled w/ factor 1.5
Cherenkov Photon spectrum measured at the back of aerogel

## Slide 3: Simulation 1: Transmission of aerogel
Transmission of aerogel after modifying aerogel properties
Aerogel from Marco
  3.3cm thick
  Refractive index 1.028 – 1.034
  Rescaled Rayleigh Scattering length (x1.5)

## Slide 4: Simulation Setup
100K optical photons beam
Launched perpendicularly at (x,y)=(0,0)mm, and right in front of the aerogel
Momentum: 1.7-6.2 eV (200-730 nm)
No Fresnel Lens
Rayleigh Scattering On

## Slide 5: Transmission of Aerogel
Normalized by the wavelength distribution of incident photons
Aerogel has a better transmission through out the whole spectrum after rescaled Rayleigh Scattering length

## Slide 6: Transmission of Aerogel
Clarity of aerogel reaches ~56 (desired value) after rescaled Rayleigh Scattering length

## Slide 7: Simulation 2: Wavelength Distribution of Cherenkov Photon
Measure Wavelength Distribution of Cherenkov Photon at the back of aerogel
Survived -- those can make it to the Fresnel lens, regardless of unscattered or scattered: all non-reflected (pz>0) photons that hits at the back of the aerogel
The rest -- those cannot make it to the Fresnel , regardless of unscattered or scattered (shown on back up slides) : all the photons that hits inside the aerogel, or reflected (pz<=0) photon
No additional cuts (e.g. mother pid cut, vertex cut)

## Slide 8: Survived Cherenkov Photons
1Gev single pi-
Back of aerogel
Before Normalization
Measure at the back of the agel
Normalized by total number of events
Rayleigh Scattering On
RS on, 150k entres
RS off, 210k entries
2GeV single pion-

## Slide 9: Simulation Setup
1000 kaons and 1000 Pions
Launched perpendicularly at (x,y)=(0,0)mm, and right in front of the aerogel
Momentum: 3 GeV, 6 GeV, 9 GeV, 12 GeV, 15 GeV
Rayleigh Scattering On (right), Off (left)
Aerogel from Marco
  3.3cm thick
  Refractive index 1.028 – 1.034
  Rescaled Rayleigh Scattering length (x1.5)

## Slide 10: Normalized Wavelength Distribution of Survived Cherenkov Photon (Pion-)
Rayleigh Scattering Off
Rayleigh Scattering On
Count is normalized by number of events (1000 events)
Rayleigh Scattering lowers the count especially in shorter wavelength region as expected
Peak value shifts to the longer wavelength region

## Slide 11: Normalized Wavelength Distribution of Survived Cherenkov Photon (Kaon-)
Rayleigh Scattering Off
Rayleigh Scattering On
Number of Cherenkov photons increases with momentum of incident particle (see back up slide)

## Slide 12: Summary
Transmission plots from updated agel properties are shown
  Better clarity (~56)  better transmission
Wavelength Distributions of Cherenkov Photon with both Rayleigh Scattering On and Off are shown
  Rayleigh Scattering lower the rate of Cherenkov photon hits as expected
  Peak value of Cherenkov photons shifts to longer (~60nm longer) wavelength region

## Slide 13: Num. of Photon Hits per Event vs Kaon Momentum
Num. of photon hit saturate as momentum increases
See more on p.20-21 of Progress Report 2015 -- https://drive.google.com/file/d/0Bxt90nyX6kjaWFE3UnYtM3k5NEE/view?pref=2&pli=1
2cm thick aerogel
3cm thick aerogel

## Slide 14: Normalized Wavelength Distribution of the Rest of Cherenkov Photon (Pion-)
Rayleigh Scattering Off
Rayleigh Scattering On

## Slide 15: Normalized Wavelength Distribution of the Rest of Cherenkov Photon (Kaon-)
Rayleigh Scattering Off
Rayleigh Scattering On