## Slide 1: ePIC DAQ System Overview Streaming Readout
David Abbott
Jefferson Lab
L3 CAM for EIC Detector Project
July 5-6, 2023

## Slide 2: ePIC DAQ/Online Computing Overview
The EIC Streaming Readout (SRO) Consortium was formed in 2018 with the goals of engaging the nuclear physics community in exploring the advantages, challenges and requirements to implement a 100% streaming readout architecture for the EIC detectors.
  Series of ten workshops between 2018 and 2022.
  General agreement in the Yellow Report, that the adoption of SRO would maximize the impact of the physics program for EIC.
Talk Outline
  General DAQ architecture
  Expected technology choices
  Interface with Detector Systems – PID focus
  Relative schedule wrt to the EIC Detector project

## Slide 3: EIC Streaming Readout Community
ePIC Electronics/DAQ Working Group
  J. Landgraf (BNL), F. Barbosa (JLab), J. Huang (BNL)
  Regular meetings to focus on design and requirements specifically for the new ePIC detector
  Interface to detectors, readout, DAQ, online processing, monitoring and control.
ePIC Software/Computing Working Group
  M. Diefenthaler (Jlab), S. Joosten (ANL), T. Wenaus (BNL), W. Deconinck (UM)
  Coordinating software development for EIC physics
  Analysis Frameworks, Reconstruction, Simulation, AI & ML
  Online Filtering (e.g. event ID, calibration)
EIC Project L3 CAMs (DAQ/Online, Electronics)
  D. Abbott (JLab), J. Landgraf (BNL), F. Barbosa (JLab)
  Project management (cost/schedule)
  Coordination between relevant EIC working groups (including Detectors)

## Slide 4: Streaming Readout Architecture
  No hardware-based trigger (well just optional…)
    Elimination of dedicated hardware and ability to select events based upon the full detector are the main advantages.
    Exposure to background and noise is the main challenge
    All front-ends are free-running (or self-triggered)
    Data flow (congestion) is managed at individual sources
  Streaming requires a robust and accurate distributed clock delivered and synchronized to all the front-ends
    All data are characterized by detector/channel ID and a time-stamp
  Real time filtering, processing and reconstruction
    Online vs Offline tasks become blurred
    Adds requirements such as the need for event identification & quasi-real time monitoring/calibration for filtering and physics results
    This is the focus of the EIC Software and Computing Group

## Slide 5: ePIC Streaming DAQ/Computing Architecture
ePIC DETECTOR
BW O(100Tbps)
BW O(10Tbps)
BW O(100Gbps)
RDO
RDO
RDO
RDO
RDO
RDO
RDO
RDO
RDO
Bunch Crossing ~ 10.2 ns/98.5 MHz
Interaction Rate ~ 2 us/500 kHz
Low occupancy.
Distributed clock
jitter ~5ps

## Slide 6: ePIC Readout Chain
Name
Design
Function
Attributes
Adapter
Detector Specific
-HV/Bias Distribution
-HV divider
-Interconnect Routing
-Sensor Specific
-Passive
Sensor
Detector Specific
-Multi-Channel Sensor
-MAPS
-AC-LGAD
-MPGD
-MCP-PMT
-SiPM
-LAPPD/HRPPD
Front End Board
(FEB)
Detector Specific
-Amplification
-Shaping
-Digitization
-Zero Suppression
-Bias Control & Monitoring
-ASIC/ADC
-Discrete
-Serial Link
Readout Board
(RDO)
Few Variants
-Communication
-Aggregation
-Formatting
-Data Readout
-Config & Control
-Clock & Timing
-FPGA
-Fiber Link
Data Aggregation Module (DAM)
Common
-Computing Interface
-Aggregation
-Software Trigger
-Config & Control
-Clock & Timing
-Large FPGA
-PCIe
-Ethernet
Computing
Common
-Data Buffering and Sinking
-Calibration Support
-QA/Scalers
-Collider Feedback
-Event ID/Building
-Software Trigger
-Monitoring
-COTS
-Ethernet
Global Timing Unit (GTU)
-Interfaces to Collider, Run Control & DAM
-Config & Control
-Clock & Timing
On Detector
SMT BGA

## Slide 7: DAQ Interface to the Detector Systems
Managing data “streams” is ideally done in a deterministic way – e.g. FPGAs
Proprietary communication with the front-end electronics.
  Bi-directional link (fiber)
  Send: clock, commands, control, config
  Receive: high speed data streams
System on Chip (SoC) facilitates DAQ/User applications to communicate with the Front-end.
  Readout, Configuration and Control
DAM (Data Aggregation Module)
RDO
RDO
RDO
FPGA
DAM
Server
Server
SoC
Ethernet
PCIe
timing
FEB
FEB
FEB

## Slide 8: DAM Option - Front-End Link Exchange (FELIX)
Originally developed for ATLAS at CERN
Design team is based at Brookhaven
  Current version (FLX-172) in use at BNL for sPHENIX
New board being prototyped now for ATLAS HL-LHC running.
Notes: The Xilinx Versal Prime is a SoC.- Dual Core ARM Cortex
Power usage ~133W. No power through PCIe.
Can be implemented as a stand alone device (no Server)
Block Diagram of FLX-182 Prototype
FPGA: Xilinx Versal Prime XCVM1802
PCIe Gen4 x16
24 Firefly links with 3 config options
  24 links @ 25Gbs
  24 links @ 10Gbs
  12 @ 25Gbs + 12 @ 10Gbs
4 additional Firefly links
Front Panel: Fiber I/O
  Additional 3 Inputs, 3 Outputs
1 DDR4 Mini-UDIMM
USB-JTAG/USB-UART

## Slide 9: FELIX timelines
10 boards were produced in early 2023.
DAQ Working Group has recently acquired one of these boards for testing
General technical support for the FELIX Hardware should be available through the end of HL-LHC operation.
(i.e. into the late 2030s for Run 5)

## Slide 10
Detector System | Channels | Fiber pair | Data Volume | DAM Boards | Readout Technology | Notes
PID-TOF | 3M-50M | 240-500 | 6Gb/sec | 12 | AC-LGAD/ EICROC | Channel / Fiber counts depend on sensor geometry. Considering pitches of: .5mm x 1cm, .5mm x .3cm, .5mm x .5mm
PID-Cherenkov: dRICH pfRICH hpDIRC | 320k 70k 74k | 312 17 288 | 1830Gb/s (<20Gbps to tape) 15Gbps 11Gb/sec | 28 1 6 | SiPM / ALCOR LAPPD/HRPPD /EICROC LAPPD/HRPPD /EICROC | Worse case after radiation. Includes 30% timing window. Requires further data volume reduction (software trigger, or AI/ML) 12 boxes x 24 sensor x 4 asic x 64 ch
Detector Group | Channels | AC-LGAD | SiPM/PMT | MPGD |  | RDOs / Fibers | DAM | Data Volume Estimate (Gb/s) | Data Volume To Tape (Gb/s)
 | MAPS | AC-LGAD | SiPM/PMT | MPGD | LAPPD |  |  |  | 
Tracking | 36B |  |  | 100k |  | 415 | 11 | 35 | 15
Calorimeters | 88M* |  | 150k |  |  | 249 | 11 | 15 | 15
Far Forward | 300M | 2.3M | 500 |  |  | 174 | 5 | 1 | 1
Far Backward |  | 1.8M | 700 |  |  | 117 | 4 | 100 | 2
PID |  | 3M-50M | 300k |  | 150k | 1117 | 49 | 1856 | 45
TOTAL | 32B | 7.1M-54M | 450k | 100k | 150k | 2072 | 80 | 2007 | 78
ePIC Detector Systems: Summary of Channel Counts
PID Specific Information

## Slide 11: PID Detector Specific Integrations
Adapter
Sensor
Front End Board
(FEB)
Readout Board
(RDO)
Data Aggregation Module (DAM)
Computing
Global Timing Unit (GTU)
On Detector
SMT BGA
Detector | ASIC | RDO/Fiber | DAM | Data rate | Det. Tech
pfRICH | EICROC | 17 | 1 | 15Gbs | LAPPD/HRPPD
dRICH | ALCOR | 312 | 28 | 1800Gbs | SiPM
hpDIRC | EICROC | 288 | 6 | 11Gbs | LAPPD/HRPPD
TOF (B) TOF (FEC) | EICROC | 240-500 | 12 | 6Gbps | AC-LGAD
optional
clock

## Slide 12: Scale of the Online Task
EIC minimum bias collision rate ~500kHz
  Expected real physics data from the detector < 100Gbps
Background/Noise is the wild card.
  Synchrotron radiation, Beam Gas, Detector/electronics noise
  Try to keep below the level of the physics signal.
  Online/DAQ processing will focus on Event ID and reducing the background
Front-End (DAM Boards) - will support total bandwidth O(50Tbps)
  3000+ fibers(streams) off the detector (nominally 10Gbps links)
  ~110 DAM Boards
Online DAQ/Computing (over 100/400Gbps network)
  ~200 nodes
  GPU/FPGA processing options
  Data Monitoring
  Staged disk storage (Buffer Box)

## Slide 13: Potential “Hot spots”
In general the high fiber counts coming to the DAM boards are not bandwidth driven, but the expected numbers of RDOs needed to instrument the ePIC detector can vary for different sub-systems.
Detectors using SiPM readout at thresholds sensitive to single photons
  Dark current rates will increase over time due to radiation damage.
  E.g. dRICH could eventually generate ~1800Gbps data rates
dRICH
Tracking
Network Switch
  Example:
Use some EBDC (Event Building/DataCompression) servers as a RAM buffer until Event ID processing can identify time windows that are important. Then filter data from the high rate detector we should keep.

## Slide 14: EIC DAQ/Computing schedule
The DAQ and computing schedule is planned to be somewhat accelerated in relation to the full detector construction.
A functional DAQ will be necessary for small scale detector testing as well as commissioning and pre-ops.
Hardware and software development early in the construction phase will provide a streaming DAQ system (Minidaq) well before final detector installation begins.
Final computing resources are purposely delayed to allow access to highest performing hardware available.

## Slide 15: Summary
A general picture of the scope, scale and technologies we expect to need for the EIC data acquisition and online computing reasonably clear at this stage.
Most of the DAQ/Online will be COTS-based procurements
We have a viable candidate for a Front-end interface and stream management hardware (FELIX)
Integration plans and requirements for all the detector subsystems are currently being developed.

## Slide 16: BACKUP

## Slide 17: EIC Streaming Readout Architecture
Data
Configuration & Control
Power
Detector
FEB
(Front End Board)
RDO
(Readout Board)
DAM + Computing (Data Aggregation Module)
Storage
ASIC
FPGA
Power Supply System
(HV, LV, Bias)
Cooling Systems
Fiber
LVDS ~ 20-30 m*
Analog ~ 20m
Fiber
L ~ 100 m
fiber
Monitoring
BW: O(100 Tbps)
BW: O(10 Tbps)
Goal: O(100 Gbps)
FEB
FEB
RDO
Switch / Server / Link-Exchange: Readout
Switch / Server: Processing
Switch / Server: Buffer
Total
Bunch Crossing ~ 10.2 ns/98.5 MHz
Event Rate ~ 2 us/500 kHz
Low occupancy.
Jitter ~ 5 ps
Front-End Electronics
DAQ
GTU
(Global Timing Unit)
*LVDS – ANSI/TIA/EIA-644A standard. Maximum cable length dependent on data rate.

## Slide 18: Boundary between Online and Offline
Full understanding of the Online processing responsibilities and physical make-up is still being hashed out.
We still require elements of the Offline Computing framework within the Online
Online Storage (Buffer Boxes) are intended as a “pause” and a decoupling with further Offline processing .
Offline buffering will allow several weeks for calibration and reconstruction.

## Slide 19: Slow Control Integration
There will be many slow control and monitoring systems associated with the EIC collider and ePIC detector subsystems.
  BPMs, magnets, detector biases, HV, gas flows, temps, pressures, etc…
Design and implementation of these control systems driven primarily by the relevant subsystems.
  We want to coordinate ePIC slow control as much as possible with the collider approach (still not finalized) – some SCADA type system.
  sPHENIX currently supports Ignition and WinCC using UPC-UA.
DAQ/Computing has defined responsibility for SC Integration (L4 WBS 6.10.09.2)
  Databases for maintaining SC data for calibrations and online/offline processing
  Manage SC data readout to synchronize with the physics stream data
  Maintain Software tools and libraries
Also included is the development and implementation of a general network infrastructure in the experimental hall and counting house to support slow controls and other ancillary systems.