## Slide 1
Sensor Effects in Stellar Radial Velocity Measurements
Some things to worry about when trying to measure spectral line centroids on your focal plane to +/-1 nm
Cullen Blake UPenn

## Slide 2
Outline
Detecting exoplanets via the Doppler wobble method
A modern Doppler spectrometer
Spectroscopic challenges related to CCDs
The motivation for employing thick CCDs
Suggestions/comments/questions from you, the CCD experts!

## Slide 4
RV Planet Detections Over Time
We have gotten a lot better at this over 20 years!

## Slide 5
K=1.3 m/s
Proxima Cen b (Anglada-Escude+ 2016)
RMS residuals: <1.2 m/s

## Slide 6
10cm/s corresponds to 1/6,000th of a 10 micron pixel
This is Hard

## Slide 7
Silicon Lattice: High Resolution TEM Image of individual Si atoms.
Ki Bun Kin, SPIE 2012
This is Hard
Measure Radial Velocity:
Cross-correlate 1D spectra with a mask

## Slide 8
Spectrometer resides inside highly stable vacuum chamber, thermal stability better than 1 mK
Fiber coupled to telescope
Cross dispersed echelle spectrometer
Large wavelength coverage on 2D array

## Slide 9
Calibration
Mapping of Wavelength to Pixel
What is the wavelength of the light falling right there?
For full credit, please give your answer to +/- 0.0000000000000001 m
Laser Frequency Comb
Stabilized Fabry-Perot etalons
UNe or ThAr cathode lamps

## Slide 10
Doppler Error Budgets
Important terms – Planning for < 30 cm/s:
Wavelength calibration (relatively small)
Earth’s atmosphere (microtelluric lines – yikes)
Instrument stability (thermal expansion – not too bad)
Systematic errors related to optical fibers (manageable)
Systematic errors related to the detector (double yikes)
Many of these are calibratable to a large extent

## Slide 11: Things to Worry About
Pixel-to-pixel sensitivity variations
Charge Transfer (in) Efficiency
“Stitching” errors
Sub-pixel structure (nice talk by Zhan yesterday)
Charge diffusion (can’t loose nice stellar lines in blue)
Thermal warping of the detector
Gremlins we haven't even thought of?

## Slide 12
Some CCDs are “written” using a lithographic mask that is stepped. Chip could have 16 separate blocks, for example
Result: pixels are not exactly evenly spaced
Grossly exaggerated. Actual offsets are < 1/100 of a pixel
Dispersion solutions are discontinuous
Stellar lines moves across stitch boundaries
CCD Stitching

## Slide 13
Dispersion Solution Residuals (RV units)
Stitching errors result in discontinuities in the wavelength solutions
+/- 30 km/s motion of Earth moves some stellar lines across stitch boundaries
This can produce spurious RV signals with a period of 1 year
Dumusque et al. 2015
This effect should be stable in time and calibratable
with a Laser Frequency Comb
From Dumusque – HARPS data
(Dumusque et al. 2015)

## Slide 14
CCD Thermal Distortions
CCD
Stuff that produces heat sometimes
Stuff that produces heat sometimes
Stuff that produces heat sometimes
Stuff that produces heat sometimes
Heat dissipation on chip is not constant in time
A 5 nm displacement of the chip in the primary dispersion direction:
~30 cm/s Doppler shift – Yikes!

## Slide 15
CCD Thermal Distortions
CCD
Stuff that produces heat sometimes
Stuff that produces heat sometimes
Stuff that produces heat sometimes
Stuff that produces heat sometimes
What can be done to even out heat dissipation over the integrate/read cycle?
Add heat in a precise way?
Clock registers during integration?
Wait for thermal transient to decay between science observations? What is the thermal decay time of the device?

## Slide 16
CCD Thermal Distortions
It would be nice to be able to measure these distortions in the lab, or in the instrument
Olaf Iwert and collaborators have demonstrated a projected spot constellation approach
(Lizon et al. 2016)
Diffractive Optical Element:
Laser-coupled structured
light generator
Penn State
Also, see talk yesterday by Andres Plazas
Other ideas for measuring monitoring changes in the shape of the CCD at the 1 nm level?

## Slide 17
Charge Transfer Inefficiency
Parallel (or serial) transfer direction 
Some electrons get left behind
Electrons trapped, maybe released later
Charge Transfer Efficiency > 0.99999 (typically “five nines and zero” or maybe “and a five”)
CTI (=1-CTE) < 1x10-5 (typically < 5x10-6)
Those are small numbers, BUT large-format CCDs can involve a lot of transfers
Example: 104 parallel transfers means up to 5% of charge could be lost/deferred
Why do we care for precision radial velocity measurements?

## Slide 18
Charge Transfer Inefficiency
CTI effectively induces a skewness in the spectral lines.
This is bad…looks just like a Doppler shift
to a cross-correlation algorithm
But…do we care, if it is constant in time?

## Slide 19
CTI may be worse at low flux levels – above from HST WFC3 on-orbit measurements
So, unless you can maintain very tight control of S/N … CTI is changing at some level
Time  (years)
High S/N
Low S/N
Charge Transfer Inefficiency

## Slide 20
Bouchy et al. 2009
Charge Transfer Inefficiency
This effect is HUGE in older-generation instruments (SOPHIE at OHP shown above)
But…can be modeled and spectra corrected very well

## Slide 21
Charge Transfer Inefficiency
What happens to RV when I tweak CTE?
If we change CTE by 10-7, we get a 5 cm/s RV bias
Bottom line (for this specific detector):
1) CTI < 10-7 at all flux levels (sounds tough)
2) CTI difference over relevant range of flux levels < 10-7 (maybe possible)
3) Measure CTI to +/- 10-7 across range of flux levels and model it out

## Slide 22
Charge Transfer Inefficiency
New approaches to measuring CTI?
Structured light generator in fused silica coupled to a super- stable light source - measure CTI vs. flux level in the lab?
Use a Laser Frequency Comb with modulated intensity - measure CTI vs. flux level in situ

## Slide 23
Redder is Better
HARPS
Simulated RV precision vs. central wavelength of spectral order

## Slide 24
Redder is Better
NIR Doppler spectrometers are being built (CARMENES, HPF, IRD, iLocator)
These instruments are expensive, and Hirata is scarred of the detectors...for photometry!
Extending CCD-based spectrometer sensitivty in the 850-900 nm to >1000 nm ranges very attractive option

## Slide 25
Redder is Better
NEID and ESPRESSO will both employ 40 micron thick devices
Are precise Doppler measurements possible with a 250+ micron thick device?
What are the key systematics that might limit
Would charge diffusion preclude high specral resolution at blue wavelengths on the same device?

## Slide 26
Conclusions
For the next generation of Doppler spectrometers, subtle CCD effects are important
We believe that most of these effects are understandable and/or calibratable
Some new approaches to measuring CCD performance may be required
Suggestions…what haven’t we thought of?
Thanks!

## Slide 27: Redder Is Better

## Slide 28
Redder is Better
Contours of relative integration time required to detect planets of fixed mass in host star’s liquid water habitable zone – vs. spectral order central wavelength

## Slide 29
Redder is Better
Contours of relative integration time required to detect planets of fixed mass in host star’s liquid water habitable zone

## Slide 30
RMS residuals – 13 m/s
K=59 m/s