## Slide 1: ePIC Slow Controls Preliminary Plans
July 13, 2023
Lee Flader

## Slide 2: Goals for Slow Controls
Create a homogenous hardware environment
  Equipment will be as COTS as possible
  Equipment can vary between detector types
  Equipment must be consistent between detectors of the same type
Common monitoring and controls
  Hardware will integrate with EPICS
  A central EPICS server will manage soft IOCs
  Data from the EPICS server will be backed up to DAQ servers
Tiered control scheme for low vs. high granularity of control

## Slide 3: Input Output Controllers (IOCs)
For detailed explanation visit this link.
The long and short of it:
  IOCs execute records in one or more databases
  IOCs integrate with hardware through a specified device support package
  Many device packages already exist and can be written if they don’t
Detector equipment will be encapsulated by an IOC
  The IOC will:
    Manage interlocks of high and low voltage supplies
    Provide an interface for detector controls, monitoring, and alarms
    Integrate with DAQ servers to provide historical data for ePIC at large

## Slide 4: sPHENIX Controls Implementation
Global Interlock System
Detector Interface
Detector Racks
Detector Racks
Detector Racks
Equipment Power
High Voltage Distribution
Low Voltage Distribution
Rack Sensors
Logic Controller
Detector
Detector Equipment
Power
Sensor Network
Detector Interlock System

## Slide 5: ePIC High-Level Plan
Detector Racks
Detector Racks
DAQ Interface
EPICS
Server
Soft
IOC
Soft
IOC
Soft
IOC
User Interface
Detector
Detector Racks
High Voltage Distribution
Low Voltage Distribution
Logic Controller
Detector Sensor Network
Detector Hardware

## Slide 6: Possible Example Implementation
Barrel
HCAL
Controls
Backward
HCAL
Controls
Forward
HCAL
Controls
Power Distribution Device IOCs
Logic Controller and Sensor IOCs
Barrel
Rack 1
Barrel
Rack 2
Barrel
Rack 3
APC PDU
Wiener-Iseg
MPOD HV Crate
Wiener-Iseg
MPOD LV Crate
Sensor Network and Hardware
AB MicroLogix Controller
Detector Hardware