## Slide 1: Electronics & DAQ WG
Fernando Barbosa (JLab)
10 August 2023

## Slide 2: Agenda
Welcome & News
eRD109 Updates
HDSoC Tests – Steve Titus (Jlab)
AOB

## Slide 3: Welcome & News
The TIC asked Norbert (H2GCROC) and I (EICROC) to collect the respective detector requirements, determine if they were appropriate choices and identify any needed input for further development of the ASICs and further discussions with the ASIC designers.
The TIC meeting was Monday 7 August 2023; Silvia sent an email yesterday with a summary of the findings: “Strategy emerging from the TIC meeting on August 7 dedicated to HGCROC and EICROC.”
The following are the highlights:

## Slide 4: Welcome & News
Calorimetry
  Most calorimeters benefit from the use of the new H2GCROC development.
  The backwards EMCAL – Discrete/COTS.
  The forward EMCAL – consider both H2GCROC and Discrete/COTS.
AC-LGAD Pixel Sensors
  RP, OMD, B0 trackers, Forward TOF – EICROC.
AC-LGAD Strip Sensors
  Barrel TOF: consider both EICROCx and FCFD.
HRPPD and MCP-PMT
  Consider both HGCROC/EICROC and FCFD.

## Slide 5: ePIC Readout Channels (w/ Project P6 updates)
Detector System | Channels | Nominal Readout Technology | eRD109 Initiatives
Si Tracking: 3 vertex layers, 3 sagitta layers, 4 backward disks, 5 forward disks | 7 m^2 32 B pixels 5,200 MAPS sensors | MAPS – ITS-3 | 
MPGD tracking: 3 layers | 100 k | Strips | SALSA
Calorimeters: (in P6) Forward: LFHCAL pECAL Barrel: HCAL ECAL SciFi/Pb Imaging Si Backward: ECAL nHCAL | 31640 19000 1536 5760 88 M 3256 3240 | SiPM SiPM SiPM SiPM Astropix SiPM SiPM | Discrete/H2GCROC Discrete/H2GCROC Discrete/H2GCROC Discrete/H2GCROC ASTROPIX V4 Discrete/H2GCROC Discrete/H2GCROC
Far Forward: B0: 4 AC-LGAD layers 2 Roman Pots 2 Off Momentum ZDC: Crystal Calorimeter 32 Silicon pad layer 4 silicon pixel layers 2 boxes scintillator | 1 M 560 k 320 k 400 11520 160 k 72 | AC-LGAD AC-LGAG AC-LGAD APD Si AC-LGAD PMT/SiPM | EICROC EICROC EICROC Discrete/HGCROC/H2GCROC HGCROC EICROC Discrete/HGCROC/H2GCROC
Far Backward: Low Q Tagger 1 Low Q Tagger 2 2 Calorimeters | 1.3 M 480 k 700 | Si Si PMT/SiPM | Timepix4 Timepix4 Discrete/HGCROC/H2GCROC
PID-TOF Barrel TOF CTTL Hadron Endcap TOF FTTL | 2.2 M 5.6 M | AC-LGAD AC-LGAD | EICROC EICROC
PID-Cherenkov: dRICH pfRICH hpDIRC | 5376 69632 69362 | SiPM HRPPD MCP-PMT/HRPPD | ALCOR HGCROC/EICROC/FCFD HGCROC/EICROC/FCFD
HGCROC – Si/PMTs
H2GCROC – SiPMs
EICROC – AC-LGAD
TBD

## Slide 6: Next Steps
Verify and collect missing parameters from detector groups:
  Qin Min-Max: The minimum charge sensitivity requirement is bound by the ENC from the combination of the sensor technology, the design of the ASIC input structure and their integration, e.g. parasitics.
  Cd: the sensor capacitance plus parasitics impact timing precision and drive the fine-tuning of the ASIC shaping parameters.
  Rates: the maximum rate per channel requirement impacts the design of the ASIC shaping parameters, memory depth and output link speed and/or number of links.

## Slide 7: Next Steps - continued
ePIC specifications and requirements will be proposed and discussed with the Omega/IN2P3 groups to finalize the specifications of the EICROC and its variants.
The Omega/IN2P3 will then propose design and development plans.
The path is clear and will follow the eRD109 initiatives.

## Slide 8: eRD109 Updates
 | Detector/Technology | Discrete/ASIC | Group | Awarded
A | Calorimeter | Discrete | IUCF | April 2023
B | Calorimeter | HGCROC | ORNL | April 2023
C | dRICH | ALCOR | INFN | April 2023
D | AC-LGAD | EICROC | Omega/IN2P3 | Fall 2023
 |  | FCFD | FNAL | June 2023
 |  | Barrel L-M Serv. Hybrid | ORNL | April 2023
 |  | 3rd Party Evaluation | UCSC | Pending Legal
E | MPGD/µRWell | SALSA | CEA | May 2023
 |  |  | USP | May 2023
FY23 - Contract awards have taken much longer than expected.
The synergies of the various groups working on the clock will be considered at a future Electronics & DAQ WG meeting.
FY24 – Proposed and subject to DAC review 28-31 August 2023.
 | Detector/Technology | Discrete/ASIC | Group
A | Calorimeter | Discrete | IUCF
B | Calorimeter | HGCROC | ORNL
C | dRICH | ALCOR | INFN – BO, TO
D | AC-LGAD | EICROC | Omega/IN2P3/IJCLab/CEA/IRFU
 |  | FCFD | FNAL
 |  | Barrel L-M Serv. Hybrid | ORNL
 |  | High Precision Clock Distribution | BNL/Rice/UIC/ORNL
E | MPGD/µRWell | SALSA | CEA
 |  |  | USP