## Slide 1
Introduction to Bayesian Optimization
Yinan Wang, Ph.D.
Assistant Professor, Department of Industrial and Systems Engineering
Rensselaer Polytechnic Institute
Collaboration Meeting on Aug. 25 @ Cornell U.

## Slide 2
Motivation
Identify the dimension gap
Set the locations and forces of actuators
Generate corrected dimension
Fuselage Assembly
Prediction
Optimization

## Slide 3
Data Visualization
Intuitive Example of Bayesian Optimization

## Slide 4
Data Visualization
Intuitive Example of Bayesian Optimization
Note: With an appropriately defined surrogate model and an acquisition function, we can efficiently evaluate the point that will highly likely lead to the optimized output.
Acquisition function
Surrogate model

## Slide 5
Data Visualization
Note: With an appropriately defined surrogate model and an acquisition function, we can efficiently evaluate the point that will highly likely lead to the optimized output.
General Formulation

## Slide 6
Surrogate Model: Gaussian Process (GP)
GP is essentially a model of the distribution of functions given the current observations.
GP model: is determined by the mean function and covariance function
Posterior mean and variance can be computed explicitly given the collected observations (dataset).

## Slide 7
Surrogate Model: Multi-layer Deep Gaussian Process (MGP)
Note: MGP is proposed to learn the complex dependency of the underlying process and improve global optimum function approximations.
-layer MGP: Formulation
response
input
Transformation of input (feature space)
Mean function in the layer
Covariance kernel
AlBahar, A., Kim, I., Wang, X., & Yue, X. (2022). Physics-constrained Bayesian optimization for optimal actuators placement in composite structures assembly. IEEE Transactions on Automation Science and Engineering.
Wang, Y., Yue, X. (2023). Multi-modal Deep Learning Methods with Applications to Advanced Manufacturing (under review).
-layer MGP: Marginal likelihood
Gram matrix of the kernel function

## Slide 8
Surrogate Model: Performance Comparison
Gaussian or Student-t distributed noise
Visualization of
SGP: Stationary GP with Matern kernel.
NSGP: Non-stationary GP with Polynomial or ArcCosine kernels.
NNGP: NN for mean function and Matern kernel.
MGP: Multi-layer GP for mean function and Matern kernel.
Note: Nonstationary GP allows the model to adapt to functions whose smoothness varies with the inputs; Stationary GP has the covariance between any two points is a function of Euclidean distance.
AlBahar, A., Kim, I., Wang, X., & Yue, X. (2022). Physics-constrained Bayesian optimization for optimal actuators placement in composite structures assembly. IEEE Transactions on Automation Science and Engineering.
Wang, Y., Yue, X. (2023). Multi-modal Deep Learning Methods with Applications to Advanced Manufacturing (under review).

## Slide 9
Surrogate Model: Performance Comparison
Note: The 95% confidence intervals of the predictive posterior distributions of the 2-layer MGP and 3-layer MGP have a better coverage on observations with narrower intervals.
AlBahar, A., Kim, I., Wang, X., & Yue, X. (2022). Physics-constrained Bayesian optimization for optimal actuators placement in composite structures assembly. IEEE Transactions on Automation Science and Engineering.
Wang, Y., Yue, X. (2023). Multi-modal Deep Learning Methods with Applications to Advanced Manufacturing (under review).

## Slide 10
Acquisition Function: GP Upper Confidence Bound (GP-UCB)
https://ekamperi.github.io/machine%20learning/2021/06/11/acquisition-functions.html
Exploitation
Exploration
Note: UCB is a weighted sum of the expected performance captured by and the uncertainty . It will favor exploitation with smaller and exploration with larger .

## Slide 11
Acquisition Function: Expected Improvement (EI)
Exploitation
Exploration
Note: The trade-off between exploitation and exploration can be adjusted by introducing a hyper-parameter in . A larger value of will encourage exploration.

## Slide 12
Demonstration of BO

## Slide 13
Constrained Expected Improvement (cEI)
Optimization with linear constraints
Objective and constraints as GPs
Integrate the feasibility through the CDF
infeasible
Note: The idea of cEI can naturally benefit to the physics-constrained optimization.

## Slide 14
Case Study: Physics-Constrained Bayesian Optimization
Note: The objective is to place a set of actuators in all feasible locations to minimize the total variations under the constraints of feasible ranges of forces and a maximum number of actuators.
Adjusted deviation
Initial deviation
Displacement matrix
AlBahar, A., Kim, I., Wang, X., & Yue, X. (2022). Physics-constrained Bayesian optimization for optimal actuators placement in composite structures assembly. IEEE Transactions on Automation Science and Engineering.
Wang, Y., Yue, X. (2023). Multi-modal Deep Learning Methods with Applications to Advanced Manufacturing (under review).

## Slide 15
Case Study: Results
Note: MGP-CBO achieves smaller shape deviation using fewer actuators and smaller forces.
AlBahar, A., Kim, I., Wang, X., & Yue, X. (2022). Physics-constrained Bayesian optimization for optimal actuators placement in composite structures assembly. IEEE Transactions on Automation Science and Engineering.
Wang, Y., Yue, X. (2023). Multi-modal Deep Learning Methods with Applications to Advanced Manufacturing (under review).
Performance comparison between physics-constrained BO and other optimization method

## Slide 16
Summary
Bayesian optimization is a sequential optimization framework with the interaction between surrogate model and acquisition function.
Domain knowledge or physical insights can be incorporated into the design of surrogate model and/or acquisition function to develop physics-informed Bayesian optimization.
There is still no uniform framework for Pi-BO, which is worth exploring for specific application task (i.e., optimization of Beam polarization) and generalizing into widely applicable framework.

## Slide 17
Thank you!
Q & A
Yinan Wang (wangy88@rpi.edu)