## Slide 1: EIC – IP-6
Ring Inside
Ring Outside
Electrons
Hadron
Control
&
DAQ-ROOM
Assembly
Hall
Possible
2nd Detector
Location
Project
Detector
Location
IP-6 provides an interaction region with
a hall with all infrastructure needed for a collider detector
Assembly hall provides amble space for installation and maintenance.

## Slide 2: IR-Integration and Interfaces
Space Constrains:
-4.5 m – IP – +5m not negotiable
<50 cm space to 1st IR-magnets occupied by vacuum pumps, valves, …..
IP moved 81 cm towards ring inside compared to RHIC; y: 432 cm above floor
RCS to IP: radial distance 335.2 cm at a height of 372 cm above floor
  Maximum outer radius ~ 3.2 m
limited installation possible in Collider Hall
  endcap hadron calorimeters need to be split transverse to beam pipe
  RCS vacuum needs to be broken
9.5 long detector does not fit through the door
  Door-Size: 823 cm x 823 cm
  endcaps need to remain in collider hall, if central detector rolls in assembly hall
RCS
Hadrons
Electrons