## Slide 1: WBS 6.10.14 Polarimetry
Oleg Eyser (BNL) / Dave Gaskell(JLab)
EIC Detector Comprehensive Detector Design Review
August 29-30, 2023

## Slide 2: Requirements
Polarized Electron Beams | Polarized Hadron Beams
Highly polarized beams, P≈70% | 
Fast feedback for machine setup | 
Excellent measurement of absolute polarization, ΔP/P≈1% | 
Non-destructive polarimetry | 
Bunch-by-bunch polarization measurement (fill pattern: P↑,P↓, Δt≈10 ns) | 
Bunch replacement every few minutes (Sokolov-Ternov ΔP↑≠ΔP↓) | Polarization decay (ΔP≈1-2%/h)
 | Transverse bunch polarization profile
Polarization vector at experiment (transverse, longitudinal) | 
Charge questions:
Given the detector progress over the last two years and the status of the ePIC detector, are the projected timelines of the Electron-Ion Collider detector feasible? Do there remain significant open detector technology questions?
Are the requirements for the detector and their flow down sufficiently comprehensive for this stage of the project to complete the design of the various detector technologies?
Are the interfaces between the elements of the design adequately defined for this stage of the project and to proceed with the detector long-lead procurement items?
Is the design of these long-lead procurement items sufficiently advanced and mature to start procurement in 2024? Are the technical specifications complete?
Is the projected design maturity of the further detector components likely to be accomplished by the end of 2024 for CD-2 and CD-3?
Is the overall schedule for completion of the design, production, and installation of detector components realistic?
#2 requirements

## Slide 3: Overview
Electron bunches are replaced every few seconds.
Hadron bunches are stored for many hours.
transverse
longitudinal
IR-4
Hadron polarimetry
HJET for absolute polarization
Fiber target for time dependence and bunch profile
IR-6 / ePIC
Local polarimetry
Inside spin rotators
Fiber target for hadron polarization orientation
Compton backscattering for electron polarization
#2 requirements
#3 interfaces

## Slide 4: Electron Polarimetry – WBS 6.10.14.01
Electron Storage Ring Compton polarimeter
Rapid Cycling Synchrotron Compton polarimeter
Electron Storage Ring Compton (ESR)
 Upstream of IP6, between IP and spin rotating solenoid
Will measure polarization for each bunch
Measure both transverse and longitudinal beam polarization
Detect backscattered photon and scattered electron
Rapid Cycling Synchrotron Compton (RCS)
Primarily for machine setup – less stringent precision requirements
Detect backscattered photons, multi-photon mode
Average over several bunches
e-beam
#2 requirements
#3 interfaces

## Slide 5: Electron Storage Ring Compton
Hadron beamline
D3EF4
Q8EF Xfocusing
Q7EF
Q6EF
(-18.6 T/m)
Q5EF
(+12.2 T/m)
Q4EF
(-4.15 T/m)
Q3EF
D2EF4
(0.29 T)
electron beamline
Laser IP
72 m upstream of IP-6
Electron detector
9.7 m from Laser IP
Photon detector
29 m from Laser IP
Sim axes at Q9EF
Crab cavity
Will operate in “single photon” mode
Polarimeter Components:
RF-pulsed laser system (under development)
Position sensitive detectors (diamond strips) for scattered electrons and backscattered photons
Calorimeter for backscattered photons
Beam energy | PL | PT
5 GeV | 96.5% | 26.1%
10 GeV | 86.4% | 50.4%
18 GeV | 58.1% | 81.4%
Polarization components at Laser IP
*
#2 requirements
#3 interfaces
#5 design maturity

## Slide 6: ESR Compton – Laser System
Laser system based on similar system used in JLab injector and LERF
Gain-switched diode seed laser – variable frequency, few to 10 ps pulses @ 1064 nm
   Variable frequency allows optimal use at different bunch frequencies (100 MHz vs 25 MHz)
Fiber amplifier  average power 10-20 W
Optional: Frequency doubling system (LBO or PPLN)
Insertable in-vacuum mirror for laser polarization setup
Gain-switched seed laser components procured under earlier generic EIC R&D  (Ciprian Gal et al.)
Fiber amplifier ordered  work will restart at JLab in existing Compton polarimetry laser lab
#2 requirements
#3 interfaces
#5 design maturity

## Slide 7: Position Sensitive Detectors
JLab Hall C diamond detector
10 ns
Position sensitive detectors needed to measure:
  Scattered electrons  PL
  Backscattered photons  PT
Technology choice – diamond strips  radiation hard, good time response
Diamond used during Q-Weak expt at Jlab  no performance degradation after 10 MRad of exposure
Required detector segmentation = 500 mm (electrons)/100-200 mm (photons)
Detector size = 6 cm (electrons)/ 5 cm (photons)
Custom ASIC required  new “FLAT32” chip based on “CALYPSO” (used at LHC) under development for Jlab/MOLLER
  Already meets timing requirements of EIC (10 ns)
#1 technology questions
#5 design maturity

## Slide 8: Photon Calorimeter
On-going value engineering (cost/risk)
Good energy resolution required for longitudinal polarization measurements, but fast time response required for bunch-by-bunch measurements
Tungsten-powder calorimeter (similar to STAR Forward Upgrade) satisfies timing requirements for Compton polarimeters
  Scintillating fiber embedded in tungsten powder
  Ample experience with such detectors at BNL
Detector size 16 x 16 mm2
Initially, that long time component rules out lead-tungstate
  Recent publication suggests time response at room temperature may be acceptable
M. Follin et al 2021 JINST 16 P08040
#1 technology questions

## Slide 9: ESR Compton – Detector Simulations
Need high position resolution for backscattered photons for transverse polarization measurement
Best results from longitudinally segmented calorimeter with (x-y) diamond strips
Overall efficiency 60% w/adequate resolution
x and y diamond strips
0.5 cm thick PbWO4
20 cm long block

## Slide 10: ESR Compton – Beamline Design and Synchroton Backgrounds
Beampipe design for region downstream of laser-electron beam collisions underway
Need photon exit window and room to accommodate scattered electrons and electron detector
Impedance likely an issue – electron detector may need to be outside beam pipe, but this could limit how much of the spectrum we can detect
Synchrotron backgrounds at 18 GeV require 2 cm tungsten shield!  Although polarimeter location has been chosen, need to iterate with machine group to minimize synchrotron backgrounds (dipole bend too large)
Zhengqiao Zhang (BNL)
#2 requirements
#3 interfaces
#5 design maturity

## Slide 11: Rapid Cycling Synchrotron Compton
RCS properties
RCS accelerates electron bunches from 0.4 GeV to full beam energy (5-18 GeV)
Bunch frequency  2 Hz
Bunch charge  up to 28 nA
Ramping time = 100 ms
Polarimetry challenges
Analyzing power often depends on beam energy
Low average current
Bunch lifetime is short
Compton polarimeter can also be used for measurement of polarization in RCS
Measurements will be averaged over several bunches – can tag accelerating bunches to get information on bunches at fixed energy
Requires measurement in multiphoton mode (many backscattered photons/electron bunch)
Laser IP
Photon detector
Bijan Bhandari - BNL
#2 requirements
#3 interfaces
#5 design maturity

## Slide 12: Transverse Polarimetry in Multi-Photon mode
Highest precision transverse Compton polarimeter operated in single photon mode (HERA)
RCS requires position sensitive measurement in multi-photon mode
Need highly segmented detector sensitive to signal size (not just counts above threshold)
LEP polarimeter operated in this fashion, although with relatively low precision
Simulations will guide the detector technology choice based on requirements for radiation hardness and position resolution
Note: RCS Compton only needed for machine setup
#1 technology questions
#2 requirements
#5 design maturity

## Slide 13: Overview
IR-4
Hadron polarimetry
HJET for absolute polarization
Fiber target for time dependence and bunch profile
IR-6 / ePIC
Local polarimetry
Inside spin rotators
Fiber target for hadron polarization orientation
Compton backscattering for electron polarization
Hadron bunches are stored for many hours.
transverse
longitudinal
#2 requirements
#3 interfaces

## Slide 14: Hadron Polarimetry – WBS 6.10.14.02
Using transverse spin asymmetries from elastic recoil
  Based on RHIC experience
  Absolute polarimeter: HJET
  Fast polarimeter: ultra-thin fiber target
Measure energy, angle, time-of-flight
RHIC Data
Simulation (PYTHIA+GEANT4)
#2 requirements
#3 interfaces

## Slide 15: IR-4 Layout
10X Kickers
3X HSR 98 MHz
HSR Triplet
Carbon polarimeter
HJET
D0 replacement dipole
Tagger location & drift space
HSR Q4
Sector 3
Sector 4
RCS
ESR
Hadron Storage Ring
Choice of location driven by size of HJET setup and the following drift space
Phys. Rev. Lett. 123, 162001 (2019)
Currently at IR-12
Decommissioning after RHIC Run 25
Planned setup in BNL Physics for refurbishment and modifications
  Target gas analyzer ( content)
  Target chamber / magnetic field
#2 requirements
#3 interfaces
#5 design maturity

## Slide 16: Local Polarimeter at IR-6
Spin rotators for longitudinal polarization
Crab cavities for increased luminosity in collision
Limited space in hall / straight section
Polarimeter in incoming hadron beam
  Single target chamber similar to IR-4 device
  Primarily for polarization vector determination
#2 requirements
#3 interfaces
#5 design maturity

## Slide 17: Fiber Target Polarimeters
Ultra-thin ribbon targets:
Target holder inside the beam pipe
Energy loss of hadron beam heats up target
Investigating target modifications / material
#1 technology questions
#2 requirements
#5 design maturity

## Slide 18: Impedance in Polarimeter Chamber
A. Blednyk (BNL)
Usability of existing chambers to be verified for EIC short bunch spacing (GHz)
Fiber target chambers
Single-Bunch - Ok
Higher order modes → Pumping ports will require RF shielding
Simulations with targets are the next step
Hydrogen Jet (IP4)
Single-Bunch simulations in progress
Single bunch simulation for geometric and resistive wall wakefields
#2 requirements
#3 interfaces
#5 design maturity

## Slide 19: Hadron Polarimeter R&D
Second detector layer installed in pC polarimeter
  Included in DAQ since start of Run22 operations
  Data from RHIC Run 22
Tof vs. Ekin in layer 1 (F)
with a match in second layer (R)
Hybrid simulation
  PYTHIA & GEANT
  Repeated with 10 ns bunch spacing
Proton time-of-flight
Veto punch through particles
(Part of WBS 6.02.03 Accelerator R&D)
#2 requirements
#3 interfaces
#5 design maturity

## Slide 20: Hadron Polarimetry R&D
break-up
  Tagging with hadron calorimeters
ZDC’s installed downstream of HJET (behind DX)
  Operational in RHIC Run 23 ()
  Neutron peak calibration needed
To be scheduled in APEX
  beam, EBIS source is ready
  RHIC Run 24
target
DX
(Part of WBS 6.02.03 Accelerator R&D)
#2 requirements
#3 interfaces
#5 design maturity

## Slide 21: Polarimetry Subsystem Status Review
Review took place Jan. 17-18, 2023
Committee:
Dipangkar Dutta (Mississippi State University)
Jenny List (DESY)
Paolo Lenisa (Ferrara University)
Frank Rathmann (Julich)
Tuesday, Jan. 17
08:00-08:30 Executive Session
08:30-09:00 Welcome and Introduction to the EIC Project (Elke Aschenauer and Rolf Ent)
09:00-09:30 Polarized Beams at the EIC (Vadim Ptitsyn)
09:30-10:10 Hadron Polarimetry Overview (Oleg Eyser)
10:10-10:40 R&D for Hadron Polarimetry
10:40-11:00 Break
11:00-11:40 Electron Polarimetry Overview (Dave Gaskell)
11:40-12:10 Backgrounds for Compton Polarimetry (Mike Sullivan)
12:10-12:40 Laser System for Compton Polarimetry (Ciprian Gal)
Wednesday, Jan. 18
09:00-11:30 Executive Session
11:30-12:00 Closeout

## Slide 22: Polarimetry Subsystem Status Review
Summary of Recommendations
Hadron Polarimetry
Target gas analyzer should be used to determine molecular fraction in the H-Jet
Explore using thinner Si detectors in both H-Jet and p-Carbon polarimeters to veto punch through events
In addition to exploring new target materials for p-Carbon polarimeter, explore larger beam size
Obtain beam time with AGS p-C polarimeter to test detectors
Theoretical assessment 3He-3He analyzing power
Further 3He studies during remaining RHIC runs
Electron Polarimetry
Develop alternative detector concept based on silicon
Detailed simulations including all backgrounds and shielding
Explore transverse polarization measurements using synchrotron radiation
More detailed detector requirements for RCS polarimeter
On-going/scheduled
alternatives under discussion
On-going effort, not part of initial baseline

## Slide 23: Polarimetry Schedule
Final RHIC operations
Final Design Review
Final commissioning
Polarimeters ready for beam development
(L2_0600 Construction of Components Complete)
#6 schedule

## Slide 24: Summary
The basic polarimetry methods and detector technologies are established. Options for value engineering are under discussion.
The requirements and interfaces, mostly with the accelerator, are defined.
The design is progressing towards CD2/3 in FY25.
  Demands at EIC are higher than at previous facilities, some improvements are still needed.
  Future modifications beyond the EIC baseline are not precluded within the current scope.
All polarimeters have to be ready for operation with the start of polarized beam development. Some polarimeters are for solely for beam development, while others provide constant monitoring throughout physics data taking.
The schedule has significant float.

## Slide 25: EXTRA

## Slide 26: ESR Compton – Synchrotron Radiation
Water cooling
Mike Sullivan (SLAC)
Mask needed to mitigate SR on photon exit window
120 W remains with broad peak at the center of the window
 May need a fairly thick W shield ( 2 cm) for the 18 GeV beam
10 GeV beam has a softer photon energy spectrum  2 mm of W looks to be quite effective in blocking all of the SR photons at this beam energy

## Slide 27: ESR Lattice Update
Old lattice
New lattice
dipole
“Compton” dipole removed from new lattice
New ESR lattice not compatible with existing Compton design
 Not clear new lattice can accommodate Compton requirements

## Slide 28: Beam Heating of Target Material
*Calculation by Peter Thieberger
RHIC conditions

## Slide 29: Carbon Polarimeter
is very steep
Energy calibration with -particles
  Thickness of dead layer in front of Si detectors
Energy loss in target
  Path length depends on ribbon orientation
  Multiple scattering in target
  Sway of ribbon in proton beam
Dead layer
Measured energy