## Slide 1: Background and Detector Impact
Elke-Caroline Aschenauer (BNL)
for the ePIC and EIC Collider Background WGs
ePIC TIC Meeting
September 7th, 2023

## Slide 2: Beam Background / Radiation at IR
The HERA and KEK experience show that having backgrounds well understood, is crucial for the EIC collider and detector performance
There are several background/radiation sources :
  primary collisions
  beam-gas induced
  synchrotron radiation
Note:
different to HERA and KEK the length of beam pipe the both beam share, is thanks to the crossing angle minimized
GEANT4
Ring Outside
Ring Inside

## Slide 3: EIC Beam Parameters
electron beam current and energy impact electron beam gas background and synchrotron radiation
 Radiated SR power: P(kW)=88.46 EB(GeV)4 / r(m)2 I (A)
hadron beam current impacts hadron beam gas
beam energies and luminosity impact the radiation and neutron fluence

## Slide 4: Beam Background / Radiation at IR
GEANT4
Both beams
Touschek scattering is related to intra-beam scattering, leads to particle loss, and hence a reduction in the beam lifetime  simulated by accelerator colleagues  design of momentum collimators
Touschek: Single-scattering IBS, so to speak. Transfer of transverse momentum, from the transverse focusing, into the
longitudinal direction when two electrons scatter off each other. The resulting longitudinal momentum exceeds the bucket height.
Touschek lifetime: from EIC-CDR is 5.27 h @ 10 GeV
and such not a major concern for EIC

## Slide 5: Beam Background / Radiation at IR
GEANT4
Electron beam:
Higher order mode losses
  Local heating at injection and ramp (short bunches)
  degradation of vacuum
  not relevant for EIC as we inject on energy and keep impedance low in the IR
background due to de-excitation of beam if bunches are replaced
  Note: 1 electron bunches are replaced per 1 s
  There should be “no” background for the experiment as the idea is to shave off the electron tails beyond 6 s in the transfer line.
  Electrons are injected on orbit and on energy (with reasonable errors) in one sigma, this is also required to not impact the proton beam performance
  Injection is at IP-12
  6 s electron beam would always be well within the geometric aperture limits of 13.5/23 s.
  Dynamic aperture limits are very similar.

## Slide 6: Beam Background / Radiation at IR
Electron beam:
Synchrotron radiation
  extensive simulations by of SR accelerator background WG group
  SynRad+ modeling software
  Input:
  3D model of beampipe
  Beam emittance, current Magnet locations and fields
  bunch geometry – core and tails
  Output:
  Synchrotron Radiation – Position, Flux, Energy, Direction
  Synchrotron Radiation Mitigation:
  Photon absorber configuration:
  Horizontal plane only
  Annular configuration
  Length, diameter, position
  Beamline dimensions:
  Wider beam pipe for
    13.5 s clearance in x
    23 s clearance in y
  Beampipe material/structure
  2-5 mm Au coding
  Sawtooth/ridge texture for photon absorption

## Slide 7: SR-Mitigation  Crossing Angle
Brings focusing magnets close to IP
 high luminosity
Beam separation without separation dipoles
 reduced synchrotron radiation
background
But significant loss of luminosity
Solution: Crab crossing
Head-on collision geometry is restored by rotating the bunches before colliding (“crab crossing”)
Bunch rotation (“crabbing”) is accomplished by transversely deflecting RF resonators (“crab cavities”)
Actual collision point moves laterally during bunch interaction
Completely new concept for a collider

## Slide 8: Synchrotron Radiation Results
Rates in different subdetectors:
Effect of gold coating on SR
 Example mvertex MAPS layers
Need to repeat all synchrotron radiation studies due to recent lattice change

## Slide 9: SynRad+/Molflow+ Coupled Simulations
Pump ports
Photon flux density on surfaces
Pressure profile along beamlines
Chart: Dose [accumulated photons/m]
| 1430000000000000 | 4.29E+18 | 1.43E+19 | 1.43E+20 | 1.43E+21 | 1.4300000000000001E+22 | 1.4299999999999999E+23 | 1.43E+24 | 1.4299999999999999E+25
OFHC H2 | 0.00196 | 0.00196 | 0.000918 | 0.000214 | 5e-05 | 1.17e-05 | 2.73e-06 | 6.35e-07 | 1.48e-07
OFHC CO | 0.0004 | 0.0004 | 0.000152 | 2.41e-05 | 3.8e-06 | 6e-07 | 9.48e-08 | 1.5e-08 | 2.36e-09
OFHC CO2 | 0.000465 | 0.000465 | 0.000221 | 5.33e-05 | 1.29e-05 | 3.1e-06 | 7.5e-07 | 1.81e-07 | 4.35e-08
NEG H2 | 1.12e-05 | 1.12e-05 | 4.65e-06 | 1.94e-06 | 8.08e-07 | 3.35e-07 | 1.4e-07 | 5.83e-08 | 2.42e-08
NEG CO | 3.2e-06 | 3.2e-06 | 1.33e-06 | 5.55e-07 | 2.31e-07 | 9.6e-08 | 4e-08 | 1.66e-08 | 6.9e-09
NEG CO2 | 6.4e-07 | 6.4e-07 | 2.65e-07 | 1.11e-07 | 4.6e-08 | 1.92e-08 | 7.98e-09 | 3.33e-09 | 1.38e-09
Convert to desorption
Applied as surface outgassing
Geometry imported from SynRad+ to Molflow+
SR no impact on vacuum of far-forward beam pipe  ZDC, RP, ….

## Slide 10: Pressure Profile along IP
Chart: s [m]
Q0eF
Q1eF
Detector
10GeV, 2.5A
eF IP1
eF IP2
eF IP3
eF IP4
eF IP5
FPA
eR IP1
10,000 Ahr, no pumps in cryostat
+5/-15m Avg: 1.3e-8
+4.5/-5m Avg: 3.3e-9
10,000 Ahr, all pumps
+5/-15m Avg: 3.0e-9
+4.5/-5m Avg: 2.7e-9
100 Ahr, no pumps in cryostat
+5/-15m Avg: 1.5e-7
+4.5/-5m Avg: 3.5e-8
Note all simulations presented use blue curve:
10000 Ah correspond to 5month @ 1034 cm2s-1
 beam pipe bake-out critical to keep a good vacuum
e-beam
IP

## Slide 11: Beam Pipe Bake-Out
Remember: limited installation and maintenance possible in Collider Hall due to space constrains
Will have to break vacuum each time we roll into the assembly hall for maintenance
  will have separation valves around the detector
    no pumping over 9.5 m
  will vent under nitrogen and keep beam pipe rolling
  with detector under nitrogen
  will need to bake-out beam pipe integrated in central detector
Considerations for central beam pipe bake-out
  1st MAPS mvertex tracker sits at 36 mm radius, so 5 mm from the beam pipe
  MAPS sensor cannot go higher as 30oC
    rules out std. bake-out methods and NEC
    pumping
    want to cool with air to keep material budget
    as low as possible
  Investigate baking out the central beam pipe
  with hot gas at > 100oC to break water bonds
rolling to
assembly hall

## Slide 12: Beam Gas Background
GEANT4
Electron beam:
Beam gas interactions
  generation of non-gaussian tails  accounted in accelerator simulations
    Off momentum electrons  will be shielded by collimators  simulations of collimation system underway
  Big contribution for detector background
  Bethe-Heitler process: eBeam + H2restgas  e’ + g + H2restgas
  Kinematics: fixed target  particles boosted towards outgoing electron direction
  Generate real tracks not random hit pattern like SR
  Mitigation: excellent vacuum
Proton beam:
Low beam lifetime during injection and ramping  collimator setup  simulation by accelerator colleagues, but ample experience for 21 y of RHIC running
Beam gas interactions
concern: large hadronic cross section p/A + H2restgas
  Secondary interactions with aperture limitations, i.e. magnets, beam pipe, masks
  Beam-gas interactions are also a source of neutrons that thermalize within the detector hall and can cause damage  need still to model it
  Kinematics: fixed target  particles boosted towards outgoing hadron direction
  Generate real tracks not random hit pattern like SR
  Mitigation: excellent vacuum

## Slide 13: Cross Section and Rate Comparisons
Remember:
electron beam current and energy impact electron beam gas background and synchrotron radiation
hadron beam current impacts hadron beam gas
Different to hadron-hadron colliders beam related background cross-sections are larger than signal cross-section

## Slide 14: DIS and Beam Gas Background Rates
Hadron Beam Gas
protons: 275 GeV
vacuum after 10000 Ah
Electron Beam Gas
10 GeV
vacuum after 10000 Ah

## Slide 15: Notes on Far-Forward and Backward
Far-Forward:
”no” contribution from synchrotron radiation and electron beam gas
hadron beam gas contribution
  good vacuum in hadron beam pipe  acceptance only for limited region along beam pipe
Far-Backward:
”no” contribution from hadron beam gas
electron beam gas contribution
  vacuum level good in this part of electron beam pipe – 5 x 10-10 mbar
Need still to simulate synchrotron radiation for this region
low-Q2 tagger sees large rate from process used to measure luminosity
 Bethe Heitler ep  e’p’g lepton goes to the low-Q2 taggers
Total cross section for elastic bremsstrahlung and for two models for inelastic ep scattering​
Large bremsstrahlung cross section implies a pile-up interaction in each bunch crossing​
The bremsstrahlung makes a background in photoproduction measurement​
Reconstructed Q2 shown for bremsstrahlung and photoproduction
True Q2 for bremsstrahlung in consistent with zero​
Distributions are normalized to event rates​
Opportunity to extract clean photoproduction signal over a limited interval in Q^2

## Slide 16: Radiation at IR
Primary collisions contribute a substantial fraction of the ionizing radiation and low energy neutron fluence in the experimental hall
Simulations use Pythia-6 well tuned to HERMES, COMPASS and HERA
  rates: “min-bias” DIS data  Q2> 10-9 GeV2
  Validation: Yuri Fisyak et al. NIM A 756 (2014) 68-72, arXiv:1310.2495
Study dependence on physics-list in GEANT-4  especially for low energy neutrons

## Slide 17: Proton and Neutron Radiation

## Slide 18: Radiation in ZDC

## Slide 19: Impact of Beam Background on Detector Performance
Background hits will impact the track finding and reconstruction
  Embedding of beam background events in DIS signal event in MC simulations
  Impact depends on speed of subdetector readout speed, MAPS 2 ms AC-LGAD 30 ps
Background will impact of energy reconstruction in calorimeters
Need to know the total rate per readout channel (== Background + DIS) for DAQ
  impact needed data rate capabilities
Total Radiation (== Background + DIS) impact subdetector lifetimes
 urgently need the thresholds per subdetector on hit level and summed energy to
finish all the work  Please fill excel-sheet at
EPIC Detector DigitizationModel.09.2023.xlsx by Friday CoB

## Slide 20: Summary and Outlook
All background sources are understood and simulated
  well documented on the wiki: https://wiki.bnl.gov/EPIC/index.php?title=Background
  good vacuum is critical to keep beam gas related backgrounds under control
Impact of SR and beam gas events on detector performance understudy
  embedding of beam backgrounds in DIS events under way  see Kolja’s talk
Next studies
  ion beam gas events
  update SR studies with new electron lattice including far-backward direction
  study beam gas event contribution to radiation and neutron fluence
Information:
  wiki: https://wiki.bnl.gov/EPIC/index.php?title=Background
  email-list: eic-projdet-background-l@lists.bnl.gov Indigo: https://indico.bnl.gov/category/461/ Meetings: bi-weekly Tuesday at 1:00 pm to 2:00 pm

## Slide 22: Lessons from HERA II upgrade
HERA performed an upgrade to increase luminosity by a factor of 5
  Mainly by squeezing the beam more at the IP by redesign of the IR
The upgrade increased backgrounds dramatically  Several month shutdown to implement improvements
Main culprits:
  no careful simulations prior to the upgrade
  Proton beam-gas interactions most severe background
    Needed an extremely good vacuum to mitigate this
  Synchrotron radiation background
    Background to detectors
    Excess heating of beam pipe
      Can damage flanges, etc.
      Can heat beam pipe, decreasing vacuum
  Electron beam-gas

## Slide 23: Lessons from HERA II upgrade
Dynamic pressure increase due
to thermal and photo desorption
Pressure vs. integrated electron
current 2002 - 03
Proton Beam Gas Background
Two time constants for vacuum
conditioning
Short term after leaks 20 – 30 days
Long term 600 days