## Slide 1: Pythia8 occupancy studies
Henry Klest

## Slide 2
  Determine necessary SciFi resolution in Z
  Most challenging for us will probably be jets at very high Q2
    High multiplicity & likelihood to be in the barrel
  Pythia 8.303 + Dire
    Used in my HERA high Q2 event shape analysis
    Acceptable to first order, but fewer multi-jet events than in data
    Non-radiative, lepton PDF off
  Study Q2 > 1000 GeV2
    Cross section of ~280 pb
    10M events simulated, corresponds to something like 35 fb-1
Goals & setup

## Slide 3
  If two photons land in the same phi slice of the SciFi, likely that their energy will be summed unless we do something beyond GlueX
    GlueX signals ~ 80 ns long, rise time ~ 8 ns
    8 ns corresponds to something like a meter in Z
    Time resolution much much shorter than pulse length, only need first few samples to determine time of arrival
    Likely need first pulse to start falling before second pulse can be distinguished
  This presents an issue for , AstroPix can tell us that there were two photons, but without E1 and E2 separately can’t determine the invariant mass
motivation
Pulse 1
Pulse 2
Summed Pulses

## Slide 4
Kinematics

## Slide 5
Kinematics

## Slide 6
Simulation
  For these high Q2 events, how likely are we to have two photons in the same event registered by the same SiPM*
    48 Modules, 5 SiPMs wide, each SiPM covers 1/240th of the azimuth
  Assume for now that particles striking the same phi slice are integrated
  Charged particles will have energy well measured by inner detectors, likely to deposit only MIP energy
    Can subtract tracker energy from total measured in Ecal
  Big worry is neutrals, especially photons
*If signals are too slow, could even have photons from different events overlapping

## Slide 7
Multiplicities in Barrel
Bumps at even numbers from
Peaks at 0 could be an artifact
Barrel defined as pseudorapidities between -1.7 and 1.3

## Slide 8
Particles in Same Phi Slice
  Unfortunately, particles in the same phi slice tend to also be close in Z
    Imagine a Gaussian jet in x,y space

## Slide 9
Likelihood that an event has two photons in the same phi slice
~50%

## Slide 10
Energy of those two photons in the same phi slice

## Slide 11
Likelihood that an event has a photon in the same phi slice as the DIS electron
1%

## Slide 12
  High Q2 will be challenging on the SciFi
    Considering here only impact position, no spreading of showers between SiPMs which will certainly happen, real case is likely worse
  Would be nice if we could somehow distinguish two hits in the same phi slice
    Faster SiPM? Faster scintillation? Higher refractive index fiber?
    Which factor dominated the GlueX pulse width?
Conclusion