## Slide 1
Machine Learning applications for luminosity maximization
Xiaofeng Gu
Collaborators:
MSU: Yue Hao, Will Fung
LBNL: Ji Qiang, Sherry Li, Yi-Kai Kan
BNL: Xiaofeng Gu, Robert-Demolaize, Takeshi Kanesue
MAC Review

## Slide 2
Outline:
Motivation
GPTune and APEX
GPTune and EBIS
Summary

## Slide 3
sPHENIX luminosity Optimization
Global Parameters:
Orbit (Dipole)
Tune (Quadrupole),
Chromaticity (Sextuple)
Octupole
Local (IR8) Parameters:
Beta*
S* (more sensitive than head on)
Transverse offset
Other Parameters:
RF Voltage
Collimator Position
Many variables;
Maximize the useful signal within VTX while minimize the unwanted signal outside of VTX
Machine learning could be a good tool for a fast, multi-objects tunning.
GPTune will be used.
sPHENIX:
max. VTX (+/-10 cm)
min. unwanted signal
Crossing angle (2mrad)
Maximize
minimize

## Slide 4
Outline:
Motivation
GPTune and APEX
GPTune and EBIS
Summary

## Slide 5
Bayesian optimization at LBNL GPTune
Several features of GPTune (BLNL) are very useful, including:
relies on dynamic process management for running applications with varying core counts and GPUs
can incorporate coarse performance models to improve the surrogate model
allows multi-objective tuning such as tuning a hybrid of computation, memory and communication
allows multi-fidelity tuning to better utilize the limited resource budget
supports checkpoints and reuse of historical performance database.
https://github.com/mkturkcan/GPTune
https://nimrodteam.org/meetings/team_mtg_5_21/nimrod_meeting_YangLiu.pdf

## Slide 6
GPTune Optimization with the Analytical Luminosity
Unwanted
Maximize
minimize
Vertex signal (±10cm)
Unwanted Lumi

## Slide 7
GPTune Optimization with Simulated Luminosity
The optimization of the lattice setting with respect to the luminosity is performed for the head-on collision of two Au-Au beams in the Relativistic Heavy Ion Collider (RHIC). The parameters of the lattice setting with only two variables and .
The value of the objective function converges when more optimization steps are executed. This implies the value of the objective function is minimized and hence the total luminosity is maximized.

## Slide 8
Optimization method
VTX
signal
Machine
parameters
S*
GPTune
Luminosity Measurement
1. S* and beta* changing scripts: Tested (next slide)
change the target s*, beta* within ‘deltas.dat’ file;
run ‘madx job.madx_Au16-e0::store’ command, will get ‘IP8knob.dat’ file;
run ‘CreateSend.IP8’ command, will get ‘SendTrim.IP8’ file;
run ‘SendTrim.IP8’ command.
3. GPTune: Tested (next several slides)
Installed and tested
Did some optimizations EBIS and got some good results.
2. Vertex Signal: contacted with sPHINEX people:
Did it with PHENIX before
Send the vertex data several ways.
APEX for Luminosity Optimization

## Slide 9
Script Test at IR12
Successfully test the s* script at store (IR12).
No additional significant beam loss during +/- 0.5 m s* change.
Will explore a large safety range next time at IR12 without separation bump.
Beam Loss During Test
IR12 PS Current
PS Current
s* measurement

## Slide 10
Outline:
Motivation
GPTune and APEX
GPTune and EBIS
Summary

## Slide 11
GPTune Test: EBIS Intensity Optimization
LION
EBIS Injection Line (fc96)
EBIS
EBIS Extraction line (xf14)
RFQ
MEBT
Linac
HEBT
EBIS
RFQ
LINAC
fc96
xf14
LION
1
2
3
5
4
8
7
6
Buncher1
Buncher2
Buncher3
 |  | Injection [xf14] | Extraction [fc96]
1 | IonLens20-40kV |  | 
2 | DeflPlatBias |  | 
3 | 16PoleX |  | 
4 | 16PoleY |  | 
5 | Gridded_Lens |  | 
6 | Horiz_Bend_Defl |  | 
7 | Inter_Vert_Defl |  | 
8 | Inter_Vert_Defl_Lower |  | 
9 | Horiz_Sphere_Bend |  | ×
10 | RFQ_Horiz_Bend | × | 
11 | LEBT_Solenoid | × | 
 | Total Variables | 9 | 10

## Slide 12
GPTune: EBIS Injection Line (9 parameters)
  GPTune: minimize the signal to get a maximum output.
  script was running from 12:33 to 13:36 (~63 min)
  1 pulse / super-cycle [6.6 s]; it takes 2 super-cycles for the powers settle down; 4 super-cycles for measurement.
  fc96 measurement was used for injection optimization
  9 control parameters after 70 iterations
GPTune Signal

## Slide 13
GPTune: EBIS Injection Line (9 parameters)
11.5
~14.0
fc96 Intensity
  ~22% improvement after optimization

## Slide 14
GPTune: EBIS Extraction Line (10 parameters)
  script was running from 10:18 to 11:15 (~57 min)
  2 pulses / super-cycle [6.6 s].
  xf14 measurement was used for extraction optimization.
  10 control parameters after 60 iterations
GPTune Signal

## Slide 15
GPTune: EBIS Extraction Line (10 parameters)
1.4
~2.0
Xf14 Intensity
  ~43% improvement after optimization

## Slide 16
GPTune: EBIS Intensity Gain (11/25/2023)
Intensity detector | Original | Ext. optimized with xf14 | Gain | + Inj. Optimized with FC96 | Total Gain | Total Gain
xf14 (uVs) | 1.48 | 2.23 | 42~50% | 2.53/2.49 |  | 68~71%
fc96 (uVs) | 11.22 | 12.61 | 8.4% | 13.67/13.89 |  | 22-24%
GPTune works with std ±10% (pp ±15% ) noisy signals!
Possible more gain with fc96 instead of xf14 for the extraction line?
1.48±0.13
Inj+Ext.
12.16±1.23
13.67±1.40
Ext.
Original.
2.23±0.17
2.53±0.20
11.22±1.05
13.89±1.76
2.49±0.24
Inj+Ext.
?
fc96 Intensity

## Slide 17
GPTune: EBIS Injection + Extraction (19 parameters)
12/03/2023:
Change 19 parameters simultaneously
Fc96 was used.
Original: 22 [uVs]
80-iterations: 23 [uVs]
90-iterations: 23.56 [uVs] (7%)
1.07×1.22 ~ 1.30 ?
90 iterations
Original
80 iterations
fc96 Intensity

## Slide 18
Outline:
Motivation
GPTune and APEX
GPTune and EBIS
Summary

## Slide 19
Summary
GPTune has been demonstrated as a powerful tool for optimization. It was used for EBIS intensity optimization and got 22~30% intensity improvement at xf14 CT (70% with fc96 CT) , with ±10% std noisy signals and 19 variables. GPTune is planned to be used for other beam lines in RHIC complex.
The luminosity optimization plan has been developed: testing scripts, variable limits and beam loss at IR12 (injection and store), then at IR8 (store).
Scripts for Luminosity optimization have been tested at IR12. No significant beam loss during the test. Maybe more time to explore the variable limits.
The experience of luminosity optimization with a cross angle is very useful for EIC.

## Slide 20
About the last year’s recommendations
Recommendations: Develop a plan and assess the resources needed to carry out the plan. The plan needs to have well-defined and achievable goals.
Partially Done: Scripts for Luminosity optimization are tested at IR12 at injection and store; will do it at IR8 this run.
Recommendations: and include defined measures and actions to protect the machine and the detector.
Done: No significant loss during the test. Will explore the limit range again.
Recommendations: The protection measures need to be agreed upon with sPHENIX management.
Partially Done: Have contacted with them about the vertx signals; will communicate with them for APEX.

## Slide 21
Acknowledgement
R. Guillaume
T. Kanesue
M. Okamura
J. Morris