## Slide 1: High current laser ion source
Dec. 20, 2023
Maashiro Okamura (BNL), Guy Garty (Columbia University)
Funding Opportunity Announcement (FOA), FY23 & FY24

## Slide 2
Project goals
Develop Laser ion source (LIS) and Radio Frequency Quadrupole (RFQ).
Very high current and highly charged state ion beam will be delivered.
Use Direct Plasma Injection Scheme which was invented by us.
Target species are from light to medium mass ions.
    (before challenging heavier species)

## Slide 3
State of the art ion sources for heavy ion beams
Biri, S., Vajda, I.K., Hajdu, P. et al. The Atomki Accelerator Centre. Eur. Phys. J. Plus 136, 247 (2021). https://doi.org/10.1140/epjp/s13360-021-01219-z
Electron Cyclotron Resonance Ion Source (ECIRS)
Good for CW beam ( cyclotron or LINAC)
High average current
Electron Beam Ion Source (EBIS)
Pulsed beam for synchrotron
High flexibility

## Slide 4
laser ion source (LIS)
~ns
Laser
Target
~ a few ns
~20 deg.
~ms
z
x
z
x
z
Plasma formed
Plasma expands
Extraction field
Ion beam
Drift length
x
High density plasma created from a solid.
Fast switching target materials.
Low temperature after adiabatic expansion.
Uniform density of beams.
Scheme of laser ion source

## Slide 5
Plasma
Ion beam
Thermal distribution
Hot plasma becomes very cold at the extraction
Less emittance growth
Pin point ionization
-uniform plasma density-
Other type ion sources:
Projection of plasma becomes beam

## Slide 6
Magnetic field at extraction point increases emittance.
Solenoid axis
Ion born at extraction
r
No strong magnetic field in laser ion source

## Slide 7
Why Laser Ion Source is good for next generation accelerators??
LIS has been spoken badly: poor stability
uncontrollable emittance
not great for long time operation
LIS provide very high current beam
No hysteresis effect
High charge state ions using high laser power density

## Slide 8
Why Laser Ion Source is good for next generation accelerators??
LIS has been spoken badly: poor stability
uncontrollable emittance
not great for long time operation
(Previous FOA reviewer’s comment)
LIS provide very high current beam
No hysteresis effect
High charge state ions using high laser power density
These are false statements

## Slide 9
Low current LIS is providing beams to
NASA Space Radiation Lab
Relativistic Heavy Ion Collider
 | NSRL | RHIC
For what? | Simulate galactic cosmic rays | Create quark gluon plasma
species | All kinds of cosmic rays | Au
energy | Fe ~1GeV/n | 100GeV/n
Ion source needs to serve two major users simultaneously

## Slide 10
EBIS
4rod RFQ
IH DTL
Laser ion source
(LION)
Since 2014, we have provided various ion beams without major maintenances.
Never opened the beam extractor assembly.
No need to change optical window or lens for laser beam.
Very good beam current reproducibility.

## Slide 11
Expanding plasma
Laser light
What is Direct Plasma Injection Scheme (DPIS)?
Since the plasma start from solid state ( not gas ),
the current density can be very high.

## Slide 12
+
+
RFQ
+
DPIS source
Traditional injection scheme is not good for very high current beam
+
-
N
S
+
-
+
-
+
+
+
+
Confine field
S
N
Electrode
Microwave
+
+
+
Solenoid
Solenoid
We can provide ultra high current, but,,
It’s not so easy to put it into an RFQ!!

## Slide 13
+
+
RFQ
+
+
+
+
-
+
-
+
-
+
-
-
+
-
+
+
-
+
-
+
-
-
-
+
-
+
+
Laser
+
+
-
-
+
-
+
-
+
-
+
+
-
-
+
-
+
-
-
-
+
-
-
+
-
+
+
-
-
+
-
-
+
-
+
+
-
-
+
-
+
+
+
+
-
+
+
-
-
+
-
+
+
+
Solid target
+
Dense expanding plasma from solid targets.
Retaining high brightness, heavy ions can be delivered to RFQ.
Since ions in plasma state, space charge effect can be neglected.
No focusing lenses.
No high voltage cage, no isolating transformer.
Direct Plasma Injection Scheme (DPIS)
Plasma guide
Performance of DPIS was verified by some limited species.
We explore possibility to accelerate heavy ions with DPIS.
This work will give a benchmark for future accelerator project.

## Slide 14
Project Status (control milestones)
FY2023-Q1
1 Subcontract with Columbia University
Dec. 31, 2022 Dec. 22
2 Open call for a postdoc position
Dec. 31, 2022 Oct. 4 Madhawa joined Sep. 1 2023
FY2023-Q2
1 The first beam through the RFQ
Feb. 28, 2023 Feb. 10 (11B5)
FY2023-Q3
1 The second species acceleration
Jun. 30, 2023 Jun. 30 (12C6)
2 Design of new laser irradiation box
Jun. 30, 2023 May 20
FY2023-Q4
1 Design of RFQ electrodes
Sep. 30, 2023 Sep. 30
3 Presentation at international conference
Sep. 30, 2023 Sep. 30, 5 presentations at ICIS2023
FY2024-Q1
1 Procurement of new electrodes type 1
Dec. 31, 2023 In progress
2 The third species acceleration
Dec. 31, 2023 Sep. 20 (26Mg10)

## Slide 15
We have demonstrated that 1.2x1011 of C4+ can be provided by a single laser shot.
Carbon beam, before FOA funded

## Slide 16
7Li3+ beam, before FOA funded
(parameters from target to FC were optimized for 7Li3+)
CT peak : 43 mA, 95 nC
FC peak : 35 mA, 74 nC
FWHM : 2.0 us
Laser
  Thales
  QS220 us,
  1.6 J at laser exit (~0.8 J at target)
Solenoid : 15 A (790 G)
Extraction voltage : 52 kV
RF power : ~ 100 kW
Q1 : 8A
Q2 : 13.2 A
Q3 : 6.8 A
Dipole : 110 A (2.7 kG)
Ring bias : -400 V
Typical beam currents in other facilities are less than 100 mA

## Slide 17
Contamination ~ 2 %
Analyzed beam
Collaboration with Nagaoka University of Technology, RIKEN and Nuclear Physics Institute of Czech
Now expanded to ANSTO, Wollongong University, Technische Universität Darmstadt and Tokyo Medical Dental University.

## Slide 18
Improvement of the accelerator system and R&Ds

## Slide 19
Test of new beam extraction structure

## Slide 20
11B5+ beam was accelerated. Accelerated particle number reached 7.43E9 ions.
Typically, conventional ion source provides less than 10 mA.
Jyväskylä ECR recorded 52 mA.

## Slide 21
To prevent magnetron discharge in the
solenoid, the space was filled by Teflon.
12C6 beam with the new ion source structure.
1.58E10 ions (BNL EBIS: 2.5E9)
12.7 mA peak current
So far, we tested Li, B, C and Mg.

## Slide 22
New design of RFQ electrode (type 1)
Design criteria
Max m/q = 7/3 (assuming 7Li3+)
Target output peak current > 100 emA
Extraction voltage ~50 kV
100 MHz
Transmission ~ 75% inter-vane voltage of 105 kV
Kilpatrick factor <2
2 m long
Output energy 280 keV/n
Collaboration with GSI, Tokyo Tech, Nagaoka University of Technology

## Slide 23: BNL test RFQ for DPIS

## Slide 27
Variable aperture design
r0 [cm]
Larger aperture around injection to keep beam radius large until finishing bunch formation.
Property as a RF resonator need to be verified.

## Slide 28
~2m
Injection
Extraction
Shape of RFQ vanes

## Slide 29
Simulation: Pk-pk = 36.4 kV
Design: A0=0.36, V=105kV -> 37.8 kV
Voltage on axis [V]
10 kV
20 kV
Distance from wall [mm]
3D modeling is almost done. Ready for RF simulation

## Slide 30
Consideration of capacitance variation
Injection
Extraction
As r0 is reduced from entrance to exit, capacitance of electrodes also decreases
This may result in variation of resonant frequency and electrode voltage

## Slide 31
Investigation of resonant frequency variation with simple model
Short model with periodic boundary condition
Entrance
Exit
Variation
Vane shape needs to be designed to have small variation of capacitance and voltage
The final RF property is being simulated by CST.

## Slide 32
Simulation strategy at the injection region
Anode nozzle
Parmteq design
Optimized design
Plasma sheath: IGUN
3D field: OPERA
Tracking: GPT
The first set of the vanes are being procured.

## Slide 33
red 6Li1
green 6Li2
blue 6Li3
magenta 7Li1
cyan 7Li2
black 7Li3
51%
59%
82%
100%
Particle removal start
at Z=77mm
OPERA
Formula
GPT + OPERA/Formula
Simulation condition
10 RF periods
L = 25 mm, dt = 100 ns, I_peak = 1 A - 1.3 A, 4.2 keV initial kinetic energy
Output current
7Li3 : 350 mA
Others : almost no ions accelerated
A simulation paper for current limit is almost ready to submit.

## Slide 34
Mg acceleration test
Plasma Chamber
RFQ accelerator and beam line
Dipole magnet and end of beamline
Solid targets
800 mJ 1064 nm 6 ns

## Slide 35
Faraday Cup Signal
Current Transformer Signal
RFQ cavity signal

## Slide 36
FC Max Voltage vs RFQ Power
FC Max Voltage vs Lens Position
These data were taken without biasing Faraday cup.

## Slide 37
FC Max Voltage vs Extraction Voltage
FC Max Voltage vs Bias Voltage

## Slide 38
Good working region at a low field

## Slide 39
Parameters FC | Analysis | Measured from Oscilloscope
Area under the curve | 785 nVs | 689.9 nVs
Ch2 Max Voltage | 1.153 V | 1.137 V
Total charge | 1.57e-08 C | 
No of particles | 9.82e+09 | 
Beam current at faraday cup | 23.07 mA | 
Mg10+ max beam current (Tentative results)

## Slide 40
Parameters CT | Value
Vmax | 0.039 V
Beam current | 31.39 mA
Area under curve | 40 nVs

## Slide 41
Parameters FC | Analysis | Measured from Oscilloscope
Area under the curve | 238 .7 nVs | 133.6 nVs
Faraday Cup Max Voltage | 0.61 V | 0.609 V
Total charge | 4.77e-09 C | 
No of particles | 2.49e+09 | 
Beam current ar faraday cup | 12.34 mA | 
Mg12+ max beam current

## Slide 42
Parameters CT | Value
Vmax | 0.022 V
Beam current | 17.65 mA

## Slide 43
Scintillator image of Mg10+ beam
Mg10+ using Image J software
Slit width ~25 mm

## Slide 44
Isotopes separation
Isotope | Abundance
24Mg | 79%
25Mg | 10%
26Mg | 11%
m for Mg Isotopes | q | m/q | Dipole current based on Mg10+
24 | 12 | 2 | 102.5
25 | 12 | 2.083333 | 106.7708
26 | 12 | 2.166667 | 111.0417
24 | 11 | 2.181818 | 
25 | 11 | 2.272727 | 116.4773
26 | 11 | 2.363636 | 121.1364
24 | 10 | 2.4 | 123
25 | 10 | 2.5 | 128.125
26 | 10 | 2.6 | 133.25
24 | 9 | 2.666667 | 136.6667
25 | 9 | 2.777778 | 142.3611
26 | 9 | 2.888889 | 148.0556
24 | 8 | 3 | 153.75
25 | 8 | 3.125 | 160.1563
26 | 8 | 3.25 | 166.5625
24 | 7 | 3.428571 | 175.7143
25 | 7 | 3.571429 | 183.0357
26 | 7 | 3.714286 | 190.3571
m | q | m/q | Dipole Current | Ion
16 | 7 | 2.285714 |  | 16O7+
14 | 6 | 2.333333 |  | 14N6+
26 | 11 | 2.363636 | 121.1364 | 26Mg11+
24 | 10 | 2.4 | 123 | 24Mg10+
12 | 5 | 2.4 |  | 12C5+
Scan from 117A -129 A dipole current range to find isotopes and contaminants that could be influence to Mg10+ beam current
Data analysis of Mg beam is in progress

## Slide 45
Charge State | FC Beam Current (mA) | CT Beam Current (mA)
Mg12+ | 0.51 | 31.38
Mg11+ | 2.58 | 31.85
Mg10+ | 14.51 | 31.27
Mg9+ | 4.85 | 30.31
Mg8+ | 0.14 | 32.37
Mg7+ | 0.01 | 30.96
Charge state distribution optimized for Mg10+

## Slide 46
Major deliverables up to now
Test RFQ and beam analyzing line were improved and commissioned.
New beam extraction system was introduced.
Plasma guide solenoid and ion source chamber were modified.
A low solenoid field region for good working condition was discovered.
High current heavy ion RFQ was designed.
Four species were accelerated. (Mg10+ more than 20 mA)
Peak currents of 11B5+, 26Mg10+ and particle number of 12C6+ are world records.
7. Fully striped Mg was detected. (Mg12+ more than 10 mA)

## Slide 47
FY2024-Q2
1 Installation of electrodes type 1
Mar. 30, 2024
2 The fourth species acceleration (plan to accelerate Oxygen)
Mar. 30, 2024
FY2024-Q3
1 Procurement of new electrodes type 2 (This is for heavier species)
Jun. 30, 2024
FY2024-Q4
1 Installation of electrodes type 2
Aug. 30, 2024
2 The fifth species acceleration (Ti, Fe,,,)
Sep. 30, 2024
3 Submit a journal paper
Sep. 30, 2024
Schedule
We would like to start a new project for
high current Pb, Au and U acceleration with DPIS.

## Slide 48: Thank you for your attention