## Slide 1: Routing & Services
ePIC Collaboration Meeting
July 25th, 2024
Roland Wimmer (BNL)
Contributions from everyone

## Slide 2: Outline
Recent updates
  Updates needed from subgroups
Current available spaces
RDOs
Moving forward

## Slide 3: Recent Updates
Working on converting the volume services model to an actual services model
Only Inner MPGD Barrel and Disks so far

## Slide 4: Recent Updates

## Slide 5: Modeling Updates
Certain groups are starting to give models that have various ports or cable leads to indicate where the services will be coming out of their detectors and boards

## Slide 6: Updates

## Slide 7: Updates

## Slide 8: Available Space
Example shown below of the available space estimates
  The services from each detector are broken down into 2 sides, Lepton and Hadron
  Find the total cross-sectional area for each service for each detector
  Add 50% to that number because the services wont stack nicely
  Add an additional 50% for miscellaneous spacing needs (cable trays, raceways, bend radii, etc.)
  Total it all up

## Slide 9: Available space
Several locations of high concern

## Slide 10: Available space
94%
95%
98%

## Slide 11: Update Me!
ePIC.Interface Control Document for Services.052023.xlsx
Please go through and update the values for your detectors
  Quantities / Diameters / Cooling & Gas needs / Power estimates / etc.
  Adding your level of confidence in these numbers to the descriptions would be very helpful
As we get further along accommodations for any necessary changes become harder to make
Space is a commodity and were already running out!
If you don’t have access request it

## Slide 12: Channels & RDOs
Below is the summary of channel counts from the EE group
Detector​ Group​ | Channels​ |  |  |  |  | RDO​
 | MAPS​ | AC-LGAD​ | SiPM/PMT​ | MPGD​ | HRPPD/​ MCP-PMT​ | 
Tracking (MAPS)​ | 16B​ | ​ | ​ | ​ | ​ | 183​
Tracking (MPGD)​ | ​ | ​ | ​ | 164k​ | ​ | 160​
Calorimeters​ | 500M​ | ​ | 100k​ | ​ | ​ | 510​
Far Forward​ | ​ | 1.5M​ | 10k(+201k*)​ | ​ | ​ | 80(+218)​
Far Backward​ | 66M​ | 128k​ | 4k​ | ​ | ​ | 60​
PID (TOF)​ | ​ | 6.1M​ | ​ | ​ | ​ | 500​
PID Cherenkov​ | ​ | ​ | 318k​ | ​ | 143k​ | 1283​
TOTAL​ | 16.6B​ | 7.7M​ | 432k(+201k)​ | 164k​ | 143k​ | 2816(+218)​

## Slide 13: RDO Placements
Option 1 - RDOs are placed on the outside of the barrel for both the lepton and hadron sides.
  Hadron ~7.2m
  Lepton ~7.5m
Option 2 - RDOs are placed on the outside of the barrel EMCAL for both the lepton and hadron sides.
  Hadron ~2.7m
  Lepton ~4.6m
Option 3 - RDOs are placed on the outside of the barrel EMCAL for hadron side and inside the DIRC on the Lepton side.
  Hadron ~2.7m
  Lepton ~2.8m
RDOs
RDOs
RDOs
RDOs
RDOs
*Distances are from IP*

## Slide 14: RDO Mockup
Approximately 250 RDOs shown on each side
Depending upon cable length restrictions certain detectors’ RDOs may be further away due to space constraints

## Slide 15: Items being looked into
Placements of remaining assorted electronics (RDOs, DC to DC converters, etc.)
Cooling & gas manifolds, panels and locations
Cable support systems inside the detector and how everything will integrate with installation
dRICH being spilt in half will have an impact on how services are routed
Services coming from the Lepton endcap may interfere with services coming from the barrel when the endcaps are slid in the hall
Future updates from subgroups

## Slide 16: Questions?
ePIC.Interface Control Document for Services.052023.xlsx
Please update the ICD!

## Slide 19
RDOs
RDOs
Option 1-
RDOs are placed on the outside of the barrel for both the lepton and hadron sides.
Hadron would be 6.5m +10% for contingency, so ~7.2m
Lepton would be 6.8m +10% for contingency, so ~7.5m
For all the numbers I list the distances are from the Inner MPGDs since I believe they are the worst case. If we need RDOs for the inner Silicon we must add to 0.5m the numbers.
~7.5m Silicon ~7m MPGD
~7m Silicon ~6.5m MPGD

## Slide 20
RDOs
RDOs
Option 2-
RDOs are placed on the outside of the barrel EMCAL for both the lepton and hadron sides. This option potentially creates issues for the Hadron side as getting access to the RDOs may be difficult. Also routing of the cables in this area will be a nightmare. On the Lepton side we have much more space since we are not limited by the dRICH.
Hadron would be 2.4m +10% for contingency, so ~2.7m
Lepton would be 4.2m +10% for contingency, so ~4.6m

## Slide 21
RDOs
RDOs
Option 3-
RDOs are placed on the outside of the barrel EMCAL for hadron side and inside the DIRC on the Lepton side. This option has the shortest distances, but I don’t think its possible. It has the same issues on the Hadron side but also additional issues on the lepton side. The EEEMCAL and pfRICH will be slid into and out of the detector here, so anytime we need to service them or another detector inside of them we’ll have to disconnect every RDO in this area and remove them. The cabling in this area would also be extremely messy.
Hadron would be 2.4m +10% for contingency, so ~2.7m
Lepton would be 2.5m +10% for contingency, so ~2.8m