## Slide 1: Joint EICUG/ePIC Collaboration Meeting
July 25, 2024
Barrel EMCAL Engineering Update

## Slide 2: BIC Sector, End View:

## Slide 3: BIC Length:

## Slide 4: “Recent” Change Summary:
Needed more space for end-of-sector boxes
  Originally allocated 10cm
  Increased to 15cm to accommodate light guides and connectors
  Distance to dRICH has to be unchanged (hard requirement)
  Reduced active length of the detector from 440cm to 435cm to maintain service gap
Detector was out-of-phase with the DIRC
  We have 48 sectors, DIRC has 12 segments
  We had a single “cap-stone” sector, which made us 3.75 degrees out of alignment with the DIRC
  Rotated barrel 3.75 degrees to put edge of sector on vertical plane which restores alignment
  Unclear how/if this will impact installation

## Slide 5: BIC Placement in Global Model:
Interference
w/DIRC
East (+Z)
West (-Z)
Facing North
6.75cm gap to
DRICH

## Slide 6: DIRC Interference:
4.74cm

## Slide 7: Dirc Interference, Astropix Access:
New orientation in phase w/DIRC
Support Tube for
Inner Detectors
DIRC Lenses block inner Astropix

## Slide 8: DRICH End:
6.75cm gap to DRICH
ESB’s extend 1.25cm beyond DIRC Bar

## Slide 9: ASTROPIX Tray

## Slide 10: ASTROPIX Installation

## Slide 11: Barrel Construction/Installation
Unpack sectors and attach light guides
Assemble sectors (with light guides) next to solenoid (on dRICH side)
Slide assembled barrel into position and connect to support rings
Insert AstroPix into drawers,
  Trays are half-length, each sector has 2 trays back-to-back
  Prefer installation (and servicing) from both ends
Assemble end-of-sector boxes at both ends of each sector

## Slide 12: Next Steps:
Finalize engineering interface documents
Resolve interference with DIRC and overlap with lenses?
Incorporate interface with support rings into sector design
Design AstroPix installation/maintenance fixtures
Clarify support scheme for inner detectors and evaluate impact on AstroPix installation/maintenance
Our Requirements:
Ability to access and replace end-of-sector boxes on each end of the detector
Access to AstroPix staves, preferably from both sides (this impacts tray design and installation tooling)