## Slide 1: Streaming DAQ Development at JLab and Ideas for EIC DAQ Prototyping
SRO+DAQ Workfest
ePIC Collaboration Meeting - Lehigh University
July 25th 2024
David Abbott
FEDAQ Group
Jefferson Lab

## Slide 2: Data Acquisition at Jefferson Lab
At JLab we have 4 Experimental Halls, all running with different detectors - and physics focus.
  Of course all are having increased demands for the DAQ.
The Fast Electronics/DAQ (FEDAQ) support group provides custom electronics, as well as firmware and software libraries and tools for all experiments.
Our current goals are to support both the traditional Triggered model along with the Streaming Model within one integrated DAQ framework.
  Leverage existing hardware to implement Streaming
  Add support for new electronics
  Try to keep it as seamless and user friendly as possible
A
B
C
D

## Slide 3: CODA – CEBAF Online Data Acquisition
What is CODA (also see coda.jlab.org)
  Software toolkit for implementing data acquisition systems.
  Hardware/Electronics
    Custom electronics , FPGAs, ASICs, TDCs and ADCs.
    Support for commercial hardware.
  Software includes :
    Interfaces with electronics (libraries/drivers).
    Readout Front End and Data Formating (ROC)
    Inter-process communication - Control and Data (cMsg)
    Manage data streams (DC, PEB, SEB, PAG, SAG)
    Give users access to data for analysis and monitoring (ET System)
    Write data to files (EVIO, ER)
    Manage and control the data acquisition system (AFECS)
CODA is modular. Build a single crate DAQ or a full Experimental Hall system

## Slide 4: The CODA Data Acquisition (software) Toolkit
CPU
TI
EMU
(Event Builder)
EMU
(Event Recorder)
File
File
ET
User
AFECS
ROC
ROC
Platform
GUI
COOL
Database
ROC – Readout Controller
EMU – Event Management Unit
ET – Event Transport (Shared memory)
AFECS – Agent Framework Experiment
Control System (JAVA)
The ROC is software responsible for collecting data from front-end hardware and sending it to the next stage.
Trigger/Clock
CPU
VTP
TI
SD
PCIe TI
ROC
VME
VXS

## Slide 5: JLAB Clock and Trigger Distribution System
For large DAQ systems with many front-ends (ROCs)
The TI board can be used as a TS for small (up to 9) front-ends

## Slide 6: VXS Standard (VITA 41)
JLab standardized on this technology for the 12GeV Upgrade
    - Originally used for the L1 trigger data path
Dual Star – switched serial backplane (along with original VME)
Up to 20Gb (4 lanes) from each Payload to the 2 Switch slots (A, B)
Up to 18 Payload slots are available
Easy distribution of Trigger, Sync and low jitter clock to all modules in the crate.
A B
VXS Trigger Processor (VTP)
Relieve the ROC of all of the “Readout” tasks and implement them in the FPGAs.
Triggered or Streaming readout from All payload modules in parallel
    This requires the payload modules to have some intelligence/programmability and serial link capability (e.g. FPGA-based).
    The Software ROC now is primarily responsible only for Configure, Control and Monitoring the VTP-Based DAQ.

## Slide 7: JLAB – VTP Board
Linux OS on the Zync-7030 SoC
(2-core ARM 7L , 1GB DDR3)
10/40Gbps Ethernet option
(runs the CODA ROC)
Xilinx Virtex 7 FPGA
Serial Lanes from both the VXS backplane and the Front panel
4GB DDR3 RAM
16 total lanes
for external
serial links
16 Payload
Ports
64 total
serial lanes
Four
10Gbps
Ethernet
V7
Z7
FADC
FADC
FADC
FADC
FADC
FADC
FADC
FADC

## Slide 8: Flexible Platform
In addition to supporting all the older VME electronics, we have developed a number of custom boards that take advantage of the VXS backplane.
Streaming Model tests grew out of the original purpose of VXS for the trigger data path.
250 MHz FADC
16 Channels
12 bits
JLab workhorse in all current experiments
Subsystem Processor (SSP)
FPGA board
8 QSFP Inputs (32 links)
QSFP->VXS adapter card
Simple direct serial link
access to the VTP for
External custom
Front-end electronics
Supports 4 separate bidirectional links
Drift Chamber Readout Board (DCRB)
96 Channel TDC
boards
Used to readout Hall B/CLAS12 drift chambers

## Slide 9: JLAB FADC – Streaming
TF1
0
16383
ROI
TH
ROI
TH
ROI
TH
ROI
TH
TF2
TF3
TF4
ROI
TH
ROI
TH
ROI
TH
Fine
Time Stamp (4ns)
Chan 1
A 250 MHz FADC generates a 12 bit sample every 4ns. That’s 3 Gb/s for one channel. A 16 channel module is 48 Gb/s. That is over twice the available VXS bandwidth. But we don’t need ALL the samples.
Within the FPGA we keep only the data around a Region of Interest (ROI) from each channel, along with a fine time stamp (4ns ticks) in each time slice window (65µs). Then we do some pulse processing for each hit.
Chan 16
Readout Time Frame
(65µs)
.
.
.
FPGA Pulse Processing (one 32 bit word/hit)
1 hit/32ns (double hit resolution)
- Pedestal subtracted
- Integrated Charge(13bit)
- Timestamp (14bit – 65µs)
- 8Gpbs/Module rate to the VTP

## Slide 10
Globally “Sync” from the JLAB Clock/Trigger distribution system is used to start and stop all the streams at their source (FADC Boards)
Locally, PPs stream hits to a VTP DRAM buffer. The Frame Builders (V7 FPGA) have a frame output “fifo”
A Frame builder will only aggregate hits into a ROC frame if the fifo is not full. Otherwise the frame is dropped.
Built ROC frames at the Zync will always get sent (eventually).
Up to 4 independent network streams can be defined. Each PP maps to a specific output stream.
Limited Zync resources only provide 2 high performance TCP connections (or 4 UDP streams)
PP 1
PP 16
VXS
VTP
BUF 1
BUF 16
4 x Frame
Builder
TCP/UDP
TCP/UDP
UDP
UDP
DRAM
Zync
1
2
3
4
VTP - Frame Builder
FADC Boards
V7
EMU
(Stream
Aggregator)

## Slide 11: Simple Hybrid DAQ System
EMU
(Event Builder)
File
CPU
TI
EMU
(Stream
Aggregator)
VTP
SD
File
FADCs
PC/Server
e-
DISC
Trigger
Two ROCs are defined for the DAQ System
VME_ROC
Runs on the CPU
Reads out Triggered data
VTP_ROC
Configures and manages the stream data
10Gbps
1Gbps
VXS Crate
phototube
scintillator
Lead glass
JLAB 250MHz FADC board has the ability to support simultaneous Triggered and Streaming readout
This system Streamed integrated hits while Triggered data were the full waveforms for the ROI

## Slide 12
VTP Streaming Readout Testing in CLAS/Hall B – with recent DCRB support
Front-end Crates
VXS Backplane
10Gbps per Slot
Fibers: 4x 10Gbps Ethernet Links from each VTP
DCRB
FADC250
DC Hits
(32ns Timeslices)
Drift Chamber
FTCAL
FTHODO
ECAL
PCAL
FTOF CTOF
CND
HTCC
FADC Pulses
(4ns Timestamp & integrated Charge)
VTP
Ethernet Routers
Computing & Storage
New Firmware
Existing Firmware
FADC250 streaming support (pulse charge & time) already supported
DCRB streaming support added for CLAS12 beam tests (2 sectors -> 6 crates)
First streaming test in CLAS12 with calorimeters, Cherenkov, and Drift Chambers for large triggerless DAQ

## Slide 13: EVIO Primitive Data Structures
EVIO data formats are based on 32 bit words

## Slide 14: Example Data Structure – Triggered Readout
Note that Banks can contain Banks or Segments which can further encapsulate information for the User.
Lengths in the headers facilitate finding the start of the next bank or segment.
For purposes of transporting or archiving these bank structures we wrap them up within another header called an EVIO Block header (8 Words).

## Slide 15: Example Data Structures – Streaming Readout
Streaming Data Structure is analogous to existing Triggered Data
Aggregation just appends Streams and updates a new SIB

## Slide 16: DAQ/Computing Activity in 2024
Finishing timing studies
  Define clock/command distribution protocol
  Jitter and phase drift – (measured ~3ps at RDO)
  Refine requirements for the GTU
  (scale of the distribution, interface to DAM)
Finalize requirements for FELIX development to define EIC DAM Board.
  Collaborating with ATLAS OMEGA group at BNL
  Currently using FLX-182 engineering article in tests
Refine expected RDO counts and flavors for all detector sub-systems and
  Required interfaces with FEB electronics (ASICS, VTRX+, FADC).
  Better estimates of backgrounds and data volumes.
All for development of the TDR and the CD2 baseline.
FLX 182 board
Used for timing studies and
DAM firmware/software development
XEM8320,
Artix Ultrascale+
(RDO)

## Slide 17: FELIX Updates – FLX 155
FELIX hardware for future ATLAS experiments at HL-LHC is being developed at BNL (Omega Group)
  Long term support is insured. Development timelines are compatible with EIC.
Latest (FLX-155) design review completed by ATLAS and AMD
  This revision should be the final engineering article
  It has been sent out for fabrication. PCBs available this month.
First 4 populated boards expected by late August/early September
  We expect to receive at least one board by the end of this year
Note: 4 fiber LTI Link supports receiving either reconstructed or a direct clock
Versal FPGA is a SoC (Dual Core ARM). The FELIX board can operate either standalone or in a Server

## Slide 18: Supporting FELIX Hardware at JLAB
RDO
RDO
RDO
RDO
Versal Ultrascale+ FPGA (SoC, ROC)
PCIe
DRAM
DAQ Server
CODA
EMU
Control/Clock
Data
Detector
FELIX: FLX 182 (we have 2 boards)
24
24
JLAB
Clock/Trig
FPGA: Xilinx Versal Prime XCVM1802
PCIe Gen4 x16
24 Firefly links
Implement a protocol based
on the proposed EIC Link
Questions:
What can we use for RDOs?
Is there a potential “cheap” commercial option for the DAM that could be used for prototyping?

## Slide 19: Pre-Prototyping EIC DAQ at JLAB
ALINX VD100 ($800)
Versal SoM (dual core ARM)
2x SFP+ (12.5Gps)
2x 1Gb Ethernet
4GB DRAM
156MHz on board clock
VMM ASICs + Artix Ultrascale+
EIC PP-RDO

## Slide 20: What’s Next?
The VXS platform works for JLAB for the near term, but how do these solutions evolve for future experiments, and in particular the Streaming model.
Introduce the DAM/RDO architecture to our DAQ development with FELIX and other viable commercial options.
Implement a DAM/RDO clock distribution and communication protocol that is consistent with the EIC proposal.
This will initially be a useful testbed for the overall performance of the clock reconstruction and phase synchronization.
RDO
RDO
RDO
RDO
FPGA
ROC
Server
Server
SoC
ethernet
PCIe

## Slide 21: Backup Slides

## Slide 22: FADCs - Triggered vs Streaming
External
Trigger
(timestamp)
PL (0-8µs)
PTW (0-2µs)
ROI
TH
0
511 (Sample #)
PL: Programmed Lookback
PTW: Time window
Data we get on a trigger:
- FADC waveform values for the ROI
- Threshold Sample # (hit time)
- Trigger absolute time stamp
Triggered Mode
Streaming Mode
Time Slice
(Frame #
& timestamp)
ROI
TH
0
N ( Max Sample #)
1 Frame = N Clocks (up to 16bits, currently 65536 ns)
Data we get for a Frame:
- Pedestal subtracted sums over an ROI for every hit over threshold
- Threshold sample # fine time stamp for each hit
- Frame # and absolute time stamp for the frame
ROI
TH
ROI
TH
ROI
TH
ROI
TH
Fine time stamp (4 ns)
Trigger Bank
Data Banks
Length (words)
Tag
DT
M
ROC Data Format
Stream Info Bank
Data Banks
Length (words)
Tag
DT
SS
ROC Data Format
Trigger #
timestamp
Frame #
timestamp

## Slide 23: Readout Controller (ROC)
VME
OS: Linux
ARCH: Intel, Arm
ROC
Output Thread
Trigger Thread
Process Thread
to EMU, ET
stdout or File
DMA
Lib
VME
Lib
DMA
Pool
Control
cMsg
USB
PCI
User
Libs
User
User
FIFO
User
FIFO
ROL2
ROL1
Buffer
Pool
FIFO
Interactive shell (Tcl)
$ <cmd>
Buffer
Pool
DL Lib
Remex
Buffer Pool
Modules
VXS
to Trigger Processor
The CODA ROC is a software application that has multiple options for the User to implement custom code or hardware for their specific needs.
External Trigger/Clock

## Slide 24: Example – The GlueX trigger
Each ADC sends signals to a crate level trigger processor over VXS serial bus.
  And stores the signal locally in memory
Each CRATE Trigger processor sends signal to a global trigger for all crates over fiber optic cable.
Global trigger tells trigger supervisor (TS) which events are good.
The TS tells Trigger Interface (TI) board in each crate.
The TI signals the CPU to read out crate and provides information about which trigger the data belongs to.
VXS
Fiber
Cable
VXS
FIBER
Look back some # clocks
Copy data from
all ADCs in the crate
To the CPU
VXS
8µs
Trigger

## Slide 25: HALL B RICH Detector - Readout
MAPMT Sensors (25024 Channels)
138 Readout Boards (Tiles)
(Blue fiber cables)
5 SSP FPGA boards aggregate the fibers
In a single VXS crate

## Slide 26: New Detectors - New Electronics - ASIC Front-End Examples
FPGA
GEM Detector
SAMPA ASICs
VMM3 ASICs
64 Channel
10bit/6bit ADC
GEM readout
FPGA
MAROC3 ASICs
64 channel
Fast ”trigger” bits
MAPMT/SiPM readout
Optional 8/10/12bit ADC
FPGA Daughter card
with 1Gb Ethernet port
GBT ASICs
This FEE card was originally designed for the ALICE TPC
(High radiation environment)
SAMPA ASICs
32 channel
10 bit (10Mhz) ADC
Optional DSP
sPHENIX @BNL

## Slide 27: Beam Tests
Time Slice Frame containing a Trigger
FADC Channel
Time
Calorimeter spectra – Streaming Data
(Electron beam centered on the central crystal)
Can look for “triggers” in software