## Slide 1: Metadata/SC data handling in STAR
Jeff Landgraf

## Slide 2: Metadata / SC data handling
The talks in this session (aside from Lee’s talk) are meant to address the question of communicating Slow Controls (and other metadata) to the echelon 1.
  Dmitry Arkhipkin about STAR’s metadata using relational DBs (mysql) and object DBs (Mongo).
  Dave Abbott regarding GlueX
  Jin Huang regarding sPHENIX
Here, I on additional sources / sinks of metadata within STAR outside of the DBs – my prior is that ePIC will have similar metadata paths.
RDO/DAQ
IOCs
DAQ Files
SC DBs
EPICS
RDO/DAQ
EIC
EIC DBs

## Slide 3: Run Control
Slow Controls and Run Control have no formal interface in STAR:
  Slow Controls turn detectors on, both low voltages and high voltages. They set detector power modes (off, STANDBY, APEX, PEDESTAL, RUNNING)
  Run Control sets up parameters that go into the detector electronics.
    Directly
    By setting detailed configuration files
Communication to realtime processing nodes via XML configuration file
XML file contains both enabled components AND configuration of those components
XML file stored to MONGO database
Schema evolution facilitated by
  Java class hierarchy automatically generates configuration file editors
  Star uses tree of DSM/QT boards with VHDL defined capabilities that are different for different running modes
    “TIER1 file”
      Contains each trigger components VHDL code name
      Contains dictionary of output bits
      Contains dictionary of setable registers
      TIER1 file selection, defines dictionary for trigger definition and register settings
  Flexible document based orientation of MONGO database
RC
XML
Mongo
DB

## Slide 4: CDEV
CDEV is the RHIC controls data storage system
To CDEV
  RICH scalers
    16 parameters representing simple trigger counter rates passed to CDEV
  Trigger rates
    4 configurable rates from physics (scaler rates / or taken rates) written to cdev from Trigger/DAQ
  Output from High Level Trigger (vertex x, y, z) for each event analyzed by HLT
From CDEV to STAR DB to run control
  STAR magnetic field
  Selected RICH scaler counter to represent base event rate
From CDEV to EVBs to DAQ files
  1 second update but stored in each event
  Magnetic field
  16 RICH scaler values

## Slide 5: Pedestal, Gains, Bad Channels
TPC (and select detectors) pedestal values:
  Calculated at end of pedestal runs by DAQ (~1 pedestal run per day)
  Stored in data file as pedrms banks in event “token=0”
  Cached locally and loaded automatically via RDO protocol to ASICS by DAQ at start of each run
BCAL(and select detectors) pedestal values:
  Calculated each run by L2 trigger (running inside event builders), but not updated
  Files cached and on web pages.
  Updated by hand (via setting link to produced file) periodically by BEMC expert
Channel by Channel gain calibration, T0 calibration, and bad channel list for TPC
  Produced automatically via pulser runs every few months
  Uploaded to ASICs via RDO protocol at start of each run
  Pushed to STARDBs by hand

## Slide 6: Questions / Discussion