## Slide 1
MPGD - ECT
Annalisa D’Angelo
University of Rome Tor Vergata & INFN Rome Tor Vergata Rome – Italy

## Slide 2: μ-RWELL Position Resolution
2
Charge Centroid reconstruction method
The track position is determined as a weighted average of fired strips
GOOD FOR ORTHOGONAL TRACKS
FOR INCLINED TRACKS &/or HIGH B FIELD
the Charge Centroid method gives a very broad spatial distribution on the anode-strip plane.
The spatial resolution is strongly dependent on the impinging angle of the track A non-uniform resolution in the solid angle covered by the apparatus Large systematical errors.
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo
Notes: .Applying a suitable voltage between the copper layer and the DLC, the well acts as a multiplication channel for the ionization produced inthe drift gas gap.
The streamer created inside the amplification volume , inducing a large current flowing into the resistive leyer, generate a localized drop of the amplifying voltage with an effective quenching of the moltiplication process in the gas.=> this process strongly suppress the discharge amplitude allows to operate at large gains with a single amplification stage.
This time 𝜏 strongly affects the rate capability of the detector because of a local charging-up. In case of discharge this effect lowers the amplification field then stopping its propagation but at the same time switching off that part of the detector. The resistivity of the DLC is then a crucial point: a large resistivity makes the detector safer but increases the earlier mentioned 𝜏 then worsening the rate capability of the detector; a low resistivity plays an exactly complementary role: larger rate capability but lower discharge quenching power.

## Slide 3
      The μ-RWELL Development for Large Area Detectors : TPC reconstruction
A possible solution :
The electrons created by the ionizing particle drift towards the amplification region
In the μTPC mode from the knowledge of the drift time and the measurement of the arrival time of electrons, the track segment in the gas gap is reconstructed
The fit of the digitized charge signal as a function of the sampling time gives the arrival time of drifting electrons.
By the knowledge of the drift velocity, the 2D trajectory of the ionizing particle in the drift gap is reconstructed.
3
G. Bencivenni et al 2021 JINST 16 P08036
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo
Notes: The idea developed for the ATLAS MicroMegas of the New Small Wheels [10, 11], and also implemented on the BESIII cylindrical GEM [12, 13], is to reconstruct a track segment inside the detector conversion gap rather than a single hit exploiting the analog readout of the signals.
TPC0=> a readout approach that combines measurement of the arrival time of electrons and the amplitude of the signals on the strips
The fired strips represent the projection of the track on the readout and each center is the x coordinate of the corresponding ionization.
These hits are recorded at different times tk , depending on the distance of the ionization electrons from the readout plane. Applying the simple formula
zk = v_drift * (tk-t0) the z position of the k-th cluster can be computed.
The idea developed for the ATLAS MicroMegas of the New Small Wheels [10, 11], and also implemented on the BESIII cylindrical GEM [12, 13], is to reconstruct a track segment inside the detector conversion gap rather than a single hit exploiting the analog readout of the signals.
𝜇TPC0=> a readout approach that combines measurement of the arrival time of electrons and the amplitude of the signals on the strips
The fired strips represent the projection of the track on the readout and each center is the x coordinate of the corresponding ionization.
These hits are recorded at different times tk , depending on the distance of the ionization electrons from the readout plane. Applying the simple formula
zk = v_drift * (tk-t0) the z position of the k-th cluster can be computed.

## Slide 4
      The μ-RWELL Development for Large Area Detectors : TPC reconstruction
The reconstruction algorithm:
4
G. Bencivenni et al 2021 JINST 16 P08036
tk
The algorithm requires knowledge of:
the reference time t0
the strip charge arrival time tk
the charge drift velocity vdrift
It requires a fit for each hit strip
Electron drift velocity of different gasses, as a function of the applied electric field
PDG
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo
Notes: The idea developed for the ATLAS MicroMegas of the New Small Wheels [10, 11], and also implemented on the BESIII cylindrical GEM [12, 13], is to reconstruct a track segment inside the detector conversion gap rather than a single hit exploiting the analog readout of the signals.
TPC0=> a readout approach that combines measurement of the arrival time of electrons and the amplitude of the signals on the strips
The fired strips represent the projection of the track on the readout and each center is the x coordinate of the corresponding ionization.
These hits are recorded at different times tk , depending on the distance of the ionization electrons from the readout plane. Applying the simple formula
zk = v_drift * (tk-t0) the z position of the k-th cluster can be computed.
The idea developed for the ATLAS MicroMegas of the New Small Wheels [10, 11], and also implemented on the BESIII cylindrical GEM [12, 13], is to reconstruct a track segment inside the detector conversion gap rather than a single hit exploiting the analog readout of the signals.
𝜇TPC0=> a readout approach that combines measurement of the arrival time of electrons and the amplitude of the signals on the strips
The fired strips represent the projection of the track on the readout and each center is the x coordinate of the corresponding ionization.
These hits are recorded at different times tk , depending on the distance of the ionization electrons from the readout plane. Applying the simple formula
zk = v_drift * (tk-t0) the z position of the k-th cluster can be computed.

## Slide 5
5
Tests performed on 1D Rwell prototypes
The reference time t0 is provided by
plastic scintillators providing the DAQ trigger
The reconstructed track: z = p0 +p1 x
is used to provide the “measured” x at the middle plane of the detector:
Zc=3 mm
X
G. Bencivenni et al 2021 JINST 16 P08036
1D 400 m pitch
Ar:C02:CF4
40:14:45
Gas mixture
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 6
6
Tests performed on 1D Rwell prototypes
G. Bencivenni et al 2021 JINST 16 P08036
1D 400 m pitch
Ar:C02:CF4
40:14:45
Gas mixture
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 7
7
Tests performed on 1D Rwell prototypes
ePIC Collboration Meeting- July 25 2024 – Annalisa D’Angelo
E=0.5 KV/cm
E=3 KV/cm
Combined results of 1D space resolution from charge centroid (CC) and -TPC algorithms
1D 400 m pitch Ar:C02:CF4 40:14:45 Gas mixture

## Slide 8
8
Future test on 2D GEM+Rwell+ TPC
2D GEM - Rwell Technology
PCB read-out
Rwell
GEM
cathode
3/6 mm gas gap
2/3 mm transfer gap
Two 2D 10cm x10 cm GEM- prototype with 400 pitch à la Compass are being produced
A Test beam will take place at CERN on 13-27 November 2024.
The detector response will be tested as a function of the tracks angle in 2D
New detector holders
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 9
9
2D 10x10 cm2 GEM-Rwell prototype assembly
GEM-Rwell 10x10 cm 2 prototypes assembly
GEM foil
Glue on peek frame
GEM stretching
GEM tension measurement
Frame assembling
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 10
10
2D 46x38 cm2 Large Area Rwell prototype with capacitive Sharing
30 mm drift gas gap
Ar:CO2 70:30
590 V
First tests on large gas gap
With capacitive sharing show good 3D track reconstruction
By Carlo Gustavino
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 11
11
Start time t0
Charge sampling at 50 MHz
Number of sampling larger than the maximum drift time
Precise tk determination in the data stream: rise-time fit not the time of the maximum collected charge
Requirements to the DAQ electronics
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo

## Slide 12
12
-TPC PROs and Cons
The -TPC algorithm requires:
Precise charge timing information
A start timing information
A fit for each strip signal
A fit for each track
Never systematically applied on 2D -Rwell detectors
Never applied to 2D GEM- -Rwell detectors
Very complicated for multiple tracks
Is it compatible with charge sharing?
PROs
The -TPC algorithm provides:
Improved position resolution for Inclined/bent tracks
The timing information is embedded in the detector response
CONs
ePIC Collaboration Meeting July 26 2024 – Annalisa D’Angelo