## Slide 1: Basic mechanics considerations
Apologies if you know all this already, but to remind of a few basic concepts, that I hope will be useful for some
Based on slides I made for the Silicon Detector School

## Slide 2: Purpose of mechanical structures
Tracking will usually require linking measured positions from several modules (can be metres away from each other)
The support should not degrade module-internal measurement accuracy (typically at level of µm)
The relative positioning of these modules is called alignment
  Alignment in modern trackers is found by software (also called track-based alignment - TBA)
  Software alignment is performed with selected track data acquired over an extended alignment period
#1 requirement is stability of the module positions to allow software alignment to work
  This does require identification of the loads that are relevant, and their time scales (will discuss later)
  Typically, stability must be comparable to module precision (~1 µm)
Module placement is secondary
  Everything needs to fit together, clearances (for installation or HV), overlaps for tracking hermeticity and TBA
  All these are typically a very few 100 µm
The support structure should achieve this with minimal material
Additional tasks:
  Support services (cables, fibres, cooling pipes, etc.)
  Sometimes part of the thermal management (conductive heat paths)
  Sometimes part of the grounding & shielding system
Need stiffness, strength is secondary

## Slide 3: Composites design
Carbon fibre design is fundamentally different from machining metal
Design for metal structures involves removal of material (subtractive machining), and then usually connection by bolts
  Metal designs therefore often involve straight and square geometries
  Manufacture requires placement of the piece into a machine for the material removal
    This becomes more difficult and precision harder to achieve the larger the piece is
  Recently, additive metal manufacturing is changing this paradigm
Composites on the other hand comprise often sheets, which are appropriately shaped
  Structural performance is often achieved by shaping, and the design optimizes the shape according to the loads, which typically results in non-square forms
  Composites are anisotropic, so design is significantly more complex
  Shaping of composite structures in principle gives a lot of freedom for geometries
  In particle physics we are often not exploiting these possibilities (even if work with CF) – we tend to design in cylinders or disks
    Apart from being structurally inferior, this also is suboptimal in reducing tracker material
Joints are usually bonded
  Bolted connections are actually difficult and require inserts and local reinforcements
  Because carbon fibre is so structurally powerful, it often is actually the bonds, which limit the structural performance
Structural dimensional precision is best not achieved by machining of precision interfaces, but by gluing parts held in place by precision jigs
The most efficient tracker geometry:
What we have now:
ATLAS ID

## Slide 4: Carbon fibre - properties
Fibres can be classified according to their tensile modulus
  For us only high-end fibres are interesting: High modulus (HM, 400-700 GPa) or Ultra-high modulus (UHM, 700-1000 GPa)
  Widely used fibres in PP are K13C2U (900 GPa) or K13D2U (935 GPa)
  UHM fibre is ideal for high stiffness application, but useless for high strength (thus not common)
  Because of the high stiffness this fibre is brittle, and cannot be woven – only uni-directional
  If more strength is required a woven HM fibre like M55J or similar is useful
Density is mildly correlated with modulus - More important is prepreg fibre area density, which is a feature of manufacturing process (how many fibres per width or area)
A useful feature of carbon fibres is that longitudinal heat conduction is good, and correlated to modulus
  Cross-plane heat conductivity is usually poor (a factor 1000 smaller than along the fibre)
The coefficient of thermal expansion of a uni-directional layer is usually slightly positive across the fibre direction, but negative along the fibre (about -10-6 m/m°C)
  Therefore combinations of layer orientations can be found which have zero CTE in certain directions (those are not necessarily the lay-ups with the highest modulus)
Only defence

## Slide 5: Type of loads
Vibrations (timescale seconds)
  External (seismic and/or from other parts of experiment) or internal (typically flow of coolant)
Thermo-mechanical (seconds to hours)
  Structures and modules contain elements with different CTE, so temperature changes over time will lead to load changes
  This can also be due to changes in power consumption, because of thermal impedance of thermal path from heat source to local heat sink (coolant)
Seismic shocks (days to months)
  Significant perturbations or change of state, usually brief, but with significant times of stability between
  Examples are magnet ramp/quench, power or cooling system stoppage (planned and unplanned)
Long-term effects of static loads (months to years)
  For example creep or relaxation effects
  Humidity effects
  No defined time of change, but over long time scales
In order of increasing time scales (relevant to correlate with duration of stability required)
Relevant within TBA periods
Sets boundaries of TBA periods
Tracked by TBA

## Slide 6: 1D oscillator – Miles’ equation
To understand the response of a periodically excited object we start with a very simple model, a 1-D damped oscillator ()
John W. Miles
with
Integrate over all frequencies
Miles’ equation: a good estimator of the dynamic response of a mechanical system

## Slide 7: Simple beam theory
Support structures are complex 3D-objects: they have a rich resonance structure
A simple picure: Bernoulli beam (essentially a 2D beam, with d << l)
  Characterized by bending stiffness EI, with E the Young’s modulus (material property), and I the (area) moment of inertia (beam geometry)
After separation and boundary conditions
  Resonance frequencies:
  Spatial part:
Combined frequency response
  Weighted with modal participation factors
  which relate to modal mass
with
Even-n modes are not excited because of symmetry (would require rocking excitation)

## Slide 8: Bending stiffness
We have seen with the Bernoulli beam that , and from Miles’ equation , so
The relevant property of the structure (for a given mass density) is the bending stiffness EI
E is the modulus of the beam material – material property
  In our case that’s dominated by the fibre
  We have seen that it’s already common to use UHM fibre – not much room for improvement
b
h
, (area) moment of inertia, aka second moment of area – geometrical property
  z is the distance from the neutral fibre, in symmetric cross-sections the neutral fibres is the centroid of the cross-section
  The neutral fibre is the axis in the cross section along which there are no longitudinal stresses or strains
  (if the cross-section is not up-down symmetric there is a non-zero product moment of area and the beam will deflect sideways and downwards)
Example: square beam

## Slide 9: Buckling
How do we improve stiffness (for a given amount of material)?
Separate high-modulus layers (`skins’)
However, now we run into a new problem: buckling stiffness
  Buckling theory is a little more advanced, but to give a feel:
  A long, slender, ideal column will buckle if the axial load exceeds (Euler 1757)
    We know EI (this corresponds now to the bending stiffness of an individual skin)
    KL is the effective length of the column (product of K, which is a support constraint factor, and L, the unsupported length)
    Usually we are worried about plate buckling, for which similar expressions exist
There are several ways to deal with buckling:
  Fill the space between the two skins with (light) material, which is bonded to the skins throughout (e.g. foam, honeycombs…) – increases EI
  Bond ribs to the skins - decreases KL
  Add profile to the skin (grooves) – if these are in different directions, they will again decrease KL

## Slide 10: Vibration response – internal vibrations
The most important source of internal vibrations is the flow of coolant through the system
This is particularly a concern for air flow cooling, which is considered for future lepton colliders
The exact prediction of displacement response is difficult, as it does depend on the coupling of the flow to the structure, which is a 3D problem
  In particular if flow is turbulent
Example: Study of Plume ladders (supplied by Bristol)
Peak at 1st mode frequency
However, because of the large modal mass, the structure will be dominantly excited in the first mode
We have built an experimental setup for this at Oxford
~ 10 cm
Unfortunately no
visualization of flow…

## Slide 11: Case study: Plank structure (ATLAS barrel strip stave)
Good thermal connection from silicon to cooling pipe (embedded in carbon foam with high thermal conductivity) – short thermal path
High degree of symmetry to reduce thermo-mechanical deformation
High buckling stiffness
But stiffness-to-mass ratio not overwhelming (area moment of inertia limited)
Interesting detail: Ti cooling pipe is bonded into foam. Despite FEA predicting that foam should break during thermal cycling, this was never observed in built stave
  Shows the shortcomings of FEA, when modelling complex geometries
Carbon honeycomb
Carbon foam
Ti cooling pipe
6 mm
Silicon modules
Skins: K13C2U w/
co-cured Kapton/Cu

## Slide 12: Case study: Truss structure (ALICE et al.)
Truss structures from filaments, which get soaked in resin, and then wound on a template
Very high stiffness to mass ratio
Performance difficult to predict (buckling, joint-driven) and complex mode spectrum (not only bending modes, but also torsional modes)
Power bus
Space Frame
Cold Plate
2x7 sensors
FPC
ALICE OB
CBM-STS (GSI)

## Slide 13: Case study: Box channel (STAR PXL)
0.4%X0/layer
Mechanics optimized for quick installation/de-installation
  Structure consists of cantilevered sector tubes
Air flow cooling through sector tube (9 m/s)
  Sector first mode: 230 Hz (measured)
  Sensor vibration at full flow: 5 μm RMS
  Sensor displacement at full flow: 25-30 μm
No TBA assumed for design
  All sensor positions surveyed on a half-detector
  But TBA was used in the analysis
Deformation under air flow
Sensor survey
7 layers of M55J

## Slide 14: Case study: Plume
Design for vertex detector under study for LCFI (aka PLUME)
Double-sided ladder with SiC foam core
  120 mm long, 10 mm wide
  Sensors: MIMOSA26, 50 micron thick
External air-cooling
0.65%X0 (but plans to improve, ultimate goal 0.3%X0)
  SiC foam 0.18%, sensors 0.11%, glue 0.2%, flex 0.29 %

## Slide 15: Case study: extremely low mass – Mu3e
Ultra–low mass (0.1%X0/layer)
Support structure originally planned to be made from folded Kapton
  Structural stiffness achieved by linking adjacent ladders to modules, which increases area moment of inertia
Recently started to look into single layer ultra-thin UD UHM carbon fibre for ribs
Electrical connection: Kapton/Al High Density Interconnect with tab bonding
He gas flow cooling
Steel dummy modules

## Slide 16: Further Material

## Slide 17: Track-based alignment
For TBA a subset of real data is used
  Typically well-constructed tracks with high momentum
  To get enough statistics need to accumulate data for finite alignment periods
    The length of these periods depend on the granularity of the alignment, and the rate of events (luminosity)
Then create a huge Χ2 with all the tracks and as parameters the positions/orientations of the substructures
This is typically done in granularity hierarchies
  Sub-detectors (barrel, endcap, etc.)
  Large structures (cylinders, disks, etc.)
  Local supports (staves/ladders, petals, etc.)
  Individual modules
At the highest level TBA can be done at ATLAS/CMS daily (few hours at SLHC)
Deformations below the level of individual modules can also be reconstructed
  Example: CMS barrel pixels – calibration of module bows
  To keep parameters manageable requires realistic deformation models/parametrizations
Number of parameters can be reduced if positions of subgroups of modules can be mechanically constrained
  Either build with high accuracy, or survey after construction – must not deform under dynamic loads
Developed for reconstruction of ATLAS & CMS – now used for all particle physics silicon systems
More
parameters
More data
required
Length of alignment period
Time between alignments

## Slide 18: Challenges for TBA
Weak modes
  These are certain classes of deformations with coherent degrees of freedom
  Not constrained by the global Χ2 fit – the results for these parameters are arbitrary
    That means that even if the system is perfectly positioned an arbitrary deformation will be introduced
  Solutions:
    Cosmics
    Higher level physics analysis (reconstruct mass peaks and see that they are correct for all directions)
Position perpendicular to detector plane
  High-momentum tracks typically cross detector planes perpendicularly – low sensitivity to perpendicular plane displacement
  While this will have a small effect for the high-momentum tracks used for the alignment, this can be an issue for low-momentum tracks
  Solutions:
    Cosmics
    This is an example where other (mechanical) means of position control or knowledge can be helpful (at the level of <100 µm)
Tracks going through one sense element (pixel/strip)
Well defined in this direction
Poorly in this

## Slide 19: Composite structures
The most efficient structural material are carbon fibre reinforced plastics (CFRPs)
  Efficiency here means stiffness/material
  CFRPs consist of a matrix of carbon fibre, embedded in a polymer
  The polymer is typically cured in an autoclave at elevated temperature (for polymerization) and pressure (for compaction) from a resin (which is tacky at room T)
    Typical cure temperatures are below 100°C (low T cure), around 125°C (medium cure T), or 170-200°C (high T cure) – dependent on resin
    The higher the T, the bigger the thermal stress is locked in; the lower it is the shorter the shelf life of the material is, and the lower the glass transition T
    Pressure is usually a few bar
Typical resin material is epoxy or cyanate ester
  We like the latter because it is very radiation hard and has a low CME (coefficient of moisture expansion)
  These can be procured already soaked into a prepreg, or on its own if needed as a glue or for wet lay-ups (where dry prepreg is used and the user infuses the resin)
Alternative fibre materials are glass fibre or synthetic fibres like Kevlar (Aramid)
  These usually have lower modulus, and are thus less useful for high stiffness applications (better for high strength)

## Slide 20: Carbon fibre - manufacture
Carbon fibres are fibres of about 5 to 10 µm diameter (1/10 of human hair)
Several 1000s of fibres (filaments) are spun into a tow
  Filament number (tow size) depends on brand
Start with a polymer such as polyacrylonitrile (PAN), rayon, or petroleum pitch
Then heated to drive off non-carbon atoms (carbonization)
Unidirectional
Weave
The final production step is a coating to protect them from damage during winding or weaving
  This is called sizing - process and material is proprietary
The carbon fibres are then often prepared in woven or uni-directional pre-preg and impregnated with resin

## Slide 21: How to minimize thermo-mechanical effects
Large silicon detector systems are a complex mixture of different materials
  Generally, they will have different CTEs (coefficients of thermal expansion)
  Hence the structures will encounter temperature-dependent deformations (like a bi-metallic strip)
    These can also be power-dependent, because of temperature gradients along thermally resistive conduction paths from the heat source to the local heat sink (typically coolant)
  Often, but not only, this is to due trigger rate variations within a fill
What strategy?
  Equalize temperatures and power consumption (good number: ±0.5-1°C)
    This is an important requirement that needs to be made clear to the cooling and the electronics people in your collaboration from early on
  Design symmetric structures
    Thermal strains balance – minimize deformations
Example of what can go wrong: ATLAS IBL
  Electrical cable bonded to one side of local support only
  Does require temperature control at the level of 0.2 K and regular alignment correction in the offline reconstruction
Service Flex Bus
CO2 Cooling Pipe
Pixel Module
Carbon Foam

## Slide 22: External vibrations
External vibrations are most usefully described by a vibration spectrum
  These are usually shown as power spectra
Two versions:
  Acceleration spectral density (ASD) – often in g2/Hz: More useful for load spectrum
  Displacement spectral density (DSD) – in something like µm2/Hz: More useful for response spectrum
  Connection is
For a given external vibration spectrum the displacements of the structures will have a spectrum , where is the response function of the structure
  can be obtained from FEA or measurements
ATLAS ID – measured ASD spectrum
Long-term-average over several months
Typically, external vibration spectra in static particle physics experiments are low
  A common misconception is that they have some special feature at line frequency
The external vibration spectrum depends on your location and environment
  Ideally, they need to be measured for your specific experiment, but this is not always possible in advance
  I have seen spectra for a range of experiments, with one exception, they have all been (well) below 10-7 g2/Hz
As we will discuss more quantitatively in the next lecture, these vibration levels are very low, and displacements due to external vibrations easy to be controlled
  In fact, I have the suspicion that most silicon detector supports are over-designed

## Slide 23: Milking Miles’ equation
If oscillator is loaded by external static force mg (gravity), can be expressed through the static deflection (sag)
and

## Slide 24: Bernoulli beam example
Beam length 1.08 m, EI = 32.92 kgm3/s2, mass density 0.31 kg/m, ζ = 0.017
fixed-fixed
Note that higher modes do not contribute that much, because their resonance peak is already in the damping tail of the 1st mode Miles’ equation is still a good predictor
Comparison to 1D oscillator
(use f1 as resonance frequency)
1st mode max
2nd mode max
3rd mode max
Even-n modes are not excited because of symmetry (would require rocking excitation)

## Slide 25: … and the mysterious Q factor…
The quality factor is a result of the damping of the system
I do not know of a simple way to predict this factor, yet it contributes as much to the displacement response as the ASD
In the study of a number of structures we have done it appears that bare mechanical structures have typically a Q value of a few 10
However, structures equipped with sensors (or sensor dummies) and services (or service dummies) tend to have lower Q values
  Which is what you would expect
I would be very interested if anybody has an idea to predict this…