## Slide 1: Introduction

## Slide 2: Goals of the meeting
Purpose:
  Come up with an (or a small number of) idea(s) what the ePIC SVT outer layer mechanics could look like
  Agree on a distribution of tasks
Target:
  Primarily: SVT outer barrel layers (L3 & L4)
  Including global supports, service management and cooling – this is likely to be the UK deliverable
  But, if there are good ideas for inner layers or disks, or implications from the outer layer design for these parts we can bring these to the collaboration as well

## Slide 3: Some context
Still many unknowns in the project (see later)
The EIC project needs to progress according to the DOE Project Path through a series of Critical Decision (CD) Milestones. Delaying CDs is not an option for a DOE project.
This means that the EIC project needs to demonstrate already now a level of detector technological readiness that is beyond where DSC are in term of R&D.
  Situation was created by funding delays & lack of critical mass to start R&D in earnest (affects many sub-detectors),
  As such, project engineers work on best “guesstimates” provided by the DSC
  Project engineers have shown a tendency to re-use previous technological solutions rather than looking at more recent developments
This is being remedied now – with the formation of the ePIC SVT collaboration…
  More institutes have joined! Meaning more people to do work and more experts that can help steer detector choices towards innovative, (beyond) state-of-the-art solutions
  Project has been divided into WP and WP leaders - most relevant here: WP4 Layers and disks, Nikki Apadula (LBNL) and Georg Viehhauser (Oxford)
  In the process of finalizing a Work Breakdown Structure (WBS)
  Next step is collection of system requirements and specifications
    This clearly is necessary for any progress on the mechanics and service management
  However, as will be discussed, there are central system specs that will only be finalised well after the mechanics and service designs are required for CD reviews
    Our solutions will have to provide flexibility to accommodate these changes
    At the same time, the project knows their current integration scenarios will need updating

## Slide 4: Knowns
Basic layout
This will be a MAPS detector
  ALICE ITS3 wafer-scale sensor for IB
  EIC Large Area Sensor (LAS) design derived from ALICE ITS3 sensors for OB/EE/HE
    We have no control over specs and timeline
  For further discussion of current size and considerations see James’ talk
Material requirements:
  Material per layer L0‒L2: 0.05% X0,
  Material per layer L3: 0.25% X0,
  Material per layer L4: 0.55% X0,
  Material per disk: 0.24% X0
The beam pipe is flared
  At least the inner layers and disks
  need too be designed so that they can be split
  That does not require a split of the outer layers, but it might facilitate integration (we become more independent of actual integration sequence)
Another consideration:
Lower material is wanted on the electron-going side (-z in the ePIC coordinate system
Momentum transfer measured primarily from the scattered electron, so we need to measure that scattered electron as well as possible.

## Slide 5: Layout
SVT in yellow
Other tracking systems: MPGD and LGADs
Inner layers (L0-L2) wants to follow the ITS3 design with bent sensors (see later)
Outer layers probably staves

## Slide 6: Sensor
Power density
Power density in the left endcap: 900 - 1200 mW/cm2
RSU size: 19.564 mm (w) × 21.666 mm (l)
Endcap size: 4.5 mm (L), 1.5 mm (R)
Sensor thickness
  Inner layers 20-40 μm
  Outer layers 50 μm
RSUs are connected by “stitching”
Currently considered for outer layers: a Large Area Sensor (LAS) comprised of 5 or 6 RSUs, and only left endcap

## Slide 7: FPC
More on this later, but here just to introduce:
Sensors will be connected to Flexible Printed Circuit (FPC)
  Length of the FPC < 50 cm, width not known
  Connected to readout board - RDO (ALICE calls this the detector service board – DSB)
    RDO will contain significant power sources, so will need (liquid/evaporative?) cooling – exact power not yet known
    RDO design and size not known
Data from DSB likely by optical fibre
Cables for power
Readout scheme for ePIC still under discussion (see Laura’s talk)
ALICE readout scheme

## Slide 8: Cooling
Radiation damage is not an issue, so no need for going cold
  Operational temperature is room temperature, no temperature cycling
  Power for SVT estimated about 5kW
Ideally we want to use gas cooling, at least for the inner layers
  See talk on ITS3 design on how this could be done
  Air flow through foam
  LBNL is investigating this actively
  Probably worth looking into also for outer layers (even power density might be higher in outer layers)
It is conceivable that there will be areas with high power densities that require fluid cooling
  The project baseline is liquid cooling based on previous experience
    Currently investigating sub-atmospheric water
  Evaporative cooling a possible alternative (would reduce material and service volume)
  If we use gas-cooling:
    Where is the heat sink (do we need to bring in the gas from the outside, do we exchange heat locally)?
    How do we move the gas (Pressure set externally, or local fan system)?

## Slide 9: Summary and timeline
Main unknowns
  Number of RSUs per sensor is converging to 5 to 6, but might change when yield is known
  If we rely on stitching (baseline, for alternative see more on this in discussion on flex circuits), this will depend on yield
  mechanics design needs to be flexible
  FPC design and connections
  Cooling technology
Timeline
  TDR by end of 2024
    By then we need technology choices and a demonstration that all ingredients to deliver them work