## Slide 1: Software Status updates
Takashi Hachiya
Nara Women’s University

## Slide 2: Toward DST Production
Workflow of DST production
  Rawdata DST(TrkrHitSet) is produced for each sub-system
  Decoder issue will be fixed soon (Chris sent a message he updated the decoder yesterday)
    Event synchronization among subsystems is also done at this production
      Synchronization is done by BCOFull
    Event Header
      Each subsystem has their own event header in DST
        Joseph made 1st version of INTT event header.
        Chris mentioned that the data size is too much. (8 BCOFULL (40bits each))
        Need to consider what information should be saved in the event header: Failure information, and so on
  At GM, agreed that any results by the private decoder cannot be sPHENIX official result
Decoder issue
  Last week, found that F4A decoder mistakenly produced multiple events which have the same BCOFULL value
    Chris said it is fixed now (yesterday). I will check it again

## Slide 3
Nhit can be recovered by adding two events
My decoder
FFA decoder
Nhit (BCO)
Nhit (BCO)

## Slide 4: Implementing HotDeadmap code
InttDeadMap.h/cc (simulation/g4simulation/g4intt)
  To mask dead channels in simulation. Implemented a few years ago by Purdue group
  I would like to use this as the v0 version for Hot/Dead map
    Just for simulation but can be used for both data and sim with updates
  In InttDeadMap, dead ch are managed by stl::set (key=64bit int)
    Offline numbering is used
  To update,
    I would like to ask which online(hard) or offline numbering is good
      I prefer online numbering because I want to use the same format to manage hot/dead channel map for both DST reconstruction and DAQ
    Data structure needs to be updated to handle dead/hot (/ warm/ cold) statuses
      Set -> map
63-56 | 55-40 | 39-32 | 31-16 | 15-0
Layer | Ladder_phi (ladder) | Ladder_z(sensor) | Strip_z (chip) | Strip_phi (channel)

## Slide 5: Current status：Work flow for the production
Event-Gen
Ghit (PHG4Hit)
Trkrhit (hits in local coordinate)
TrkrCluster
<Simulation>
DST-sim
Martin, Joseph
Root Raw Data Format*
…
Unpacker
Joseph
OutputTree（Raw Data）
Amp, Hit Ch, ADC, Chip, Ladder-ID, bco, bcofull
Online->offline Conversion map
Online Monitor
Hot/dead channel map
Amp is to be dropped
Manami
Event Display
RCDAQ
physics
calib
evt (32 bit word)
Remove HotDead
Fun4AllDecoder
(SingleInttInput)
InttCombined
RawDataDecoder
InttCombined
RawDataConverter
Remove Badhit
Two different mod.？
New format？
EventBaseTree(or HitBaseTree)
Geometry
alignment
Cut cls w smallerE
InttDeadMap

## Slide 6: (expected) workflow : Multi-stage approach
INTT (Fun4All_Intt_Conbiner.C)
EVT file
Decoder
Raw data DST (HitSetContainer)
MVTX(Fun4All_Mvtx_Conbiner.C)
EVT file
Decoder
Raw data DST
TPC
Raw data DST
Intt
Clustering
MVTX
Clustering
CAL
Raw data DST
TPC
Clustering
CAL
Clustering
Clustering and tracking
Global Tracking
1st stage
2nd stage
Benefit: we scan the data to determine hot/dead/bad channel. These info can be applied in 2nd path
Remove HotDead
HotDead
map

## Slide 7: Alignment procedure
We expect : subsystem is responsible for local alignment, and tracking group is for Global alignment
  This is not sure for now. Tracking group said that all the alignment will be done by tracking group with the cosmic ray data
  But no time line, no framework, It will take huge amount of time
  We need INTT local alignment for dN/deta
    It is good to start the alignment by ourselves.
    MVTX/MIT group knows how to use the alignment package based on Milliped.
      I asked them to show their code

## Slide 8: 存在するDeadMapの構造
InttDeadMap.h (simulation/g4simulation/g4intt以下)
  G4intt以下なのでSim専用という位置づけ
    → データでも使う場合、要変更。
  STLのSetを使用した配列 ( mapのKeyだけ)
    std::set<PHG4CellDefs::keytype> Map;
      typedef uint64_t keytype;
        Layer, ladder, sensor , chip, channel を含む64bit integer : OFFLINE_CHで定義
  Hot, Deadなど(Warm, Coldも？) 、状態を分けたい場合、 setでは情報がたりない。
    →MAPに変更したらよい。
DAQ用のHotChannel リスト
  テキストファイルを直接読む形式： Hardware Chによって制御 (Jaeinのフォーマット？)
63-56 | 55-40 | 39-32 | 31-16 | 15-0
Layer | Ladder_phi (ladder) | Ladder_z (sensor) | Strip_z (chip) | Strip_phi (channel)