## Slide 1: SVT-DSC – Test beams
2024: no EIC-LAS; ITS3 wafer scale sensor TB organized by ITS3
2025: 1 to 2 weeks, EIC-LAS v1
2026: 3 to 4 weeks, EIC-LAS v1 and v2
2027: 2 weeks, EIC-LAS v2
2028: possibly 2 weeks, EIC-LAS production
Updated in test beam spreasheet
Irradiation, latch-up tests, etc. at local facilities (i.e., available within SVT-DCS) are not explicitly considered here.

## Slide 2: SVT-DSC – Simulations, software
Channel count updated
Threshold on individual hit level: to be reduced from 0.65 keV to 0.54 keV, being confirmed with designers
Threshold on summed energy: not applicable
  Sensor provides only binary, i.e. hit/no hit information
Pedestal position/cut on sigma of pedestal: not applicable
  Sensor provides only binary, i.e. hit/no hit information
Intrinsic/dark noise rate at this threshold: < 10-3 per pixel per second (conservative upper limit) – no update

## Slide 3: SVT-DSC – Simulations, software
Charge sharing: 1.2 at 90 degrees – no update
Gate-on time (integration time): 2 µs target – no update
Gate-off time (deadtime): no estimate at this time
Updating in the EPIC Detector Digitization Model.10.2023
  Note that we updated the information also in OLD.EPIC Detector Digitization Model.09.2023 by mistake
Shujie Li remains the main contact