## Slide 1: BHCal Thresholds in EICrecon (ca. 10.23.2023)
Threshold on Summed Energy:
  5 MeV
  This is half-MIP, or about 20 SiPM pixels
Pedestal Mean/Position:
  Set to 10 ADC counts in EICrecon
    About 0.150 MeV (for 15 keV/count)
  Expect MIP peak at ~10 MeV
    About 40 SiPM pixels…
Pedestal Sigma:
  Set to 2 ADC counts
Cut on Pedestal Sigma:
  Set to 5
  thresholdADC = (thresholdFactor x pedSigmaADC) + minADC
    thresholdFactor = 5
    pedSigmaADC = 2
    minADC = 1
Clustering: threshold on minimum energy of tile to be added to cluster
  5 MeV (or 30 MeV for central tile)
Note: ADC threshold given by:
  threshold = (cutOnSigma x pedSigmaADC) + minADC
    cutOnSigma = 5
    pedSigmaADC = 2
    minADC = 1
Note: keV/ADC count calculated via
  perCount = dynamicRange / capADC
    Dynamic range = 1 GeV
    capADC = 65536

## Slide 2: Backup | BHCal Reconstruction in EICrecon1.6.2
BHCal HitDigi Configuration
BHCal HitReco Configuration

## Slide 3: Backup | BHCal Reconstruction in EICrecon1.6.2
BHCal Clustering Configuration