## Slide 1: ML for Beam Polarization Increase Accepted ML / AI Proposal to DOE-NP FOA
CAD MAC December 20, 2023
Georg Hoffstaetter de Torquat
Collider-Accelerator Department, BNL and Cornell University
Georg.Hoffstaetter@cornell.edu

## Slide 2: DE-FOA-0002875 : ARTIFICIAL INTELLIGENCE AND MACHINE LEARNING FOR AUTONOMOUS OPTIMIZATION AND CONTROL OF ACCELERATORS AND DETECTORS
Title: Higher RHIC polarization by Physics-informed Bayesian Learning
Budget: $1.5M, duration 2 years, start 09/01/2023 to BNL, Cornell, JLAB, SLAC, RPI
Funding through DOE-NP DE SC-0024287, contr.# 2023-BNL-AD060-FUND
Funding officer Manouchehr Farkhondeh
Requested topics:
Efficiently extract critical and strategic information from large complex data sets
Address the challenges of autonomous control and experimentation
Efficiency of operation of accelerators and scientific instruments
AI for data reduction of large experimental data

## Slide 3: Desired result: higher proton polarization
What high-impact operational challenge can be addressed by MI/AI?  Polarized protons.
From the source to high energy RHIC experiments, 20% polarization is lost.
Polarized luminosity for longitudinal collisions scales with P4, i.e., a factor of 2 reduction!
The proton polarization chain depends on a hose of delicate accelerator settings form Linac to the Booster, the AGS, and the RHIC ramp.
Even 5% more polarization would be a significant achievement.

## Slide 4: Outline
Objective of proposed work: higher proton polarization in RHIC and the EIC.
Polarized-proton acceleration chain.
Potential avenues toward higher proton polarization.
(1) Emittance reduction
(2) More accurate timing of timed elements
(3) Reduction of resonance driving terms
Started Activities
Gaussian Process (GP) Bayesian Optimization (BO) and physics informed learning.
When is ML/AI better for accelerator operations than other feedbacks and optimizers?

## Slide 5: The polarized proton accelerator chain

## Slide 6
PHENIX (p)
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
Siberian Snakes
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR (p)
AGS Polarimeters
Spin flipper
Linac – Booster – AGS Optimization
Readily available, large data flow possible

## Slide 7: Topics that can improve polarization
(1) Emittance reduction
(2) More accurate timing of tune jumps
(3) Reduction of resonance driving terms

## Slide 8: Emittance reduction  less depolarization
Optimized Linac to Booster transfer
Optimized Booster to AGS transfer
Optics and orbit correction in Booster and AGS
Beam-based Quadrupole calibration from ORM in Booster and AGS.
Bunch splitting in the Booster for space charge reduction and bunch re-coalescing at AGS top energy.

## Slide 9: Linac to Booster transfer
Parameters to vary:
Transfer line steers
Main Booster dipol90e field
Booster beta wave (stop-band quadrupoles) for tune toward ½ and minimum on the foil
Last two linac phases
Injection bump elements and their time profile
Scraper amplitudes
Observables to optimize:
Transfer efficiency linac  Booster early ramp (2% absolute)
Emittance from multi wires of the AGS transfer line (5% relative)

## Slide 10: Booster to AGS transfer
Parameters to vary:
Transfer line steerers
Main AGS dipole field
AGS RF phase
Amplitudes of two Injection bumps
Horizontal orbit in the snakes
Quadrupole corrections for the snakes
Injection to accelerator tune change
Observables to optimize:
Transfer efficiency Booster  AGS early ramp (2% absolute)
Emittance from two IPMs (10% relative)

## Slide 11
Response Error model for the ORM

## Slide 12: Sensitivity studies: error sources
Name | Unit | Range
Main magnet roll error | mrad | [-0.5, 0.5]
Main magnet gradient error | m-2 | 
Quadrupole gradient error | m-2 | 
Sextupole offset error | mm | [-8, 8]
Snake magnet roll error | mrad | [-1.5, 1.5]
Name | Unit | Range
Main magnet roll error | mrad | [-0.5, 0.5]
Main magnet gradient error | m-2 | 
Quadrupole gradient error | m-2 | 
Sextupole offset error | mm | [-8, 8]
Snake magnet roll error | mrad | [-1.5, 1.5]
Sources or error and ranges come from past survey data
Criteria to quantify & visualize sensitivity:
  RMS of ORM matrix
  Beta-beating (vertical & horizontal)

## Slide 13: Where do we put AI/ML?
ORM will give us
  BPM and Corrector Anomalies (Trust Analysis)
  Gradient errors for given conditions
  Beta-deviations from model
Dispersion measurements give us
  BPM Consistency check for given dp/p (BPM Anomalies)
  Coupling through longitudinal motion (very slow, typically)
Tune measurements
  Betatron tune and coupling = destructive measurement in Booster/AGS
  Tune, Chrom, coupling, emittance, dp/p from RHIC Schottky
Chromaticity measurements – need to change energy and measure tune
Orbit Measurements – parasitic = most are time averaged, some turn by turn
Linear model + small nonlinearities with NN model

## Slide 14: Orbit & Optics correction in Booster / AGS
Parameters to vary:
Corrector coils (24 per Booster plane)
Corrector coils (48 per AGS plane)
Observables to optimize:
BPM readings (24 x&y in the Booster) (100um accuracy)
BPM readings (72 x&y in the AGS) (100um for 2mm size at 25GeV)

## Slide 15: Space-charge emittance increase
 Splitting bunches before AGS acceleration can reduce the emittance.

## Slide 16: Bunch splitting / coalescing
Splitting in the booster and coalescing after AGS accelerator reduces space charge and emittance growth  more polarization

## Slide 17: Bunch splitting and coalescing
Parameters to vary:
3 RF amplitudes and phases, and their timing
Observables to optimize:
Mountain range width (5% relative)
Mountain range oscillations (10% of a sigma)
Baby-bunch currents (2%)
Emittance in the multi-wire to the AGS (5% relative)
Emittance from two IPMs (10% relative)

## Slide 18: Timing of tune jumps
The G-gamma meter and accurate energy vs. time
Measure the energy by orbit + revolution frequency measurement
Measure of energy by field + revolution frequency measurement
Measure energy by spin flip at every integer spin tune
Combined optimization
better timing
 higher polarization

## Slide 19: Improved energy timing
Parameters to vary:
Time profile of the time-jump quadrupoles
Observables to optimize:
Revolution frequency (1.E-6)
Radial offset from BPM readings (20mu average)
Main dipole fields Hall-probe at injection (0.1%) + integrating coil (2%)
E(t) by measure f(t), x(t), B(t), P(t)

## Slide 20: Reduction of AGS resonance driving terms
Polarization is preserved in the AGS with two partial helical dipole snakes (10% and 6% rotation)
Provides spin tune ‘gap’ where imperfection and vertical intrinsic resonance condition are never met
  νs ≠ N (full spin flips)
  νs ≠ N +/- Qy
Horizontal resonance condition still met
  νs = N +/- Qx
  Horizontal resonance are weak, but many (82 crossings)
  Currently handled with fast tune jump
    ΔQx = 0.04, 100 μs
Spin tune gap
Hor resonance crossings
Tune
jump
(pause tune jump near transition)
Partial snakes drive horizontal depolarizing resonances
 Compensate by other coupling elements, e.g., skew quads

## Slide 21: Reduction of AGS resonance driving terms
Horizontal Resonance Amplitudes in AGS
Two snakes, separated by 1/3 circumference
  Modulated resonance amplitude highest near Gɣ = 3N (when snakes add constructively)
Horizontal resonances occur every 4-5 ms at the standard AGS acceleration rate
ML/AI:
Physics informed
Learning of the optimal
skew quad strength +
optimal timing.

## Slide 22: Reduction of resonance strengths
Parameters to vary:
14 Skew quad amplitudes at each of 80 resonances
Timing of skew quad changes
Observables to optimize:
Polarization after the ramp (2% relative)
Polarization at intermediate energies (2% relative)

## Slide 23: Activities
Kickoff Collaboration meeting @ Cornell, August 25, 2023 – successful in person
Weekly meetings Mondays 3:30pm of all collaborators
Interface with weekly meeting Wednesdays 11am on digital twins from Linac to AGS
Semi-weekly ML/AI software meeting Friday’s on beam & ML computer standards
To be addressed: Potential avenues toward higher proton polarization
(1) Emittance reduction
(2) More accurate timing of timed elements
(3) Reduction of resonance driving terms

## Slide 24: Dominant Participants
Dominant participants:
BNL: Kevin Brown, Weinin Dai, Bhawin Dhital, Yuan Gao, Kiel Hock, Bohong Huang, Natalie Isenberg, Nguyen Linh, Chuyu Liu, Vincent Schoefer, Nathan Urban
Cornell: Georg Hoffstaetter de Torquat, Lucy Lin, Eiad Hamwi
SLAC: Auralee Edelen
JLAB: Malachi Schram
RPI: Yinan Wang
Radiasoft: Nathan Cook, Jon Edelen, Chris Hall
Teams: (1) Accelerator simulation – digital twins, (2) ML application – code development, (3) Experiment 2 simulation comparison.

## Slide 25: Started Activities
Emittance reduction by linac 2 booster optimization:
  Adjust the model to hardware and alignment data for the L2B line
  Simulate scraping of beam in the Booster, including ionization foil with Bmad
  Write Bmad function that produces loss rate vs. last two L2B correctors and bring to OpenAI Gym format.
  Apply established ML codes to this function.
(2) Emittance reduction by booster optimization
  Compare Bmad to established Zgoubi results and compare to BPM/alignment measurements
  Establish booster-orbit response to corrector changes and produce function that gets minimized by optimizing system parameters, e.g. element alignments, bring into OpenAI gym format.
  Apply established ML codes to this function.

## Slide 26: Started Activities
(3) Emittance reduction by B2A transfer:
  Adjust the Bmad model to hardware and alignment data for the B2A line
  Simulate Booster phase space transfer through this line and compare to measured harp profiles
(4) Emittance reduction by re-bucketing
  Adapt Bmad bunch-merging code for the EIC’s RCS to the Booster (bunch splitting) and AGS (bunch merging)
  Compare Bmad to established Python re-bucketing code for Booster and AGS
  Write a function that characterizes bunch splitting/merging efficiency from RF parameters for ML/AI optimization.

## Slide 27: Started Activities
(5) Depolarization reduction by Skew-quad resonance minimization in the AGS:
  Detailed Bmad model of the AGS at all energies overcoming:
    Non-symplecticity of tracking through field maps of snakes
    Introduce differentiable models of snake fields and match these to their field maps
    Compensate the closed orbit, optics, coupling, and dispersion (esp. vertical) for these maps at all energies
  Compute resonance strength of the Bmad model and compare to established results
  Compare resonance strength to previous measurements
  Define optimized skew-quad compensation schemes at all 82 resonances, minimizing vertical dispersion, coupling, optics errors, and speed of skew-quad changes
(6) Improved g-gamma meter by combining it’s 3 measurements
  Technique discussed, Team being formed
(7) Combined and verified evaluation of existing emittance measurement techniques (through Radiasoft)
  Technique discussed, Team is formed

## Slide 28: Optimizers for different applications
Courtesy Auralee Edelen

## Slide 29: Characteristics of involved optimizations
Optimal parameter settings are hard to find, and the optimum is difficult to maintain.
The data to optimize on has significant uncertainties.
Models of the accelerator exist.
A history of much data is available and can be stored.
Is this type of problem suitable for Machine Learning?
Why would ML be better suited than other optimizers and feedbacks?

## Slide 30: Gaussian Process
GP model built with scikit-learn library
A probability distribution over possible functions that fit a set of points
Mean function + Covariance function
Kernel: covariance function of the input variables
Covariance matrix
At a sample point , Gaussian process returns mean and variance

## Slide 31: Acquisition Function
Guide how input space should be explored during optimization
Combine predicted mean and variance from Gaussian Process model
  Probability Improvement (PI)
  Expected Improvement (EI)
  Upper Confidence Bound (UCB)
[2]

## Slide 32: Merit of physics-informed optimization
Courtesy
Auralee Edelen

## Slide 33: Unknown system parameters
Courtesy
Auralee Edelen

## Slide 34: Advantages of Bayesian Optimization

## Slide 35: Why is Bayesian Optimization suitable?
1. The data to optimize on has significant uncertainties
No derivatives have to be computed.
2. Models of the accelerator exist
the expected functional form can be included in the function search (Physics-informed learning)
3. A history of much data is available and can be stored
 All past data are included to model the function to be optimized.

## Slide 36: Summary
A proposal to DOE-NP has been accepted for the enhancement of proton polarization using ML/AI. Goal: 5%.
Several accelerator optimizations can impact polarization.
These topics are of the type suitable for Bayesian Optimization
Excellent team has formed, items being addressed:
Emittance reduction (orbit, optics, bunch splitting)
More accurate timing of quadrupole jumps (G-gamma meter)
Reduction of resonance driving terms (Horizontal spin matching with skew quads)

## Slide 37: Publications
ML/AI efforts at BNL/CAD
B. Huang, C. González-Zacarías, S. Sosa Güitrón, A. Aslam, S. G. Biedron, K. Brown, T. Bolin, Artificial Intelligence-Assisted Design and Virtual Diagnostic for the Initial Condition of a Storage-Ring-Based Quantum Information System, IEEE Access, Volume 10, 2022, pp.14350-14358
Y. Gao, W. Lin, K. A. Brown, X. Gu, G. H. Hoffstaetter, J. Morris, and S. Seletskiy, Bayesian optimization experiment for trajectory alignment at the low energy RHIC electron cooling system, Phys. Rev. Accel. Beams 25, 014601 – Published 7 January 2022
Y. Gao, J. Chen, T. Robertazzi, and K. A. Brown, Reinforcement learning based schemes to manage client activities in large distributed control systems, Phys. Rev. Accel. Beams 22, 014601 – Published 2 January 2019
W. Lin, M. A. Sampson, Y.C. Jing, K. Shih, G. H. Hoffstaetter, J. A. Crittenden, Simulation Studies and Machine Learning Applications at the Coherent Electron Cooling Experiment at RHIC, IPAC2022, Bangkok, Thailand
Y. Gao, K. A. Brown, X. Gu, J. Morris, S. Seletskiy, W. Lin, G. H. Hoffstaetter, J. A. Crittenden, Experiment Of Bayesian Optimization For Trajectory Alignment At Low Energy RHIC Electron Cooler, IPAC2022, Bangkok, Thailand
Y. Gao, K. A. Brown, P. Dyer, S. Seletskiy, H. Zhao, Applying Machine Learning to Optimization of Cooling Rate at Low Energy RHIC Electron Cooler, IPAC2021, Campinas, SP, Brazil
Polarized proton beams at BNL
K. Zeno, An overview of Booster and AGS Polarized Proton Operations during Run 17, BNL-114742-2017-TECH (10/2017)
K. Zeno, Run 16 Tandem gold performance in the injectors and possible improvement with AGS type 6:3:1 bunch merge in the Booster, C-A/AP/576, (10/2016)
V. H. Ranjbar, Approximations for crossing two nearby spin resonances, Phys. Rev. ST-AB 18, 014001 (2015)
Y. Dutheil, L. Ahrens, H. Huang, F. Méot, A. Poblaguev, V. Schoefer, K. Yip, Energy Calibration and Tune Jumps Efficiency in the PP APS, in Proc. PAC2014, Dresden/Germany (2014)
V. H. Ranjbar, M. Bai, H. Huang, A. Marusic, M. Minty, V. Ptitsyn, Experimental Effects of Orbit on Polarization Loss in RHIC, Proc. IPAC2012, New Orleans/LA (2012)
V. Schoefer, L. Ahrens, K.A. Brown, J.W. Glenn, H. Huang, Optics Error Measurements in the AGS for Polarized Proton Operation, Proc. PAC2011, New York/NY (2011)
V. Schoefer, Using betatron coupling to suppress horizontal intrinsic spin resonances driven by partial snakes, Phys. Rev. AB 24, 031001 (2021)
V. Schoefer, AGS Horizontal Resonance Compensation Overview, Presentation at BNL (2022)

## Slide 38: Thank you and Questions?