## Slide 1: The JUNO distributed computing infrastructure
Giuseppe Andronico

## Slide 2: Location of JUNO and JUNO-TAO
74 Institutes, 17 Countries, about 750 people
Yangjiang NPP
20 kton LS detector
700 m underground
TAO
Yangjiang | Taishan
17.4 GW | 9.2 + 9.2 GW
Taishan NPP
Guang Zhou
Daya Bay
Hong Kong
JUNO
53 km
53 km
Notes: The 6th Yangjiang reactor core started commercial operation on July 24, 2019.
The 2nd Taishan core started generating power this June.
All six 2.9GW cores in Yangjiang and two 4.6 GW cores in Taishan are in operation now.

## Slide 3: Neutrino Physics with JUNO
Mass Hierarchy w/ reactor: 3-4σ in 6 years
Precision w/ reactor: sin212, Δm221, Δm231 to <1%
Supernova Burst: 5k events + Neutral current
Diffuse SN Background: Discovery potential
Geo-neutrino: Determine Geo-physics model
Proton Decay: Best in K channel
Solar
Atmospheric
Sterile
Neutrino from Dark Matter
Exotic searches
JUNO Yellow book J. Phys. G 43, 030401 (2016)

## Slide 4: JUNO Detector
Central detector
Water Cherenkov
Top Tracker
Calibration
Pool Depth: 44m
Pool ID:43.5m
Acrylic sphere : ID35.4m
Stainless steel latticed shell: ID40.1m
Filling/Overflow
Acrylic sphere
(20 kt LS)
18000 20” PMT
25000 3’’ PMT
~2000 20’’ PMT
SS latticed shell
Acrylic Sphere:
ID: 35.4m
Thickness:120mm
SSLS:
ID: 40.1m
OD: 41.1m
Water pool
ID: 43.5m
Height: 44m
Water Depth:43.5m

## Slide 5
  upper limit 2PB/year
Raw data
  order of 200TB/year
Rec data
  order of 100TB/year
Sim data
  0.6 PB/year
Calibration data
  order of TB/year
Analysis data
Data type and volume
Storage
upper limit 3PB disk/year
Computing
12000 CPU cores
Total resources requirements
Computing model: data

## Slide 6: Base design

## Slide 7: Network in China
REAL 10G
NEW 100G

## Slide 8: Global Networks for JUNO
ORIENTplus 10Gbs
Real 10G
INTERNET2
GEANT
TEIN3
100Gb

## Slide 9: Mail policies
Use DIRAC as DCI core service
  Experience at IHEP and in most of the data centres
Join LHCONE
  Virtual lan built on interconnected NRENs
Keep JUNO DCI in sync with WLCG
  Data centres are T1 in WLCG
  Funding agencies are familiar with WLCG standards

## Slide 10: Conclusions
JUNO needs a distributed computing infrastructure (DCI)
DCI already designed and under deployment and testing, by means of an intens international collaboration
Key components are the global research and education networks

## Slide 11
Thank you!!!
Any question?