## Slide 1: Pre-Injectors
Jim Alessi

## Slide 2
Preinjectors –ion sources and initial acceleration for all beams used for RHIC, BLIP, and NSRL

## Slide 3: Preinjector Systems
200 MeV H- Linac
  Polarized H- for RHIC
    200 MeV; mA’s
  H- for Brookhaven Linac Isotope Producer (BLIP)
    66-200 MeV; >40 mA peak, up to 130 μA average
EBIS Preinjector
  Helium to Uranium ions for RHIC and NASA Space Radiation Laboratory (NSRL)
  1 second switching between species for simultaneous operation
Two 14 MV Tandem Van de Graaff’s
  No longer used for RHIC
  Outside user program for electronics testing, micropore filter production (medical/biological), etc.
Other
  RHIC Polarimeter support
  Laser Ion Source
    1+ for EBIS and high charge state for medical applications, etc.
  EBIS-related R&D
    Polarized He-3 for RHIC
    Improved electron gun (CERN collaboration)
    Charge breeder (ANL collaboration)
    eLen – electron gun & collector design; component testing on Test EBIS
  Plasma-related applications
    Plasma windows, plasma lenses, in-situ copper coating of RHIC beampipe, etc.

## Slide 4
H- and Polarized H- sources
RFQ and buncher
~300’ transfer line; polarimeter, energy measurement
H- transfer line to BLIP
200 MeV linac, 475’, 9 rf cavities & rf systems, 286 drift tubes & quads, 143 quad ps’s
H- transfer line to Booster
Nature of preinjectors – always the first things on and the last things off
EBIS, 1+ sources, RFQ, IH Linac, 3 bunchers, heavy ion transfer to Booster
Sources, accelerators, and transport lines included:

## Slide 5
BLIP
Transport to polarimeter
LINAC
EBIS
Booster

## Slide 6: Front end of 200 MeV Linac
Magnetron H- source
RFQ
Polarized H- source

## Slide 7
200 MeV Linac – 9 cavities, 150 m long, 286 drift tubes/quads

## Slide 8
Linac rf systems (9) – 200 MHz, 5 MW peak power

## Slide 9
Lower equipment bay – tank drift tube pulsed quad ps’s, vacuum systems, transport line magnet ps’s, water systems, high power coax splitters, etc.

## Slide 10
Chopper, RFQ, and buncher cavity
H- ion source, ~80 mA peak, 600 us, 6.66 Hz

## Slide 11: 200 MeV transport lines to Booster, polarimeter, and BLIP

## Slide 12
5A proton source
3T SC solenoid
Cr:LiSAF laser & probe laser
H neutralizer
He ionizer
Polarized Rb neutralizer
Na ionizer
Sona transition
HV extraction
Low energy polarimeter
The source is comprised of many complex systems:
Highest intensity polarized H- source in world

## Slide 13
All parts of the polarized H- source
Source & polarimeter
Source ps’s
Transport, spin precession
Controls, polarimetry

## Slide 14: Polarized gas jet – before installation in RHIC (group provides primary support for operation & maintenance)
Also, for RHIC CNI polarimeter, group makes ~300 targets/year, 25mm long, 50 nanometer thick, 10 microns wide; mounted individually on frames
Atomic H beam, sextupoles, 21 turbos

## Slide 15
EBIS
RFQ
LINAC
BOOSTER
DIPOLES
BEAM TRANSPORT LINE
EBIS Preinjector – high charge state heavy ions
3He to U (15 species run to date)
All heavy ions for RHIC and NSRL
Acceleration to 2 MeV/u for injection into Booster

## Slide 16
E-Gun
(10 A)
Drift Tube Structure (P<10-10 Torr)
Electron Collector
Superconducting Solenoid (5 T)
Highest intensity EBIS in the world
Source includes 10A electron gun & collector
5T SC solenoid
Ultrahigh vacuum system
2 ion sources for 1+ ion injection

## Slide 17
Two 1+ heavy ion sources to produce desired species
EBIS source PS’s
15A, 15 kV ps between the electron gun and electron collector
Two 150 kV, 200 kVA isolation transformers
100 kV platform pulser – 200µs risetime, 500 µs flattop
40 kV, 20 mA gun anode ps
Ten 20 kV, 20 mA (100 mA burst) drift tube ps’s
2 room temperature solenoids and 8 steering ps’s (electron beam)

## Slide 18: EBIS - Heavy ion accelerators and transport lines
RFQ, MEBT, and Linac
Linac and EBIS-to-Booster transport
2 x 300 kW and 3 & 10 kW rf systems

## Slide 19
Collaboration with MIT (R. Milner, J. Maxwell, C. Epstein)
Polarized He-3 gas cell - preparations at MIT
Will be brought to BNL this fall and tested on EBIS spare solenoid for possible depolarization during injection into trap field
Polarized helium-3 source for RHIC using EBIS ionizer

## Slide 20
Improved EBIS electron gun – designed by BNL EBIS scientist, built in collaboration with CERN, and is now being prepared for testing on BNL Test EBIS
Could produce 10 times higher current density in the trap, resulting in 10-times shorter confinement times, and therefore shorter electron beam pulses
  could improve charge state distribution, vacuum, emittance

## Slide 21
40kV
Ground Potential
55 kV Break
40 kV Break
40 kV Station Insulator
Laser Ion Source for improved flexibility when running multiple species from EBIS
1+ injection into EBIS
NASA funded – will be installed on EBIS this fall

## Slide 22
H- source, LEBT, MEBT, linac, rf systems, quads, transport lines, diagnostics, vacuum ~6
Polarized H- source, linac polarimeters, RHIC polarimeters & targets ~3
EBIS source, 1+ sources, heavy ion RFQ, Linac, transfer lines, ps’s, etc. ~4
Laser source; EBIS developments; other R&D for RHIC ~3
ME, EE, machinist, secretary, group leader, floating techs ~6-7
(support for all of above)
Misc. support (other groups) ~1-2
TOTAL ~24
Procurements:
Largest is rf tubes for 200 MeV linac - ~1.1 M$/year
Otherwise, typically ps repairs/replacements, vacuum pump repairs/replacements, etc.
Rough breakdown of manpower

## Slide 23: Pre-Injectors
Reduction in labor primarily due to switch from Tandem to EBIS preinjector