## Slide 1
fECal tower components does not require radiation hardness studies:
Epoxy – two types, tested up to 15 MRad, no degradation (mechanical properties)
SiPM to light guide coupling – silicone, selected by CMS in 2002, used for STAR FCS.
Light guides and scintillation fibers, at EIC conditions does not expect to see noticeable changes in LY or transparency.
Radiation hardness studies for fECal are required only for readout electronics and sensors*
N.B. there is a plan to do SiPM irradiation and characterizations by UC EIC consortium.
Radiation hardness studies needed for forward ECAL
O. Tsai / G. Visser, 12/11/23

## Slide 2
Radiation hardness studies needed for forward ECAL
Principal electronic components
SiPM’s (S14160-6015PS)
Preamp (OPA838 or ADA4895-1†)
ADC driver THS4552
ADC ADC3442‡
bias voltage regulator parts†
Polarfire FPGA (MPF100T)
DC/DC (LTC3600 or LTC3601)
reference for bias regulator‼
LVDS driver (ADN4663)
LVDS receiver (tbd)
Jitter cleaner?
LED (tbd)
O. Tsai / G. Visser, 12/11/23
SiPM board prototype, 10 × 5 cm, 32 SiPM’s
available 3/24? (Enough SiPM in hand?)
Form for the tests
2-channel signal path test board, connects to Polarfire eval board, ~8 cm square
available 3/24, maybe sooner if need be
†) Worked well in STAR FCS, a kind of practical test
‡) Note: ADC choice is still contingent on hit rate requirements
‼) Will not use this – lesson learned from FCS – take external V ref
(SiPM gain is too sensitive to small percentage change of Vbias)
1 or 2 dedicated DC/DC prototypes, ~ 6 cm square
available 1/24
TBD / perhaps some of these parts can be selected and evaluated in common in ePIC.
For LED’s study a collection of various types, iraddiated w/o bias.
①
②
③
④
⑤
Complete FEB prototype, 20 × 10 cm
available 5/24 (but, first version not informed by component radiation tests beforehand, probably; rad. test later version may be better)

## Slide 3
Apart from the SiPM studies, radiation tests should ideally be done on devices under bias (normal operating conditions in the application)
  damage to SiPM’s in general is well understood and it’s known not important to irradiate them under bias. Right?
Consideration is needed of what characteristics of a component need to be evaluated, e.g., increase of noise, gain changes, supply currents, transient effects
  Some important characteristics might not be accessible in testing complete FEB or RDO assemblies – a program of component-level tests as indicated will be best. Suitable test points / test circuits needed.
At electronics on face of fwd ECAL, 1 MeV equivalent neutron dose 2-3 × 1010 per year (estimated from plots on https://wiki.bnl.gov/EPIC/index.php?title=Radiation_Doses)
1 MeV equivalent proton dose 9 × 109 per year
The total ionizing dose 1.5 krad per year
  Not high enough to worry about
Considering 10 year operation, test to 3 × 1011 n/cm2 and 9 × 1010 p/cm2
  Do we need to check both protons and neutrons? I don’t know. Damage does differ (e.g. https://www.oeaw.ac.at/fileadmin/Institute/HEPHY/PDF/ausbildung/teilchendetektoren/VO-4-2018-SemiconductorDetectors.pdf )