## Slide 1: Needs of radhard studies: barrel HCal
Stefan Bathe
Megan Connors
TIC Meeting
December 11, 2023

## Slide 2: Readout Chain
H2GCROC3 (54 per half-barrel) + LED driver boards
One half-sector -> 54 H2GCROC3 boards (72 channels each). Cable SiPM’s out to end of barrel HCAL to keep accessible for maintenance.
RDO’s
Fiber(s) to DAM
~5m (Cu)
~3m (mcoax)
120 cables/half-sector

## Slide 3: Barrel Hcal Radiation exposure
Orders of magnitude lower dosage than fHCal
Anticipate testing for other subsystems will be sufficient

## Slide 4: Summary
Neutron fluence low enough that it is not an issue for SiPMs
  Neutron fluence lower than in sPHENIX
  In sPHENIX dark current increase after first year of running consistent with expectations
H2GCROCs should be radiation tested
  Participation in coordinated testing
RDOs have FPGAs, but sit well outside the detector
  No concern for single event upsets (SEUs)
Considering radiation test of spare sPHENIX scintillating tiles