## Slide 1: RHIC Run 16 Radiation Upsets
Kevin Brown
2016 RHIC Retreat
July 28-29, 2016

## Slide 2: Acknowledgements
Nick Franco, Bill Eisele
  Monitored Network problems
  Coordinated with controls HW
Controls HW (Charles Theisen, Ralph Schoenfeld)
  Monitor, maintain, & replace FEC’s
  Check in-ring fiber quality
John Morris
  Analysis scripts and web data pages for network and FEC reset statistics
Al Marusic, John Morris, Jim Jamilkowski
  ram pattern measurements now logged
  Watch FEC’s very closely
Roger Smith (JTM’s summer intern)
  Analysis of reset and memory pattern data
Angelica Drees
  Just a good resource – keeps close watch on losses
Kin Yip
  Simulations of beam loss and radiation environment
Peter Ingrassia – operations statistics

## Slide 3: Outline
History/Background
Alcove Network switch resets/failures
Memory pattern data
Mitigation strategies

## Slide 4: History
Radiation Upsets in Alcove equipment have been a problem since RHIC began operating
Problems have been tactically mitigated
  Going to Radiation resistant VME Power Supplies
  Using ECC memory in (all ps, not qd or inst) FEC processor boards
  Using MRAM for WFG boards
  ado cache data for alcove FECs is stored on file server - not on local RAM that is vulnerable to rad upsets

## Slide 5: Todays Vulnerabilities
Network switches require frequent resets and even fail (2 replaced in Run 14, one replaced in Run 16)
MADCs become corrupted and stop reporting
Alcove FECs & WFGs still fail and require resets at a higher rate than in other locations
QD & BPM FECs can still hang and require resets
UPS units in alcoves have failed (11C & 5C)
Fiber runs in RHIC tunnel darken
Digi TS need AC resets at times
VME PSs still fail at times (rare)

## Slide 6: Alcoves

## Slide 7: Equipment Layout in Alcoves
18 Alcoves in RHIC, 3 per ARC.
Two basic layouts – rack use is always the same
8
9
10

## Slide 8
Rack 8

## Slide 9: Network Switch & FEC Reset Data
FECs may be rebooted or reset for a variety of reasons - some not indicative of a problem with the FEC.
All FEC reboots/resets are counted but the reasons are only recorded when resets are performed with the “fit” application. The data collected only counts resets that appear to be associated with some kind of failure.
At times multiple resets are attempted (and counted in statistics) for a single problem.

## Slide 10
Run 14, 100 GeV/n Au-Au Alcove network switch radiation upset locations
60
36
48
24
12
0

## Slide 11
Run 16, 100 GeV/n Au-Au Alcove network switch radiation upset locations
60
36
48
24
12
0

## Slide 12
255 GeV p-p Alcove network switch radiation upset locations
12
7
2
0
10
5

## Slide 13
Run 16 averaged 2.67 resets/day
Run 14 averaged 1.8 resets/day
Run 11 averaged 0.5 resets/day
For 250 GeV p-p, average 0.15 resets/day

## Slide 19: Memory Upset Measurements
Logging data this year, starting in early Feb.
Using Ram Disks in Alcove PS FECs
Place 64 bit pattern repeatedly into 2 Mbytes of memory
Creates 262,144 samples per FEC
Patterns are read on down-ramp of every store
Almost always, changes are at the single bit level [that is: the number of bit changes is small compared to the sample set, so the probability of a single bit changing twice in a sample period is insignificantly small.]

## Slide 20: Correlation between Resets and Memory Upset Statistics

## Slide 22: Mitigation Ideas of the Past
Network switches that use ECC memory
  Costs are high, >$30k/switch
  Memory corruption is not the main problem
  Address corruption hangs the switch – addresses not in ECC
Shielding Alcoves?
  Kin’s simulations (2014) suggest reduction factors are small (reduction at most ½ with lot’s of shielding – not practical)
Could move sensitive equipment to “quiet” alcoves
  Some new equipment required & labor intensive
  Space is tight & distances long
Could move some network switches out of alcoves to service buildings
  Distances are large (~1400 ft)
  Technology issues need investigation
    Use copper cable instead of fiber?
    Need to use converters, which may be susceptible and may pose operational challenges.

## Slide 23: Improvements since 2014
Improved on the data collection to better monitor the “health” of the equipment in the alcoves.
  Automate & Log data from memory pattern scans
  Monitoring network statistics
Addition of the protection masks and moving the Experiment protection bumps led to noticeable changes, although Run 16 was still worse than Run 14 
Removed UPS units from some alcoves (during run).
Automated (Tape) mass rebooting FECs on down-ramp of every store.
  helps reduce impact of madc problems
  No clear evidence it reduces impact of rad upsets in FECs

## Slide 24: Future Possibilities
Small form factor network switches placed in shielded boxes or externally (commonly used in military)
  Can come NEMA rated
  Designed for harsh environments
  May be difficult to find good compatibility with existing hardware.
External NEMA rated enclosures for network switches & possibly other equipment [cost is roughly $2k per enclosure + installation]
  Cable runs ~200 ft, could be done with copper (avoids fiber transceivers in the tunnel)
  No tunnel access to service
Shield just the network switch in the alcove
Improve on reset strategies

## Slide 25: NEMA† Ratings for External Enclosures
† National Electrical Manufacturer Association (NEMA)

## Slide 26: Shielding Small devices?
Kin Yip is simulating how effectively a small device can be shielded inside an Alcove
If the results are encouraging, a test will be done in Run 17. [use Alcoves 7b or 9c for proton operations]
Where in alcove?

## Slide 27: Assume Alcove 7B
16 ft
17 ft
12 ft

## Slide 28: Summary
Single Event Upsets cause equipment in Alcoves to hang and fail – Run 16 had the highest number of upsets ever.
Mitigations taken to reduce upsets over the years have kept the impact to a manageable level, although vulnerabilities remain a concern
Most significant vulnerability is in network switch upsets
No easy solutions, but there are still things that can be done
  External enclosures
  E.g., Improve reaction using memory pattern data

## Slide 29: Backup/Auxiliary Slides

## Slide 30: Some Terminology
ECC memory: Error-correcting code memory
  Detects and corrects most common kinds of internal data corruption.
  Is immune to single-bit errors
  Makes use of additional circuitry that checks accuracy of data during I/O operations.
  E.g., data read from a word of memory will remain uncorrupted even if a single bit in that memory was flipped.
MRAM: Magneto-resistive random-access memory
  Non-volatile memory
  Data is not stored as electrical charge, but by magnetic storage elements (via two ferromagnetic plates), so works on spin, not charge.
Single Event Upsets, Single Event Latchups, Single Event Gate Rupture, & Single Event Burnouts
  radiation striking a sensitive node in a micro-electronic device
  Most common are upsets, which are not permanent damage
  Result is at least a single bit change

## Slide 31: History – 2004
Front End Processors
  Power 3E processors lacked ECC memory
  Some locations had CPUs with ECC memory
    1007C, 1009A, 1009C
  Began process of replacing select CPUs with MVME2112 processors, that have ECC memory
VME Chassis (250 in field, 40 in Alcoves)
  13 VME PS Failures in Alcoves (38%)
  3 VME PS Failures in Service buildings (<1%)
Collaboration: VME Chassis Rad Tested for LHC at CERN (Wiener Chassis now in use)
Began looking at Rad Resistant PSs = found one that performed well (Vicor PS now in use)

## Slide 32: V115 (WFGs)
Tried ECC memory in WFGs (in 2004)
  To replace 128K x 32 static ram
  Plugged into existing memory footprint
  Initially performed well in tests
  Didn’t perform as well as expected in alcoves
After 2004 switched to MRAM
Finished MRAM installation by 2011
In addition
  Alcove FECs (for PSs) were upgraded to use ECC memory
  Stopped using RAM disks to save files
  Code was modified to save 3 copies of data that had to remain in RAM disks (to avoid corruption)
  RAM disks for FECs that did not need them were removed (i.e., BPMs and QD FECs)