## Slide 1
ePIC Synchronization and Clock distribution
- William Gu’s exploration*
EIC beam (crossing) structure
Overall hardware design
Detailed signal implementations
Exceptions
Current status
To do
* Credits give to all the community

## Slide 2
EIC beam (crossing) structure
 | Electron Storage Ring (ESR) | Hadron Storage Ring (HSR) (Nb=290) | HSR (Nb=1160)
Circumference C [m] | 3833.940 | match Trev | match Trev
Revolution period Trev=C/c [µs] | 12.7886 |  | 
RF harmonic number h [-] | match HSR | 2520 | 7560
RF bucket spacing Tb=Trev/h [ns] NOT bunch spacing!!! | match HSR | 5.075 | 1.692
Number of bunches Nb | match HSR | 290 | 1160
Bunch spacing Tbun [ns] | match HSR | 40.599 | 10.150
Gap length [ns] | match HSR | 1015 | 1015
Beam crossing: 98.5MHz
Orbit period: 12.7886 µs
 | ESR | HSR
RMS bunch length sz [mm/ps] | 7-9/23-30 | 75-60/250-200
RMS momentum spread [10-4] | 5.8-10.9 | 10.3-6.8
RMS horiz beam size sx [um] | 100-250 | 
sz/sx ratio [-] | 28-90 | 240-750

## Slide 3
EIC beam (crossing) structure
1 2 3 4 5 6 7 8
3 4 5 6 7 8 9 0 1 2 3 4
5 5 5 5 5 5 5 6 6 6 6 6
1 1 1 1 1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1 1
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
2 2 2 2
1 1 1 1
7 8 9 0
5 5 5 6
1 2 3 4
1160 (all or 1/4 with beam)
100 (no-beam /gap)
Orbit period: 1260*10.150 ns = 12.7886 µs
The natural streaming readout time slice: N*12.7886 µs
Streaming Data
Beam crossing
Time Slice M+5
Time Slice M-1
Time Slice M+4
Time Slice M+3
Time Slice M+2
Time Slice M+1
Time Slice M
SRO data header:
Packet number,
Data source ID,
Starting orbit count
SRO data trailer:
Ending orbit count
Sync/Error/buffer status
Total word count
*If this is used, there will be less data overlapping in between the time slice (the overlap can still occur if the detector response time is longer than 1 µs). There will be easier synchronization check.

## Slide 4
2. Overall hardware design
GTU: Global Timing Unit
  control encoding, status decoding.
  The interface for machine clock source,
  Data acquisition control and monitor etc.
DAM: Data Aggregation Module:
  The clock/control fanout, and status/busy accumulation.
  local control over the RDO boards connected, though the main function of the DAM is for Data Acquisition.
RDO: optical interface of detector ReaDOut
  control decoding, status encoding.
  The clock/control interface to the front end electronics.
  Data collection from Frontend boards, and data transmission to the DAM
FEE:
  Detector dependent Front End / ASIC carrier boards.
GTU
Clock
Control
Status
DAM
DAM
RDO
RDO
RDO
RDO
Data Acquisition
DAM
RDO
GTU
ePIC
EIC/RF
Online computer
FEE
FEE
FEE
System Clock: 98.5 MHz (100MHz nominal)

## Slide 5
EIC
RF
in
EIC/ePIC clock & beam orbit info
Online computer
Run control
GT
DAM
(dRICH)
SFP
Clock buffers
RDO (TOF)
RDO (TOF)
SFP
DAM
RDO
RDO
DAM
RDO
RDO
Could be a separate clock fanout PCB, if needed
GTU
FPGA
DAM
1 : ~200
May be needed, RDO(TOF) , DAM(dRICH)
CLOCK
RunControl
STATUS
2.1 GTU
2. Overall hardware design

## Slide 6
2.2 DAM
RJ45
HDMI
(?)
PCIexpress 4/5x16
Clock
buffer
FPGA
Xilinx Versal
CLOCK
98.5MHz
RunControl
STATUS
GTU
100 GBE (400?)
RJ45
GigaBitEth
Fabric
Clock
RefClks
GTYs
(24/48)
TXs
RXs
FireFly
TX
FireFly
RX
RDO
RDO
Host Computer/DAQ
Network Switch/DAQ
RunControl
RDO/FEE config
Status merging
DataProcessing
2. Overall hardware design

## Slide 7
2.3 RDO
Optic transceiver
RX
TX
1:2 fanout
O1
O2
FPGA
GTY
RX
TX
Si53x5
O1
O0
O2
IN
RxRecClk
GENIO
FEB
Phase difference detection
Fiber
FEB
optional emergency circuit I2C
RDO
N* 98.5 MHz
197 or
98.5 MHz
control
ClkRef
pseudoClock
98.5 MHz
OUT
IN3
Zero Delay FB
DAM
2. Overall hardware design

## Slide 8
3. Detailed signal implementations
3.1 Clock Distribution
EIC, RF
GTU
RunControl computer
System clock
(98.5MHz)
Two-level fanouts
Beam orbit
Ethernet
DAM
Clock fanout
(optional jitter cleaner)
DAQ
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
Copper cable:
Additive Jitter <1ps
Phase: fixed
PCB and fanouts:
Additive Jitter <1ps
Phase: fixed
RDO
Clock recovery
(optional iitter cleaner)
Clock fanouts
Control
Config
DAQ
Optic fiber cable:
Additive Jitter <1ps
Phase: fixed
GTY Rec Clock:
Additive Jitter <3ps
Phase: stable, but NOT fixed;
TClink or dedicated clock from GTU
RunControl: Run_Start/Stop, Run_type, config, Reset, Synchronization, SRO time_start/stop, Trottling…
Status: Buffer busy, out of sync …
GTY
Control config, status
Host PC
TX/RX
RefClk
Beam Orbit synchronized RunControl
GTY
TX/RX
RefClk
RecClk
FEE/ASIC
3.2 RunControl and DAQ
RunControl: forward or ‘hijack’ the GTU control;
DAM, RDO, FEE/ASIC configuration, readout backpressure
Status: Buffer, sync, etc.
Config synchronized with beam orbit, FEE/ASIC readout and control
Status: Buffer, sync, etc.

## Slide 9
3.3: Synchronization
DAM/RDO to implement time measurement, so that RDOs can compensate the fiber length delay to within one clock period;
GTU/DAM/RDO to keep a 11-bit beam crossing counter (terminates at 1260), synchronization check with streaming readout time slice (start/stop) commands; online/offline check with beam orbit structure (collision or no collision);
RDO to keep a 5-bit (min. ~409ms), 21-bit (preferred, ~26seconds), or 32-bit (over 15 hours) beam orbit counter;
GTU and DAM should keep a larger beam orbit counter;
RDO to keep a 16-bit (min), or 32-bit (preferred) time slice counter. This counter should not overflow for a run (start/stop).
RDO should assert buffer high_marker no later than one orbit period before it is full and starts to lose data.
RDO starts a new data packet upon receiving time-slice_start, and end the current packet upon receiving time-slice_end or upon receiving a new time-slice_start.
RDO to hold data if the DAM is busy (potential buffer full), and the DAM to hold data if the host computer/Network switch is busy.
The GTU can record dead time by sending TimeSlice_end, and holding TimeSlice_start in responding to RDO busy.
RDO should generate one packet on every readout time slice. The RDO can discard detector data to avoid buffer overflow, or out of synchronization, but this occurrence must be recorded in the data package/trailer.
GTU
RDO
DAM
DAQ
Data Buffer ‘FULL’ backpressure
Status accumulation:
Data Buffer conditions, Out of Sync, Reset_request, etc.
Run_control:
SRO_time_start/stop, RESETs, etc.
3. Detailed signal implementations

## Slide 10
8-bit (8b/10b encoding) every beam crossing period (788 Mbps)
8-bit plus K-bit, Beam Orbit synchronized RunControl command
Downlink:
8-bit plus K-bit, DAM and the DAM connected RDO/FEE/ASIC status
Uplink:
3.4: Copper link between GTU and DAM:
3.4.2: signal#2, RunControl: GTU_TX  DAM_RX
3.4.3 signal#3, Status: GTU_RX  DAM_TX
3.4.1: signal#1, Clock: GTU_TX  DAM_RX
8-bit (8b/10b encoding) every beam crossing period (788 Mbps)
Three pairs of differential copper wires (LVDS?, RJ45 or HDMI?)
All these copper cables to be the same length (5 meter? Within the DAQ computer/DAM racks.
3. Detailed signal implementations
To use the FELIX (DAM) optical link (LTI/100GBE), the GTU would host multiple FPGAs with connections between FPGAs.
This will also disable the 100 GBE feature on the FLX182.
There will be clock recovery and RunControl commands alignments on the DAM. I believe that the simpler the better (more reliable)

## Slide 11
98.5 MHz clock, Serial speed at 1.97 Gbps, 3.94 Gbps, or 7.88 Gbps
RunControl, forward or “hijack” the GTU
RDO/FEE configuration from DAM
Downlink:
3.5: Fiber link between DAM and RDO:
3.5.1: DAM_TX  RDO_RX
One pair (two) of optic fibers (850nm Multimode), less than 150 meters
Fiber length/signal delay to be measured, and delay compensated on RDO
* 1.97 Gbps is required, if the VTRX+ is used on RDO.
* 7.88 Gbps may be able to shorten the RDO/FEE configure time, but the I2C clock may be the limiting factor.
3. Detailed signal implementations
RunControl (from GTU) is guaranteed every beamcrossing cycle (98.5MHz). It can be hijacked by the DAM for sub-system test
The RDO/FEE configuration depends on the specific DAM (which comes from the host computer). The available bandwidth is 788 Mbps, 1.97 Gbps, or 3.94 Gbps depending on the downlink speed.

## Slide 12
Uplink:
98.5 MHz clock (or maybe other frequencies) , Serial speed up to 12 Gbps
3.5.2: DAM_RX  RDO_TX
FEE data
64-bit
MUX
Status
56-bit + K-code
8B/10B encoding
98.5 MHz clock
* It is possible to use 64B/66B or other encoding for high efficient data link…, or higher clock frequencies
Data:
time-slice packaged data
Can have K-code package header/trailers
Status:
I2C/SPI returned data,
BUSY
Fifo/buffer status
……
The Data and Status are recovered by the FPGA’MGT
By DAM board
Higher priority
80-bit per clock cycle for 7.88 Gbps (Data, Status, or idle/no_useful_data)
3. Detailed signal implementations

## Slide 13
4. Exceptions
4.1 What if the TClink does not work here?
EIC/ePIC clock & beam orbit info
GT
DAM
(dRICH)
SFP
Clock buffers
RDO (TOF)
RDO (TOF)
SFP
DAM
DAM
GTU
FPGA
DAM
1 : ~200
CLOCK
RunControl
STATUS
Dedicated clock from GTU/Fanout to RDO via optic fibers
4.2 What if the DAM is too far away from GTU?
Use SFP transceivers (from GTU MGT) via optic fibers

## Slide 14
5. Current status
5.1 DAM: BNL FELIX card FLX182
Samtec FireFly, 4Tx/4Rx
Xilinx Versal Prime VM1802
Samtec FireFly,
2* 12Tx, & 2* 12Rx
Power management
Single +12V input
Clock management
Si5345s, oscillators…
PCIexpress
Gen4, 16 lanes
DDR4 memory
MTP, 4Tx/4Rx
LTI, 100 GBE
2* MTP, 12Tx/12Rx
RDO/FE
RJ45, 1000BASE-T
LEDs, USBs
LEMO_IOs
TRG, WR

## Slide 15
FLX182
XEM8320, Artix Ultrascale+
2x12 (MTP)  24x1 (LC)
1x24  3x8(MTP 12)
5. Current status
5.1 DAM: BNL FELIX card FLX182
Powered up as PCIe4x16 inside the computer;
Successfully loaded Jlab’s Readout on the GBE interface (standalone, without the PCIexpress or host computer);
Reconfigured the clock tree (Si5345), and generated ePIC 98.5MHz clock for the MGT RefClkIn;
Downloaded the ATLAS firmware, and compiled locally;
Modified the firmware for ePIC, and loaded the QSPI flash memory and the Versal FPGA;

## Slide 16
5. Current status
FLX182:
The only major limitation for ePIC clock distribution is the lack of external clock input to the Si5345.
Si5345
IN3±
IN2±
IN1±
IN0±
OUT9±
ZDM
XPIO±
OUT8±
OUT7±
OUT1±
OUT0±
MGT_REFclkIN
WR_OSC
100 MHz
SI_OSC
200 MHz
LEMO_IN
ADCMP561BRQZ
SN65LVDS100D
XPIn±
LEMO_IN
SN65LVDS1D
XPIn±
XPOut±
LEMO_OUT
SN65LVDT2D
Versal FPGA
Because of the (slow) buffers, the LEMO_IN/OUT may be used for RunControl/Status signals (788 Mbps), but not the dedicated CLOCK (~1ps jitter) (the red line above).
Cascade to next Si5345
5.1 DAM:
Current FLX182 clock diagram

## Slide 17
5. Current status
FPGA
Front panel connector
2:1 mux
Si5345
(ZDM)
FPGA
GT(204?)
RefClkA
RefClkB
INA±
INB±
IN0±
I/ObufDS
Clock_98.5MHz, ~ps jitter
Control, ~gbps
Status, ~gbps
RxRecClk
IN2±
WR osc.
2:1 mux
INA±
INB±
SEL
RxUsrClk
Existing on FLX182
Needs be added on FLX155
To request the addition on FLX155 (FELIX board with Versal Premium VP1552, 48-channel)
Keep the MGT quad fiber connection (100 GBE), and other common FELIX functions (PCIe, etc)
? Should we ask for VP1202 compatibility? cheaper, but 24-channels only.
5.1 DAM:
FLX155 can be used as ePIC DAM

## Slide 18
5. Current status
Working on the schematics
Fully assembled boards are expected in the summer of 2024
5.2 RDO, pre-prototype

## Slide 19
6. To Do
6.1 TClink (trick) implementation on the DAM (FLX182/FLX155)  RDO (preprotype)
6.2 Define the data format
  6.2.1 define the 8-bit RunControl commands,
  6.2.2 define the status word,
  6.2.3 define the (DAMRDO) configure protocols,
  6.2.3 define the data format,
6.3 Subsystem DAQ setup (one DAM plus many RDOs)
6.4 GTU design, and the full system setup

## Slide 20
Backup Slides

## Slide 21: Artix Ultrasale+ GTY Recovered clock (RxRecClk, ClkRef_out), with regular 8b/10b coding, SFP+, 7.88gbps
All eight bytes are regular data (8b/10b encoded)
RxRecClk: TIE σ = 3.2 ps, Phase stable (aligned with source clock) @ 40 µs
Period
TIE
Frequency
Through Avago AFBR-710SMZ optic transceivers and a short multimode LC fiber (850nm)

## Slide 22: Artix Ultrasale+ GTY Recovered clock (ClkRef_out), with regular 8b/10b coding, Single Mode Fiber, 7.88gbps
All eight bytes are regular data
RxRecClk: TIE σ < 3 ps, Phase stable @ 4 µs,
Rising edges, or Falling edges
RxRecClk_P, or RxRecClk_N
30 meter fiber, or 609 meter fiber
TIE, Ch#3
Period
TIE, ch#4
Through FS.COM SFP-25GLRL-31-4 “single mode, 25G, 1310 nm, 2 km” optic transceivers,
a short single mode LC fiber, 30 meters
A long single mode LC fiber, 609 meters
Original Clock (triggered 4us earlier)
RxRecClk _P, _N crossing
40 ps