## Slide 1: Streaming Readout WG Meting 12/19/23 – Calibrations
Agenda
Announcements
  Wed 1/10/24 – Collaboration Meeting Workfest, Joint meeting of SRO and Electronics & DAQ
  Friday 1/12/24 – Software & Computing report, Electronics, Readout & DAQ report
Introduction
Tracking detector calibration and alignment (Joe Osborn)
TOF T0 and calibration plans (Zhenyu Ye)
Discussion

## Slide 2: Why talk about calibrations now?
A major goal of the offline component of the SRO is to do real-time final reconstruction
  ~3 week latency
  Bypass tape storage for reconstruction and use it only for archive
Calibrations are one of the biggest obstacles because they often take a long time
It is premature to fully define calibrations
  Detectors still being designed & characterized
  Calibrations often have an element of debugging: they can be responses to discovered problems
But…. we will need significant automation, support, and prior understanding of the calibrations to achieve real-time final reconstruction
  Strategy: go over some examples (tracking & TOF) and use them to think about the kinds of support we need to build into the SRO

## Slide 3: Organizing the calibrations
I suggest organizing the calibrations according to the location they need to be applied
Where | Examples
Detector | HV adjustments for gain corrections
Electronics (ASICS, FEB, RDO) | Thresholds, pedestals, timing offsets
Echelon 0 (prior to feature identification) | Slewing corrections, gain corrections (relative)
Echelon 1 (prior to reconstruction) | Global alignments, gains, slewing, timing, acceptance, beam effects…
Echelon 2/3 (prior / during analysis) | ???
Data Quality
Calibration Quality
Other important organizational ideas are where the calibrations are performed and what the detector settings / beam characteristics are required to take the data
Calibration | Special Run | Where Performed
Pedestals | No pedestal subtraction, black events, no beam | Automated in DAQ
Calibration systems (diodes, charge injection, etc…) | Triggered by DAQ, marked times or special runs | DAQ issued, special config?
?? | Low beam currents | ??
?? | Reduced bunch counts | ??
?? | Vernier scans | ??

## Slide 4: Other questions to keep in mind
  Is external data needed (collider information, slow controls, etc…)
  Dependency trees for detector calibrations/calibrations within detectors
  Operation scheme
    Special runs
    Continuous iteration
    Deployment method
  How much data is needed
  Does it need human intervention, or can it be done automatically
    If human intervention is needed, is there support from the SRO group that can make this human intervention easy (and fast)
  Mechanics for deployment particularly for off-site calibration
    Lustre vs Data Carousel
  If ML to be used, what support must we provide? ML packages? Training data sets? Convergence tracking?