## Slide 1: Ring Finder Algorithm for mRICH Detector Using Circular Hough Transform
Cheuk-Ping Wong
Georgia State University
2016-08-15

## Slide 2: Motivation
Quantitative data analysis on beam test data and on Simulation result
  Number of Cherenkov photon detected per event
    Both signal and background
  Cherenkov ring radius (Ring finder algorithm required)
  Performance of Fresnel lens
Method
  Ring Finder Algorithm
  Maximum Likelihood

## Slide 3: Motivation
Obtain the most likely circle : center (a,b) and radius r, from limited information

## Slide 4: Circular Hough Transform
Start from the basic A circle can be formed with at least 3 points: Find out all possible Circles
Pick any three hits from a list of hits
And try all possible three-hit combinations.

## Slide 5: Circular Hough Transform
Then find out which circle passes through most hits.
2 hits
1 hit
0 hit
Signal Cherenkov photons
Noise photons
Blue ring – 5 hits
Green ring – 4 hits
Orange ring – 10 hits
3 hits

## Slide 6: Assumptions
There is only one incident particle per event
  Only one Cherenkov ring per event, that is (a,b,r) is unique
Number of background hit is much lower then signal hits in each event
Hit position = center of pixel

## Slide 7: Drawback of CHT
Then there are up to nC3 Possible circles!!! Let’s say there are 10 hits in one event, there are 120 combinations.

## Slide 8: Combinations restrictions
Combinations restrictions :
Any two hits that are on the same pixel
All three hits are collinear
1
2
3
4
5
a
b
c
d
e

## Slide 9: Drawback of CHT
Combinations restrictions :
Any two hits that are on the pixel
All three hits are collinear
1
2
3
4
5
a
b
c
d
e

## Slide 10: CHT Implementation on mRICH
Error/tolerance
ring information (a,b,r) from picked hits
Distance (d) from other fitting hits to (a,b)
If agrees with r , the hit fits on the possible ring.

## Slide 11: CHT Implementation on mRICH
Error/tolerance
ring information (a,b,r) from picked hits
Distance (d) from other fitting hits to (a,b)
If agrees with r , the hit fits on the possible ring.
Center of the pixel

## Slide 12: CHT Implementation on mRICH
Error/tolerance
ring information (a,b,r) from picked hits
Distance (d) from other fitting hits to (a,b)
If agrees with r , the hit fits on the possible ring.

## Slide 13: CHT Implementation on mRICH
Weighting
Fill every combination (a,b,r) with voting number n
3D (a,b,r) distribution
Data of the densest bin in the histogram = most possible ring

## Slide 14: CHT Implementation on mRICH
Weighting
Fill every combination (a,b,r) with voting number n
3D (a,b,r) distribution
Extract data of the densest bin in the histogram  most possible ring

## Slide 15: Simulation Result Single 9GeV Pion
9GeV single pion launched perpendicularly toward the center of the detector
(Quantum efficiency applied)
Most Possible Ring

## Slide 16: To do
CHT Implementation on Beam test data analysis

## Slide 17
Back Up

## Slide 18: Simulation Result 9GeV Single Pion
9 GeV single Pion launched perpendicularly at (x,y)(-24,-24)mm
The ring finder algorithm does work well if background hits are outnumber signal hits
(Quantum efficiency applied)
Same event

## Slide 19: C.H.T. Implementation on mRICH
Weighting
Fill every combination (a,b,r) with voting number n
3D (a,b,r) distribution
Extract data of the densest bin in the histogram  most possible ring
Thus, final result (a,b, r) is averaged