## Slide 1: 26th Annual Accelerator Test Facility (ATF) Users' Meeting AE108 - Development of wavelength conversion techniques for generation of coherent radiation at the XUV to LWIR
March 26th, 2024
W. Li1, R. Kupfer2, F. Wang1, J. Wishart1, M. Babzien1, M. Polyanskiy1*, I. Pogorelsky1, T. Rao1, L. Cultrera1, N. Vafaei-Najafabadi1,3, M. Palmer1
1Brookhaven National Laboratory, 2Soreq Nuclear Research Center,
3Stony Brook University, *PI
Accelerator Facilities Division
Funding: BNL LDRD-21-001 and U.S. DOE Office of Science DE-SC0012704 (received)

## Slide 2: Experimental goals
Upgrading ATF CO2 laser
  9.3 μm: better LWIR seed  shorter pulse length
  4.3 μm: optical pumping  much higher repetition rate
EUV for imaging and lithography
  HHG scales with wavelength: natural fit for ATF
  With CO2 laser, potentially extend to zeptosecond hard x-rays
Seed
few mJ <500 fs 9.3 µm
10++ TW ~500 fs
Pump
100s J, < 1 µs, 4.3 µm
CO2 amplifier
Photo credit: ASML
Popmintchev, Nat. Photonics 4, 828 (2010)
CO2 laser
Accelerator Facilities Division

## Slide 3: Mid- and long-wave infrared
Commonly available lasers are limited to specific wavelengths
Generating mid- or long-wave infrared usually requires relatively inefficient OPA
Is there a better option?
Photo credit: Edmund Optics
Accelerator Facilities Division

## Slide 4: Raman + DFG
‘Cheap’ high energy laser source ωp
Raman Converter
Residual pump ωp
Converted pump ωp- ωtarget
Nonlinear crystal
Residual pump ωp
Converted pump ωp- ωtarget
ωtarget
Typical Raman shifts are on the order of 1000 cm-1
Perfect for generating LWIR!
Raman Scattering 
in
out
ΔE
ωpump
ωsignal
ωDFG
Difference-frequency generation (DFG)
Accelerator Facilities Division
Diagrams adapted from Welch, Opt. Express 26, 5145-5163 (2018)

## Slide 5: Pump (4.3 μm) generation in ionic liquid
Artificial salts that are liquid at room temperature
Can be designed to have specific properties
Settled on EMIM DCA
  Transparent at pump and Stokes wavelengths
  Peak Raman cross section at desired shift
  High viscosity (suppressing Brillouin scattering)
  Good stability
Plots from Kupfer, Phys. Rev. Applied 19, 014052 (2023)
High efficiency
Good spectrum
Raman shifts of selected ILs
Accelerator Facilities Division

## Slide 6: Open questions about ionic liquids
Cost effectiveness: how much liquid is necessary?
Repetition rate?
Other viable ionic liquids?
~300 ml
~30 ml
Original tube
New tube
Accelerator Facilities Division

## Slide 7: Ionic liquid test stand
Runs in parallel with Ti:S operations
Accelerator Facilities Division
Nd:YAG
(2nd harmonic)
Ionic liquid tube
Diagnostics

## Slide 8: Repetition rate scaling
Glass tube saturates quickly at 12 Hz, compared to metal tube
Significant improvement at 1 Hz
Thermal effects: thermal conductivity of EMIM-based ionic liquids is around 0.2 W/m·K* (water is about 0.6 W/m·K)
For high repetition rates, need active cooling
*Fröba, Int. J. Thermophys. 31, 2059-2077 (2010)
Accelerator Facilities Division

## Slide 9: Alternative ionic liquids
Now testable due to smaller requisite volume
~2200 cm-1 Stokes shift
  BenzMIM DCA, EMIM TCM: absorption at 532 nm too high
  No visible Stokes peak/burned liquid
~1000 cm-1 Stokes shift
  BuPy NTf2
  Low conversion efficiency
Accelerator Facilities Division

## Slide 10: High harmonic generation
Popmintchev, Science 336, 1287-1291 (2012)
Intense laser field tunnel ionizes gas
Free electron is ponderomotively pushed away from ion
Laser field changes sign and electron collides with ion
Ponderomotive nature of interaction causes longer pump wavelengths to lead to shorter harmonic wavelengths
Popmintchev, Nat. Photonics 4, 828 (2010)
Accelerator Facilities Division

## Slide 11: HHG apparatus
Full HHG apparatus
Gas cell schematic
Kr, Ar
Accelerator Facilities Division
Ti:S
XUV

## Slide 12: HHG commissioning
First HHG signal observed
Spectrometer camera had problems, manufacturer is repairing
Accelerator Facilities Division

## Slide 13: Plans for next year
Employ DFG to produce the seed and pump wavelengths
  DFG crystal acquired for both 4.5 μm and 9.2 μm
Improve HHG apparatus performance with repaired camera
Accelerator Facilities Division
BGS crystal for 9.2 μm
LNB crystal for 4.5 μm
UV spectrometer camera

## Slide 14: Products delivered
Conference proceedings:
  W. H. Li, R. Kupfer, M. Babzien, L. Cultrera, M. N. Polyanskiy, I. V. Pogorelsky, T. Rao, N. Vafaei-Najafabadi, F. Wang, J. F. Wishart, and M. A. Palmer. "Raman Conversion in Calcite Crystals for Seeding CO2 Lasers," CLEO: Fundamental Science, San Jose, CA (USA), May 7-12, 2023
Conference presentations:
  R. Kupfer, F. Wang, J. F. Wishart, M. Babzien, M. N. Polyanskiy, I. V. Pogorelsky, W. Li, T. Rao, L. Cultrera, N. Vafaei-Najafabadi, and M. A. Palmer. "Raman Wavelength Conversions in Ionic Liquids," CLEO: Fundamental Science, San Jose, CA (USA), May 7-12, 2023
  W. H. Li, M. Babzien, L. Cultrera, R. Kupfer, I. V. Pogorelsky, M. N. Polyanskiy, F. Wang, J. F. Wishart, T. Rao, N. Vafaei-Najafabadi,, and M. A. Palmer. " Prospective methods for generating sub-picosecond long-wave infrared lasers for advanced accelerators," Physics and Applications of High Brightness Beams, San Sebastian, Spain, June 19-23, 2023
Accelerator Facilities Division

## Slide 15: Backup slides
Accelerator Facilities Division

## Slide 16: EMIM DCA transmission spectrum
Problem for using Nd:YAG fundamental
Absorption peak from overtones of aliphatic C-H bonds
Deuteration should shift this peak without affecting the Stokes shift, which comes from C-N triple bonds
Accelerator Facilities Division

## Slide 17: HHG Feasibility for CO2
Simple model of HHG yield for unit interaction area and unit time given by equation
We can compare to Popmintchev, Science 336, 1287 (2012), using a 3.9 μm pump, where we target the same harmonic wavelength (~1 keV)
  Their yield was photons/shot in a bandwidth around 1 keV
goes as , but the peak power of the CO2 laser is much higher with a longer pulse length, and the optimal phase matching intensity is lower, so the interaction area is 20 times larger and the interaction time is also 20 times longer, resulting in a higher overall yield for the CO2 laser
Primary challenge will be developing a gas cell that can support the necessary pressure (several atm)
Accelerator Facilities Division

## Slide 18: Slides for Program Advisory Committee

## Slide 19
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800
FWHM Bandwidth | nm | 20 | 13 |  | 
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 75
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 15
Energy to Experiments | mJ | >4.9 | >80 |  | 
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 20: Special Equipment Requirements and Hazards
Ti:Sapphire and Nd:YAG Lasers
  We will be running the ionic liquid conversion experiment with the Ti:Sapphire pump YAG in parallel with other Ti:Sapphire operations.
  We will require the Ti:Sapphire laser for HHG commissioning and the frequency conversion experiment to 9.2 μm.
Hazards & Special Installation Requirements
  We will require a vacuum chamber and associated pumping to be installed in the CO2 room for the HHG gas cell. The gas cell itself will be fed with lecture bottles.

## Slide 21: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 40 | 80
Laser* + Electron Beam |  | 
CY2024 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Areas) | 40 | 80
Laser* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Total Time Request for the 3-year Experiment (including CY2024-26)