## Slide 1
PI: A. Zholents, APS/ANL
ATF user’s meeting, March 27, 2024
Continuation of the ATF experiment 306051
Funded by LDRD at ANL
S. Lee*, A. Nassiri, M. Qian, B. Popovich, S. Sorsher, K. Suthar, E. Trakhtenberg, G. Waldschmidt, J. Xu (APS/ANL)
S. Siy**, N. Behdad, J. Booske (University of Wisconsin)
M. Fedurin, K. Kusche, W. Li (ATF/BNL)
*) currently at LANL
**) currently at Quaise Energy
CHARACTERIZATION OF THE COLLINEAR WAKEFIELD ACCELERATOR MODULE
Closeout of the experiment AE120

## Slide 2
1
2
3
e-
Accelerator module installed inside the experimental chamber
Copper structure with the corrugated waveguide in the middle
Transition section between accelerator modules
Cylindrical waveguide adapter
0.3 m
Setup 1
Setup 2

## Slide 3: Motivation: a multi-user hard x-ray FEL facility
E-gun
SRF, 650 MHz
10 nC, 200 kHz,
2 mA, 2 MW
180 GHz, 4.5 GeV
1 GeV
End stations
Accelerator for
drive (10 nC) and witness (0.15 nC) bunches
Array of structure-based wakefield accelerators
FELs, x-ray beamlines and end stations,
20 kHz rep rate
drive
G. A. Voss and T. Weiland, DESY M-82-10, 1982
witness
<<
2 mm
A. Siy et al., PRAB, December, 2022
20.86mm
No use of electricity
324 MV/m
94 MV/m on axis
610 kA/m
340 mm

## Slide 4: Accelerator module components
Three transition sections were built for ATF experiment
Corrugated waveguide
e-
Two 0.3 m long copper structures were built for ATF experiment
0.5 m
The quadrupole wiggler
The transition section contains:
TM01 mode output coupler
TE11 mode output coupler (IOM)
Bellows

## Slide 5: Accelerator module components (2)

## Slide 6
A schematic of the experiment at ATF
End tip
BPM
9. TPX window
10. BLIS Michelson interferometer
11. LHe bolometer
13. Energy slit
14. HeNe alignment laser
16. Faraday cup
slit action

## Slide 7
BLIS interferometer
Wire grid polarizer

## Slide 8
Experimental setup at ATF for characterization of the transition section attached to the 0.3 m long CWG
Transition section (TS)
CWG
TM01 coupler
IOM
The beam is offset vertically by -150 mm
TE11 coupler
The goal of the experiment was the characterization of the TS
Measurement:
Calculation:
without polarizer
TE11
Sub-THz light out
where I is a peak amplitude in the spectrum
TM01
with polarizer in vertical position
locally excited

## Slide 9
Horn antenna of TM01 fundamental mode coupler
Horn antenna of TE11 coupler called Integrated Offset Monitor (IOM)
place holder for bellows
Aluminum mandrel
All four sides have horn antennas on
Measured energy of the sub-terahertz wave pulses radiated by TM01 and HE11 horn antennas.
Measurement of isolation efficiency

## Slide 10
Measured energy of the sub-terahertz wave pulses radiated from the end piece.
End piece
Off-axis parabolic mirror
Measurement of isolation efficiency
The end piece is a cylindrical waveguide with a 45o cut at the end.

## Slide 11
Results
**) Note: TM01 mode Čerenkov radiation splits in four directions in TM01 coupler and TE11 mode Čerenkov radiation splits in two directions in TE11 coupler.
*) units V/nC2
Result
CWG 1 :
TM01 coupler captures (97.9±0.5)% of the TM01 mode of Čerenkov radiation,
TE11 coupler captures (97.1±1.1)% of the HE11 mode of Čerenkov radiation.
CWG 2 :
TM01 coupler captures (95.9±1.6)% of the TM01 mode of Čerenkov radiation,
TE11 coupler captures (95.8±3.0)% of the HE11 mode of Čerenkov radiation.
Bolometer measurements normalized on the square of the bunch charge

## Slide 12
The experiment was completed achieving all goals.
Postprocessing of measurements determined that they are in good agreement with design specifications.
Acknowledgments
We are grateful to the ATF staff for their valuable help in the experiment.
We are grateful to Mark Palmer for his unwavering support for the experiment and for accommodating many scheduling constrains.
Summary

## Slide 13
Invited Talk:
  May 2023, “Fabrication and testing of corrugated Waveguides for a Collinear Wakefield Accelerator”, A. Zholents et al., Int. Part. Acc. Conf. 2023.
Future Invited Talk:
  August 2024, “Fabrication and Beam Testing of a 180 GHz Colinear Wakefield Accelerator”, B. Popovich et al., Linac Conf. 2024.
A student was trained and obtained a Ph.D.
Publication in preparation:
Impact associated with this experiment and development

## Slide 14
The development of the corrugated waveguide-based collinear wakefield accelerator module marks a significant advancement toward realizing a compact hard x-ray free-electron laser (FEL) facility. This achievement encompasses successful demonstrations of key accelerator and FEL components:
A 30 cm long robust strong-back structure designed to firmly hold and efficiently cool the corrugated waveguide.
Sub-terahertz frequency electromagnetic couplers employed for the extraction of fundamental mode power and precise beam offset diagnostics.
Implementation of high-field gradient quadrupoles crucial for beam guidance and effective suppression of beam breakup instabilities.
Deployment of a compact, small gap force neutral adjustable phase undulator (FNAPU) for enhanced FEL performance.
All structures and couplers underwent rigorous testing at the microwave laboratory at ANL, followed by validation with electron beam experiments at the Brookhaven National Laboratory's Accelerator Test Facility. Magnetic measurements were conducted at ANL to characterize the quadrupoles and a prototype of the quadrupole "wiggler," yielding results in excellent alignment with design specifications. The prototype FNAPU was fabricated. Its performance characterization is in progress.
The comprehensive series of tests and validations revealed a remarkable consistency between actual performance and anticipated design parameters, underscoring the robustness and reliability of the concept of the corrugated waveguide-based wakefield accelerator for future applications in FEL technology.
Impact associated with this experiment and development