## Slide 1: High-efficiency laser-driven electron accelerator ATF experiment AE121
PI: Matthias Fuchs,
Ethan Welch, Kyle Jensen, Tian Hu, Shao-Xian Lee, Alexander Saw, Joseph Natal, David Squires, Ping Zhang, Brad Shadwick
University of Nebraska – Lincoln (UNL)
ATF Users' Meeting, 27. Mar 2024
funding: DOE-EPSCoR (HEP), DE-SC0021132 (received)
mfuchs@unl.edu

## Slide 2: Experiment Goals
Investigate a novel laser-plasma electron acceleration mechanism to relativistic energies based on Stimulated Raman Scattering (SRS)@quarter-critical plasma density “Parametrically-excited Laser-Plasma Acceleration PEPA”
Generate ultrashort, high-current electron beams
  charge: tens of nC !!, energy: up to 10 MeV
  High laser-to-electron efficiency (>16% !!)
  accelerating gradients >1 TV/m (for 0.8 µm laser); ~200 GV/m for 10 µm laser expected
  Highly relaxed restrictions on laser pulse duration (unlike bubble regime, can be several plasma wavelengths long, i.e., picoseconds for CO2 laser)
Interaction widely unexplored in gas jets and at relativistic laser intensities, specifically for electron acceleration
Fundamentally different from self-modulated laser-wakefield acceleration
mfuchs@unl.edu

## Slide 3: 2D PIC Simulations
a0 = 0.5
density << ¼ ncr (kl/kp = 20)
density @ ¼ ncr (kl/kp = 2.25)
laser B field
(normalized by kp)
plasma density (normalized by peak)
density 2D
snapshot

## Slide 4: Experiment: Dec 4 – 22, 2023
Collaborators
  Rafal Zgadzaj (UT Austin)
  Apurva Gaikwad (Stonybrook)
  ATF team: Thank you!!
not on picture:
- Joseph Natal
- David Squires
- MF

## Slide 5: Experiment Overview: Setup
mfuchs@unl.edu
Magnet and Stage
Stage
LANEX
OAP
Jet
Optics and stage
Optics and stage
ATF Rectangular Chamber’s Current Setup:
ATF e-beam
Laser-driven e-beam

## Slide 6
mfuchs@unl.edu
Jet
ATF e-beam
Laser-driven e-beam
Experiment Overview: Setup
gas jets: 80 / 150 µm nozzle

## Slide 7: Experimental Results
mfuchs@unl.edu
78 -micron nozzle
preliminary
charge vs plasma density
electron energy vs plasma density
filtered in laser energy [2 to 4 J]

## Slide 8: Experimental Results
mfuchs@unl.edu
150-micron nozzle
preliminary
charge vs plasma density
electron energy vs plasma density
filtered in laser energy [2 to 4 J]

## Slide 9: Transverse e-beam diagnostic
Formation of bubbles above nozzle
0 ps
60 ps
330 ps
405 ps
480 ps
240 ps
preliminary
P = 50 psi, 150 µm nozzle

## Slide 10: Plan/Schedule (3 years)
2022 23: First investigation of high-efficiency laser-driven é acceleration near the quarter-critical plasma density at LWIR wavelengths - ✓ First results on LWIR-driven é acceleration using near ¼ ncr - ✓ Measure dependence on laser parameters (intensity, pulse energy, pulse duration) - ✓ plasma parameters (plasma density, density profiles incl. ultrathin gas jets with width down to a single plasma wavelength, different plasma gradients). - The experiments will be supported by simulations.
2023 24: Investigation of the plasma wave dynamics using a transverse probe pulse and incorporation of ultrathin gas jet into longer lower-density jet as electron injector
2024 25: Further investigation and optimization of two-stage electron injection and acceleration
mfuchs@unl.edu

## Slide 11: Plan/Schedule (3 years)
2024: Systematic study of PEPA regime and investigation of plasma wave dynamics using a transverse probe - systematic study of electron acceleration in PEPA regime for different plasma density profiles with a length down to only a few plasma wavelengths -> will allow direct comparison to 0.8 µm data to identify scalings - plasma wave dynamics will be investigated for different LWIR intensities from well-below to well-above wavebreaking using -> transverse electron beam diagnostic (adapt TEM grids from Navid) -> transverse optical coherent Thomson scattering probe (using Ti:Sa) - The results of years 2023 and 2024 will be used for the dissertation of graduate student Tian Hu.
2025: Further investigation and optimization of electron beam parameters - study of electron acceleration ranging from the quasi-linear to the highly nonlinear regime. - optimization of electron beam parameters using controlled electron injection -> doping with high-Z molecules -> ioniziation injection with Ti:Sa laser - optimization of electron laser-to- electron beam efficiency
mfuchs@unl.edu

## Slide 13
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 |  | 50-65
Bunch Charge | nC | 0.1-2.0 | Not critical, <1 ps bunch duration | 
Compression | fs | Down to 100 fs (up to 1 kA peak current) |  | <1 ps
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) |  | 30 µm
Normalized Emittance | mm | 1 (at 0.3 nC) | As low as possible to have small spot size and divergence@IP | 
Rep. Rate (Hz) | Hz | 1.5 |  | Same as CO2 laser
Trains mode | --- | Single bunch |  | Single bunch
Electron Beam Requirements: Transverse probe

## Slide 14
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 
 | Peak Power | GW | ~3 |  | 
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | Not critical
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 2 | ~5 TW operation is planned within the next year (requires further in-vacuum transport upgrade). A 3-year development effort to achieve >10 TW and deliver to users is in progress. | 2 TW, ideally more
 | Pulse Mode | --- | Single |  | single
 | Pulse Length | ps | 2 |  | 2 ps, ideally shorter
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | 5J, ideally more
 | M2 | --- | ~2 |  | 2
 | Repetition Rate | Hz | 0.05 |  | 0.05 Hz (depending on diagnostics)
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | Linear
CO2 Laser Requirements

## Slide 15
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800
FWHM Bandwidth | nm | 20 | 13 |  | 20
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 50
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 
Chirped Energy | mJ | 10 | 200 |  | 
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 20
Energy to Experiments | mJ | >4.9 | >80 |  | 
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 
Energy | mJ | 0.5 |  | 
Pulse Width | ps | 10 |  | 

## Slide 16: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam | 2 days* | 2 weeks
NIR Laser | 1 day* | 1 weeks
LWIR Laser | 3 days for setting up experiment* | 4 weeks
CY2024 Time Request
Capability | Setup Hours | Running Hours
Electron Beam | 5 days | 3 weeks
NIR Laser | 3 days | 3 weeks
LWIR Laser | 5 days | 8 weeks
Total Time Request for the 3-year Experiment (including CY2024,25)
*if we can use existing setup in rectangular chamber

## Slide 17: Special Equipment Requirements and Hazards
CO2 Laser
  on-target laser intensity of at least 2x1016 W/cm2 (normalized vector potential of a0>1)
  pulse duration 2 ps, ideally shorter
  f/#2 focusing; softer focusing acceptable as long as a0>1
  on-target laser diagnostics (spot size, pulse duration, pulse energy)
  on-shot spectrum of transmitted CO2 pulse if possible, ideally also 3/2
Interaction Region
  Laser-plasma imaging setup
  Lanex phosphor screen for electron detection (can bring if needed)
  Imaging optics/camera to observe Lanex screen (can bring if needed)
Hazards & Special Installation Requirements
  Generation of ionizing radiation
  request translation stages in-vacuum for positioning of target, diagnostics (can bring if needed)
  request dipole magnet for electron spectrometer (can bring if needed)
  request He or H2 gas line for gas jet and HV feedthrough for driver (will bring own gas jet and HV driver for gas nozzle)
mfuchs@unl.edu