## Slide 1
Toward bubble-regime CO2-laser-driven
wakefield acceleration*
ATF User’s Meeting
26-28 March 2024
PI: Mike Downer, University of Texas at Austin
Collaborators:
University of Texas at Austin:
Faculty: M. C. Downer
Research Scientist: R. Zgadzaj
PhD students: Y. Cao, B. Dinh,
T. Araujo
Stony Brook University:
Faculty: Navid Vafaei-Najafabadi
Roman Samulyak
V. N. Litvinenko
Postdoc: N. Pathak
PhD Students: A. Cheng, A. Gaikwad,
B. Romasky, E. Trommer
Brookhaven NL:
ATF Director: M. A. Palmer
Research Scientists: M. Babzien,
M. Fedurin, R. Kupfer, K. Kusche,
W. Li, I. V. Pogorelsky,
M. N. Polyanskiy
Main Group Funding: US Department of Energy grant DE-SC0014043 (received thru 2025)
Additional Individual Support: DE-SC0011617 (UT-Austin); DE-SC0012704 (BNL)
1
UCLA:
Faculty: C. Joshi
*
optical diagnosis emphasis (complementary to Navid’s electron radiography emphasis)

## Slide 2
Goal: develop LWFAs that routinely produce e-beams
with ∆Ee/Ee and ℇn low enough to drive XFELs
The Proposed Project builds upon AE71 and AE95 success.
1) Large plasma bubbles (Rb ≳ 0.3 mm)
⇒ ne ≲ 1016 cm-3
2) External injection of low ∆Ee/Ee, low ℇn e-bunches
Key ingredients:
*
**
**
Synchronized, compressed ATF linac bunches uniquely enable 1st-generation experiments.
Efficiently excited by LWIR laser pulses uniquely realizeable at ATF
*
• Pogorelsky et al., Phys. Rev. Accel. Beams 19, 091001 (2016);
Kumar et al., Phys. Plasmas 28, 013102 (2021)
Project # | CO2 laser parameters | Main results
AE-71 | 2 J, 4 ps, 0.5 TW, 10.3 µm | • Generation, characterization of self-modulated (SM) wakes. No electrons.
AE-95 | 4 J, 2 ps, 2 TW, 9.2 µm | • Self-injected MeV electrons produced at ne ≳ 3 × 1016 cm-3 • Quasi-monoenergetic, collimated features observed.
Proposed Project | 5-20 J, < 2 ps, 5-20 TW | • Excite, characterize Rb ~ 0.3 mm bubbles at ne ~ 1016 cm-3 w/o self-injection • Inject e- from ATF linac, characterize ∆Ee/Ee and ℇn
[1] Predicted by Kumar et al., Phys. Plasmas 26, 083106 (2019)
[1]
[2] Zgadzaj et al., Nat. Comms., in press (2024)
[2]
2

## Slide 3
Year 1-2 Scientific Goals
1) Discover low-ne, high-PL limits of self-injected LWIR-driven WFA.
• Can we reach the full bubble regime while still self-injecting?
• In AE95 (4 J, 2 ps) we observed collimated quasi-monoenergetic electrons only at ne = 4 × 1017 cm-3.
We generated electrons down to ne = 3 × 1016 cm-3, but did not have time to spectrally analyze them.
Will quasi-monoenergetic component strengthen for ne < 4 × 1017 cm-3 and PL > 2 TW?
Constraints: • CO2 laser at or near current parameters: (4 – 10 J, 2 ps, 2 - 5 TW)
• No linac e-beam needed (Navid’s group is developing e-beam probes)
• Ti:S probe laser at current parameters
• Use existing AE95 infrastructure (gas jet, magnetic spectrometer, etc.)
4 × 1017 cm-3
3 × 1016 cm-3
3 × 1015 cm-3
2 ps
10 wake periods
3 wake periods
4 J
2 ps
4-6 J
2 ps
10 J
1 wake period
• Widen experimental conditions: H2 → He target; lin → circ pol drive pulse; downramp & ionization injection
• Understand self-injection limits thru simulations (with Samulyak).
UTexas team: Dr. R. Zgadzaj, PhD
student B. Dinh
3

## Slide 4
2) Upgrade optical diagnostics of wakes in low-ne plasma
Year 1-2 Scientific Goals (cont’d)
(complement e-beam probes that Navid’s group is leading)
1) Apply collective Thomson scatter (CTS) probe during e-
acceleration (AE95: only empty wakes probed) ⇒ observe
beam-loading effects on wake structure & dynamics.
2-5 TW, 2 ps
Probe
2) Upgrade CTS sensitivity to 1015 < ne < 1017 cm-3 plasmas,
using spatial-spectral filtering techniques developed at UCLA.
Filip et al., “CTS diagnostic system for detection of relativistic waves
in low-density plasmas,” Rev. Sci. Instrum. 74, 3576 (2003)
(AE95: CTS used only for ne ≥ 4 × 1017 cm-3)
3) Add a transverse CTS probe to complement current
co-propagating probe ⇒ diagnose wake evolution due to
self-focusing, mismatched propagation, wake formation,
electron injection, and beam loading.
4) Augment current 𝜆 = 1 µm probe with 𝜆 = 3, 5 µm probes
derived from 3rd, 2nd harmonics of split-off CO2 pulses
generated in AgGaSe2 crystals ⇒ improve sensitivity to
low-ne plasma structures, eliminate pu-pr timing jitter.
Detect with cooled InGaAs or InSb CCD camera.
multi-𝜆 (1-5 µm), multi-function (CTS, Faraday)
Proposed upgraded optical diagnostic system
• upgraded CTS + Faraday probes
• longitudinal + transverse probes
• 1 µm + 3, 5 µm CO2 harmonic probes
4

## Slide 5
Year 1-2 Scientific Goals (cont’d)
2) Upgrade optical diagnostics of wakes in low-ne plasma (cont’d)
2-5 TW, 2 ps
Probe
multi-𝜆 (1-5 µm), multi-function (CTS, Faraday)
5) Observe probe Faraday rotation due to kilo-T fields from
high peak currents ⇒ visualize magnetized plasma structures
at ne < 1017 cm-3.
Chang et al., “Faraday rotation study of plasma bubbles
in GeV wakefield accelerators,” Phys. Plasmas 28, 123105 (2021)
Proposed upgraded optical diagnostic system
• upgraded CTS + Faraday probes
• longitudinal + transverse probes
• 1 µm + 3, 5 µm CO2 harmonic probes
These upgraded diagnostics will
improve our ability to observe
large plasma bubbles in
ne ~ 1016 cm-3 plasma.
5
Development of effective diagnostics of low-ne wakes
is a forefront challenge for WFA science:
Downer et al., “Diagnostics for plasma-based electron accelerators,”
Rev. Mod. Phys. 90, 035002 (2018)

## Slide 6
(1) Chang et al., “Faraday rotation study of plasma bubbles in GeV wakefield accelerators,” Phys. Plasmas 28, 123105 (2021)
Faraday rotation can image plasma bubbles in low-ne plasma
ne > 1019 cm-3:
ne ≈ 1017 cm-3:
(2) Kaluza et al., Phys. Rev. Lett. 105, 115002 (2010);
(3) Buck et al., Nat. Phys. 7, 453 (2011).
Faraday “streaks” of magnetized plasma bubble walls
in ne ≈ 1017 cm-3 plasma
𝜏pr = 1-2 ps
Texas PW
drive pulse
ne ≈ 1017 cm-3
plasma
large B𝜑 and l
compensate
small ne/ncr(pr)
𝜏pr = 1 ps
𝜏pr = 2 ps
𝜏pr = 2 ps
at ne ≈ 1017 cm-3 ≥ observed at ne ≈ 1019 cm-3
𝜆pr = 1 µm
6
Texas
Petawatt

## Slide 7
Year 1-2 Scientific Goals (cont’d)
3) Understand ∆Ee/Ee, emittance growth in large bubbles thru simulations.
(a) ne = 1016 cm-3
0.5 ps CO2 pulse
(b)
(PhD student Yuxuan Cao)
(c) Electron Energy
(d)
Evolution of
Energy Spread (%)
2 externally
injected
e-bunches
• PIC simulations take a
long time --- too many
parameters to vary to
search for optimum.
• YC will develop machine-
learning approaches to
optimize the external
injection process, and
determine what ∆E/E and
emittance are achievable
in principle.
• YC will focus on quasi-
static bubbles.
FB-PIC simulations by Y. Cao
7

## Slide 8
OSIRIS* quasi-3D simulations show that large bubbles preserve energy spread
& spin polarization of strategically injected e-bunches during acceleration
Simulations by Z. Nie, F. Li and W. B. Mori (UCLA)
• Depolarization due to spin precession is ~ few %
• Depends on coordinates of injection point
spin-polarized
injected e-bunch
slightly depolarized
accelerated e-bunch
sz
sz
sx
sy
sx
sy
• Occurs predominantly from γ = 1 10, constant thereafter
sz
1.0
0.8
0.6
1
0.3
0
2
50
100
z [mm]
1.0
0.8
injection point
after acceleration
Fonseca et al., PPCF 55, 124011 (2013)
*
E = 65 MeV,
∆E = 0.5 MeV
injected e-bunch
E = 330 MeV,
∆E = 0.8 MeV
accelerated e-bunch
0.32
0.33
0.34
0.07
0.06
-6.0
-7.0
-6.5
longitudinal distance
z – ct [c/ωp]
electron energy
[GeV]
-6.0
-7.0
-6.5
longitudinal distance
z – ct [c/ωp]
electron energy
[GeV]
Simulation
parameters:
∆E/E ≈ 0.25%
∆E

## Slide 9
Year 3 Scientific Goal:
New capabilities: • CO2 laser: >10 J, 2 ps, > 5 TW
• linac e-beam probe synchronized, compressed to fs level?
• optical diagnostic system expanded and tested
1st generation CO2 LWFA
experiment with external
injection
Dream parameters:
1) 10 fs laser-e-beam rms jitter
2) e-bunch compression to 10 fs
3) 25 TW CO2 pulse
Actual parameters will depend
on status of laser and linac
development.

## Slide 10
SUMMARY
Year 1-2 goals:
1) Explore low-ne, high-PL limits of self-injected CO2-LWFA
2) Strengthen optical wake diagnostics for ne ~ 1016 cm-3 plasma
3) Simulate energy-spread, emittance growth in low-ne wakes
• relate ∆E, en growth to laser and plasma input parameters
• use maching-learning algorithms to hasten search for optimum
Year 3 goal:
1) 1st generation externally-injected CO2-LWFA experiment.
• use current (or slightly upgraded) CO2 laser parameters
• add transverse CTS, Faraday probes; MIR harmonics of CO2 drive pulse.
• take advantage of CO2 power upgrades & e-beam synchronization/compression advances
• leverages Navid’s work in developing e-beam probes
• a preparatory “Mercury” mission to build experience for a future “Apollo” moon-landing mission
10

## Slide 11
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 Regenerative Amplifier Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | n/a
 | Peak Power | GW | ~3 |  | n/a
 | Pulse Mode | --- | Single |  | 
 | Pulse Length | ps | 2 |  | 
 | Pulse Energy | mJ | 6 |  | 
 | M2 | --- | ~1.5 |  | 
 | Repetition Rate | Hz | 1.5 | 3 Hz also available if needed | 
 | Polarization | --- | Linear | Circular polarization available at slightly reduced power | 
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | ~9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 5 | ~5 TW operation will become available shortly into this year’s experimental run period. A 3-year development effort to achieve >10 TW and deliver to users is in progress. | initially ~5, higher by year 3.
 | Pulse Mode | --- | Single |  | single
 | Pulse Length | ps | 2 |  | 2 ps or shorter
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available within the next year | initially 5-10, higher by year 3
 | M2 | --- | ~2 |  | ~2
 | Repetition Rate | Hz | 0.05 |  | best available
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization can be provided upon request | Linear
CO2 Laser Requirements

## Slide 12
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | 50-65 (year 3 only)
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | adjust for shortest length & lowest emittance (yr 3 only)
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | ~100 fs or shorter, depending on developments by yr 3.
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | ~ 30 µm; exact value will depend on results of yr 1-2 research
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | as low as achievable
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | match CO2 laser rep. rate
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | single bunch
Electron Beam Requirements

## Slide 13
Ti:Sapphire Laser System | Units | Stage I Values | Stage II Values | Comments | Requested Values
Central Wavelength | nm | 800 | 800 | Stage I parameters are presently available and setup to deliver Stage II parameters should be complete during FY22 | 800 nm
FWHM Bandwidth | nm | 20 | 13 |  | 13 nm
Compressed FWHM Pulse Width | fs | <50 | <75 | Transport of compressed pulses will initially include a very limited number of experimental interaction points. Please consult with the ATF Team if you need this capability. | 75 fs
Chirped FWHM Pulse Width | ps | 50 | 50 |  | 50 ps
Chirped Energy | mJ | 10 | 200 |  | 10 mJ
Compressed Energy | mJ | 7 | ~20 | 20 mJ is presently operational with work underway this year to achieve our 100 mJ goal. | 7 mJ
Energy to Experiments | mJ | >4.9 | >80 |  | 5 mJ
Power to Experiments | GW | >98 | >1067 |  | 
Other Experimental Laser Requirements
Nd:YAG Laser System | Units | Typical Values | Comments | Requested Values
Wavelength | nm | 1064 | Single pulse | 
Energy | mJ | 5 |  | 
Pulse Width | ps | 14 |  | 
Wavelength | nm | 532 | Frequency doubled | 532 nm
Energy | mJ | 0.5 |  | 0.5 mJ
Pulse Width | ps | 10 |  | 2-3 ps

## Slide 14: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam | 0 | 0
NIR Laser | 60 | 140
LWIR Laser | 60 | 140
CY2024 Time Request
Capability | Setup Hours | Running Hours
Electron Beam | 60 (yr 3 only) | 140 (yr 3 only)
NIR Laser | 180 | 420
LWIR Laser | 180 | 420
Total Time Request for the 3-year Experiment (including CY2024-26)

## Slide 15: Special Equipment Requirements and Hazards
Electron Beam
  Please indicate any special equipment that you expect to need, including (but not limited to) the transverse deflecting cavity, shaped bunch using mask technique, plasma capillary discharge system, bolometer/interferometer setup etc.: best possible compression and synchronization with CO2 laser (yr 3)
CO2 Laser
  Please note any specialty laser configurations required here: polarization control, harmonics of split-off portions of beam generated in e.g. AgGaSe2
Ti:Sapphire and Nd:YAG Lasers
  Please note any specialty non-CO2 laser configurations required here: compressed Ti:S pulse at LWFA chamber
Hazards & Special Installation Requirements
  Large installation (chamber, insertion device, etc.): no
  Cryogens: no
  Introducing new magnetic elements: Spectrometer magnet, < 1 T
  Introducing new materials into the beam path: no
  Any other foreseeable beam line modifications: compressor for e-beam (yr 3)