## Slide 1: 26th Annual Accelerator Test Facility (ATF) Users' Meeting Closing Session
March 27, 2024
Science Priority Research Directions & Next Science Planning Workshop
Navid Vafaei-Najafabadi
Accelerator Facilities Division

## Slide 2: Synthesis
Priority research direction (PRDs) for the facility are determined through science planning workshops
The PRDs in turn define a set of core capabilities as targets for investment
In response to the previous workshop, major laser infrastructure upgrades were implemented to facilitate high-impact experiments, but electron beam facility upgrade is also needed to take full advantage of its capability in beam-driven and integrated experiments
Potential areas of emphasis for ATF consist of
Novel acceleration research with potentially expanding areas of focus in response to P5
Radiation generation research (e.g. ICS)
Basic physics research leveraging unique ATF capabilities & diagnostics (e.g. magnetic field evolution in plasma)
Development of laser technology from NIR to Mid-IR in response to DOE BRN
Industrial test bed for emerging devices & technologies (e.g. corrugated waveguides, ML, radiation characterization for NASA, etc)
The next workshop is planned for June 20-21 this year to gather community input on the future of science program at ATF

## Slide 3: ATF Science Planning Process
Goals:
  Determine the Priority Research Directions (PRDs) that can be leveraged to establish a priority-based upgrade path for the facility.
  Determine the set of parameters to best support the PRDs and enable the exploration of new Physics
Strategy
  Refine and update the PRDs using the community input through a series of Science Planning Workshops
  Determine a set of core capabilities and upgrades required for ATF facilities to best serve the research
2019 Report Editors:
  Navid Vafaei-Najafabadi (Stony Brook University)
  Michael Downer (University of Texas at Austin)
  David Sutter (University of Maryland)
  Gerard Andonian (University of California, Los Angeles)
  Aakash Sahai (University of Colorado)
2019Report: https://www.bnl.gov/atf/docs/ATF%20Science%20Workshop%20Report%202019.pdf

## Slide 4: Overview of Previous Priority Research Directions
Long-Wave Infrared (LWIR) Driven Science.
  LWIR Laser-Driven Plasma Ion Acceleration
  LWIR Laser-Driven Plasma Electron Acceleration
  Basic Plasma Physics Research in Novel Regimes
  LWIR Laser Technology Development
Electron-Beam-Driven Science
  Advanced Acceleration Research
  Beam Phase Space Optimization
  Low Emittance Source Development
  Novel and Efficient Terahertz Radiation Generation
Laser Electron Beam Interactions
  Basic Research of Laser-Plasma Charged-Lepton-Beam Production
  Electron Acceleration Techniques Driven by the Combination of Electron Beam and LWIR Laser
  Radiation Generation

## Slide 5: Review: Facility Needs
Experiment | LWIR Laser | e-beam
PRD A.1: Ion Acceleration | 10-25 TW: up to ~ 100 MeV ions Circ. Pol. for advanced methods | 
PRD A.2 e- Acceleration | 10-20 TW, <1ps: Blowout regime Integrated NIR: two color injection | 
PRD A.3 Weibel | 1 TW, ~3 ps, circ. Pol. | 
PRD B.1 Dielectric Wakefield Acceleration |  | , pC,
PRD B.1 Two Beam Acceleration (TBA) |  | nC, , total peak power> 60 MW
PRD B.2 Structure-based phase space manipulation |  | .
PRD B.2 fs beam manipulation | TEM_10 mode | 
PRD B.4 THZ Generation |  | , pC, , 6.4 cm period undulator: 1.5 mJ THz pulse
PRD C.1 e- injection into LWFA in blowout | 20 TW, 0.5 ps: Bubble regime | , 200: 100 MeV beam injection : ultrafast electron radiography
PRD C.1 e+ beam generation | 0.5-5 TW, ~2 ps, spot size w0~50-100 µm | >60 MeV, <1%, <50 µm, Q>250 pC, <10 µm, bunch length <0.2 ps
PRD C.2 Dielectric Laser Acceleration | 20 mJ, 2 ps, 10 Hz rep rate | 50 MeV, 1 pC, , m
PRD C.2 Direct Laser Acceleration | 20 TW, 0.5 ps: Bubble regime | 0.5 ps, nC: Drive beam fs, pC: Trailing beam
PRD C.3 Inverse Compton Scattering | Circular polarization: nonlinear ICS , linear polarization: harmonic radiation , any polarization: higher order multiphoton Thomson scattering | 50-75 MeV, m, C, rep rate 3Hz
Experiment | LWIR Laser | e-beam
PRD A.1: Ion Acceleration | 10-25 TW: up to ~ 100 MeV ions Circ. Pol. for advanced methods | 
PRD A.2 e- Acceleration | 10-20 TW, <1ps: Blowout regime Integrated NIR: two color injection | 
PRD A.3 Weibel | 1 TW, ~3 ps, circ. Pol. | 
PRD B.1 Dielectric Wakefield Acceleration |  | 
PRD B.1 Two Beam Acceleration (TBA) |  | 
PRD B.2 Structure-based phase space manipulation |  | 
PRD B.2 fs beam manipulation | TEM_10 mode | 
PRD B.4 THZ Generation |  | 
PRD C.1 e- injection into LWFA in blowout | 20 TW, 0.5 ps: Bubble regime | 
PRD C.1 e+ beam generation | 0.5-5 TW, ~2 ps, spot size w0~50-100 µm | 
PRD C.2 Dielectric Laser Acceleration | 20 mJ, 2 ps, 10 Hz rep rate | 
PRD C.2 Direct Laser Acceleration | 20 TW, 0.5 ps: Bubble regime | 
PRD C.3 Inverse Compton Scattering |  | 

## Slide 6: Review: Diagnostic Needs
Expanded Experimental Diagnostic Capabilities
  Plasma Diagnostics (interferometry, shadowgraphy,etc)
  Prepulse contrast diagnostics better than 4 orders of magnitude
  Characterization of high quality e-beams requires full e-trajectory recovery within a magnetic spectrometer’s energy-dispersion plane, e-beam polarimeters based on Møller e-e scattering from polarized ferromagnetic targets, and CTR-based 6D profiling of e- bunches.
  Radiation detectors, including KBr, MCPs, x-ray CCDs, and CsI scintillators with CCD, flux measurements, Crystal Si or CdTe average flux energy spectrometer, Single Shot Double differential diagnostic, Curved bent multi layer or Si & Quartz spectrometer, liquid scintillator detector in combination with single photon count PMT, and Compton magnet spectrometer
  Achievable through collaboration with users
Beam characterization: Transverse deflective cavity (T- CAV), 2 THz interferometry from coherent transition radiation (CTR), coherent diffraction/edge/Cerenkov radiation (CDR/CER/CCR)
Alignment and Synchronization Requirements for Multi-Beam Experiments
  Implementation of computer-based optimization technologies and accompanying high repetition rate are needed for achieving and maintaining high precision alignment and synchronization between the beams
Expanded Computational Capabilities
  Availability of user-friendly simulation codes for modelling short/long-term plasma dynamics, radiation production, and machine-learning tools for beam diagnostics and steering will be a great asset for users

## Slide 7: Major Infrastructure Upgrades Facilitate High-Impact Experiments

## Slide 8: Investments in Capability Upgrades
In response to the scientific plan, the facility has focused on development of capabilities with highest scientific payoff:
  R&D in LWIR laser technologies to achieve >20 TW, <1 ps pulse
  Integration of laser and beam sources for multi-beam experiments
  Implementation of integrated femtosecond (Ti:Sapphire) laser for enabling key experiments in accelerator science and plasma physics
Investment in stability and diagnostics for the electron beam are required to fully take advantage of its capability as a science driver as well as multi-beam integrated experiments

## Slide 9: Current Status and Future LWIR R&D
Science plan shows the promise of high-impact results at >20 TW, <1ps laser pulse
Aggressive R&D program has been put in place to meet this milestone, including
Achieved:
  Vacuum transport has enabled delivery of 5 TW to user IPs
Under Way
  Generating 100s of fs pulse through research in novel nonlinear pulse compression methods
  Development of solid-state seed (~10 mJ) enabling better use of CO2 gain bandwidth
  R&D in plasma optics (user collaboration) to supersede the gradual long-term degradation of compressor gratings
March 2019: 5 TW
M. N. Polyanskiy, I. V. Pogorelsky, M. Babzien, M. Palmer, "Demonstration of a 2 ps, 5 TW long-wave infrared laser based on chirped-pulse amplification with mixed-isotope CO2 amplifiers," (Submitted to “OSA Continuum”, Oct. 2019).
2018: 2 TW

## Slide 10: NonLinear Pulse Compression (NLPC)
measured within a central portion of the beam containing 30% of the total energy
Most powerful long-wave infrared sub-picosecond pulse ever obtained
Experiment
Pogorelsky et al. – Front. Phys. (accepted)
,

## Slide 11: LWIR laser infrastructure after upgrade
Seed Laser Table
Final amplifier
Shielding wall
Experimental Hall
CO2 Room
Flexible polarization rotator (FPR)
Compressor
FEL Room
CO2
YAG
Plasma shutter
Nonlinear pulse compressor
Test chamber
YAG
CO2
plasma

## Slide 12: Two Compressors Enable Integration of the Ti:Saph at User IPs

## Slide 13: Integration of Ti:Saph at ATF
Addition of Ti:Saph is represents an important upgrade in the capabilities of ATF

## Slide 14: Planning the Future Science at ATF

## Slide 15: Shifting Landscape: Notable Developments Since Previous Report*
Particle Physics Project Prioritization Panel (P5) report (2023, link) recommended “an aggressive R&D program … toward a cost-effective 10 TeV pCM collider based on proton, muon, or possible wakefield technologies”
Basic Research Needs Workshop on laser technology (2023, link) called for programs to transform Mid-IR Sources for Science from THz to X-Rays
Advanced computational assistive tools, primarily ML but also VR/AR, have emerged to guide human operators towards desired outcome (including laser and beam profiles tuning for particular experimental results)
*Title procured from suggestions by ChatGPT!

## Slide 17: Laser Technology
  DOE BRN on Laser Technology
    PRD 2: Transform Mid-IR Sources for Science from THz to X-Rays
    Key Questions: Can we create the new laser technologies needed to meet the significant demands for high average and peak power mid-infrared (mid-IR) science, and for driving secondary sources with extreme spectral coverage? How do we overcome the current limitations in mid-IR laser intensity to take full advantage of wavelength-dependent scalings? What are the ideal wavelengths, platforms, and architectures for nonlinear conversion to generate transformative sources in hard-to-access spectral ranges?
  Discussion underway with DOE ARDAP for the ATF to develop a plan to support mid-IR (2-10 mm) Laser Science & Technology development
  ATF Pivot: BNL Program Development funded effort to develop a new proposal for the future of the ATF
    Collaborative opportunity with the SBU ECE Department!

## Slide 18: PRD 2 Transform Mid-IR Sources for Science from THz to X-Rays
Thrust 1. Reducing complexity and increasing efficiency of mid-IR parametric sources
Reduce the complexity and increase efficiency of OPA and OPCPA Type III laser sources (particular emphasis on 2um sources)
Thrust 2. Scaling peak and average power in mid-IR CPA
Both Thrusts 1 and 2 emphasize Tm-, Ho-, Cr-, and Fe-doped amplifiers for high pulse and average energy
Thrust 3. Pushing peak power for CO2 -based laser accelerators
The inherent stability, scalability, and repetition-rate limitations associated with high-pressure gas discharge pumping represent significant scientific challenges. To reach the 50-TW level and beyond in the next decade, development of novel seed architectures for high-energy amplifiers and a shift towards optical pumping are immediately necessary.
3.1) Elevating the seed energy from the 10-μJ to the 10-mJ range
3.2) Peak power scaling through nonlinear compression
3.3) Optical pumping with kJ-class pump lasers
Thrust 4. Stable, waveform-controlled sources spanning the mid-IR to THz
Overlap with the “molecular fingerprint” region of the electromagnetic spectrum … allow[s] important applications to healthcare, energy, and defense based on trace-gas analysis in complex mixtures

## Slide 19: Opportunities in Advanced Computational Tools
Exascale High Performance Computing
Adaptive instruments based on ML and AI
Emerging virtual reality (VR) and augmented reality (AR) devices as design and training tools
AI for Science: Report on the Department of Energy (DOE) Town Halls on Artificial Intelligence (AI) for Science

## Slide 20: Science Planning Workshop, June 20-21, 2024
An in-person meeting to discuss priorities for the ongoing ATF program and an expanded mission footprint in response to the shifting science landscape
Our goal will be to further develop and refine priority research directions and set the facility development priorities for high-impact results
Community input will be requested for refining PRDs, focusing on research where
  ATF can make a unique contribution
  Expected research outcomes are significant
  ATF facilities are well-suited for carrying out the proposed research
The outcome of the workshop will be
  An assessment of new opportunities enabled by the upgraded capabilities of ATF facility
  An assessment of needs for future capabilities, which will in turn inform an upgrade path for capabilities delivered by ATF

## Slide 21: Science Opportunities
Basic (draft) Framework for science planning workshop
Novel acceleration research with potentially expanding areas of focus in response to P5
Radiation generation research (e.g. ICS)
Basic physics research leveraging unique ATF capabilities & diagnostics (e.g. magnetic field evolution in plasma)
Development of laser technology from NIR to Mid-IR in response to DOE BRN
Industrial test bed for emerging devices & technologies (e.g. corrugated waveguides, ML, radiation characterization for NASA, etc)
Two primary areas of unique strength for ATF
Extensive expertise in short-pulse, mid-wave and long-wave infrared laser science allows the facility to explore basic laser research and laser matter interaction in wavelength regimes that are simply inaccessible to other facilities
Integrated multi-beam experiments to explore novel plasma physics and radiation sources

## Slide 22: Integrated Multi-Beam Experiments
Integration of LWIR laser, NIR lasers and the e-beam simultaneously, allows any beam to be used as driver or diagnostic. This has enabled novel research, including
  Study of two-color ionization injection to enable an all-optical, high-brightness “photoinjectors”
  Visualization and field mapping inside LWIR-driven wakefield
  External injection of e-beam into LWIR-driven wake for frontier LWFA research
  Study of Inverse Compton Scattering in novel regimes
  Investigation of “laboratory astrophysics”, e.g. instabilities in plasma that also seed the magnetic fields in outer space plasma

## Slide 23
Experimental Setup for Magnetostatic Mode Visualization
motorized PMQs
5x obj
100 µm YAG:Ce
CCD (GPOP10)
camera lens
CO2 focus diag.
(Pyrocam IV)
shadowgraphy
CO2 laser, ~1 mJ to avoid ionizing H2
Ti:S focus diag.
IP
Ti:S main beam (~10 mJ, 80 fs)
Ti:S probe beam (<0.5 mJ, 80 fs)
e- beam
(50.5 MeV, ~0.2% energy spread

## Slide 24
t=60ps
Bx
By
Jz
Calculating magnetic fields and plasma currents
Weibel instability in the bounded plasma

## Slide 25: Electron Beam Facility Upgrades Required for Maintaining its Role as a Science Driver
Electron beam is a unique aspect of ATF.
The high-quality electron beam is valuable both as a science driver as well as a highly sensitive field probe in multi-beam integrated experiment
Desired electron beam capabilities
  Reliability: Recent klystron failures necessitate a long-term solution
  Stability: The next phase of multi-beam experiments will require a stable electron beam for interaction with the lasers and laser-driven plasma waves
  Integrated Diagnostic, including Transverse Deflecting Cavity (TCAV): As a gold standard of temporal variation in electron beam, a TCAV on the integrated line with CO2 and Ti:Saph is highly desired.
  Energy: Interactions with e-beam as driver generally greatly benefit from increased , so multi-fold increase in electron beam energy is desired.
Electron beam as a driver will be one of the primary areas for discussion at the science planning meeting

## Slide 26: Plans for the ATF Operational Improvements
LINAC and Timing System
  To support next generation multi-beam experiments
  Updating the ATF LINAC
    Expect the next 3 years to focus on replacement of aging LINAC hardware (XK-5 klystrons, old-style modulators, magnet systems) and timing system with new and improved hardware to enable true multi-beam operations with 10s of femtoseconds resolution
Toshiba E3730A, 50MW S-band Klystrons
Next Generation CAEN PS System for ATF Magnets
Cycle – Femtosecond Class Timing Distribution

## Slide 27: Summary
Priority research direction (PRDs) for the facility are determined through science planning workshops
The PRDs in turn define a set of core capabilities as targets for investment
In response to the previous workshop, major laser infrastructure upgrades were implemented to facilitate high-impact experiments, but electron beam facility upgrade is also needed to take full advantage of its capability in beam-driven and integrated experiments
Potential areas of emphasis for ATF consist of
Novel acceleration research with potentially expanding areas of focus in response to P5
Radiation generation research (e.g. ICS)
Basic physics research leveraging unique ATF capabilities & diagnostics (e.g. magnetic field evolution in plasma)
Development of laser technology from NIR to Mid-IR in response to DOE BRN
Industrial test bed for emerging devices & technologies (e.g. corrugated waveguides, ML, radiation characterization for NASA, etc)
The next workshop is planned for June 20-21 this year to gather community input on the future of science program at ATF

## Slide 28: The End

## Slide 29: Research Area A Facility Needs
Experiment | LWIR Laser | e-beam
PRD A.1: Ion Acceleration | 10 TW: ~ 10 MeV ions 25 TW: ~ 100 MeV ions Circ. Pol. For advanced methods (RPA, etc) | 
PRD A.2 e- Acceleration | 10 TW, 1ps: Blowout regime 20 TW, 0.5 ps: Bubble regime Integrated intense NIR: two color injection | 
PRD A.3 Weibel | 1 TW, ~3 ps, circ. Pol. | 
Expanded Diagnostic Capabilities
  Plasma Diagnostics (interferometry, shadowgraphy,etc)
  Prepulse contrast diagnostics better than 4 orders of magnitude
  Ultrafast electron radiography (See research area C for more discussion)
  Accurate synchronization and alignment diagnostics for multiple beams (See research area C for more discussion)

## Slide 30: Research Area B Facility Needs
Required Diagnostic Capabilities
  Beam characterization: Transverse deflective cavity (T- CAV), 2 THz interferometry from coherent transition radiation (CTR), coherent diffraction/edge/Cerenkov radiation (CDR/CER/CCR)
Experiment | LWIR Laser | e-beam
PRD B.1 Dielectric Wakefield Acceleration (DWA) |  | , pC, r.m.s
PRD B.1 Two Beam Acceleration (TBA) |  | nC, , total peak power> 60 MW
PRD B.2 Structure-based phase space manipulation |  | .
PRD B.2 fs beam manipulation | TEM_10 mode | 
PRD B.4 THZ Generation |  | , pC, , 6.4 cm period undulator: 1.5 mJ THz pulse
Experiment | LWIR Laser | e-beam
PRD B.1 Dielectric Wakefield Acceleration (DWA) |  | 
PRD B.1 Two Beam Acceleration (TBA) |  | 
PRD B.2 Structure-based phase space manipulation |  | 
PRD B.2 fs beam manipulation | TEM_10 mode | 
PRD B.4 THZ Generation |  | 

## Slide 31: Research Area C Facility Needs
Experiment | LWIR Laser | e-beam
PRD C.1 e- injection into LWFA in blowout | 20 TW, 0.5 ps: Bubble regime | , 200: 100 MeV beam injection : ultrafast electron radiography
PRD C.1 e+ beam generation | 0.5-5 TW, ~2 ps, spot size w0~50-100 µm | >60 MeV, <1%, <50 µm, Q>250 pC, <10 µm, bunch length <0.2 ps
PRD C.2 Dielectric Laser Acceleration | 20 mJ, 2 ps, 10 Hz rep rate | 50 MeV, 1 pC, , m
PRD C.2 Direct Laser Acceleration | 20 TW, 0.5 ps: Bubble regime | 0.5 ps, nC: Drive beam fs, pC: Trailing beam
PRD C.3 Inverse Compton Scattering | Circular polarization: nonlinear ICS , linear polarization: harmonic radiation , any polarization: higher order multiphoton Thomson scattering | 50-75 MeV, m, C, rep rate 3Hz
Experiment | LWIR Laser | e-beam
PRD C.1 e- injection into LWFA in blowout | 20 TW, 0.5 ps: Bubble regime | 
PRD C.1 e+ beam generation | 0.5-5 TW, ~2 ps, spot size w0~50-100 µm | 
PRD C.2 Dielectric Laser Acceleration | 20 mJ, 2 ps, 10 Hz rep rate | 
PRD C.2 Direct Laser Acceleration | 20 TW, 0.5 ps: Bubble regime | 
PRD C.3 Inverse Compton Scattering |  | 

## Slide 32: Electron and Ion Acceleration
Uniqueness of ATF Contribution
  LWIR laser is ideal for operating the LWFA in the blowout regime at low densities of 1016-1017 cm-3. The bubbles in this regime have a radius of hundreds of microns
  Low dark current (no self injection observed in simulations even at )
,
P=20 TW,
𝜏=0.5 ps,
cm-3

## Slide 33: Electron and Ion Acceleration
Uniqueness of ATF Contribution
  Hot electron yield is significantly higher with an LWIR laser (vs NIR), which plays a critical role in creating the force that will accelerate ions.
  Collisionless electrostatic shock acceleration has been an ongoing experiment at ATF with very promising results. Achieving 200 MeV at ~ 10 should be pursued as the primary goal.
  The critical density for an LWIR laser pulse (ne ~ 1019 cm-3 for λ = 10 μm) can be achieved by using supersonic gas targets as opposed to a solid target
Ion Acceleration at ATF

## Slide 34
Pulse compressed from 2 ps to 290 fs
Autocorrelator image
Proof-of-principle NLPC experiment
5 J
500 mJ
Principle Diagram of Full-Scale NLPC
5 TW
2 ps
KCl
5 cm
BaF2
5 cm
10 TW
500 fs
BaF2
lens
beam spatial filtering for higher uniformity
Opt. Express 29, 31714 (2021)

## Slide 35: Plasma Compression
Counter-propagate ATF CO2 and an ultra-short seed pulse with slightly longer wavelength
  Timing jitter must satisfy Δt << c/L, where L is the interaction length, L ~ 1 mm
Driven by ATF Ti:sapphire laser
Seed source
ATF CO2 Laser
Pump source
Demonstrate plasma compression of a CO2 laser pulse from 3 picoseconds to 0.15 picoseconds, with multi-terawatt peak power
Helium/Hydrogen
Ne = 5x1017 cm-3
L = 1.5 mm
100 nJ
11 micron
100 fs
Output:
0.5 J
11 micron
150 fs
9.2 micron, 3 J, 5 ps
35

## Slide 36: Experimental Setup for LWIR Seed Source
D.F. Gordon et al., Phys. Plasmas 28, 033104 (2021)
36

## Slide 37: Two-Color Ionization Injection
Uniqueness of ATF Contribution
Schroeder, European Conference on Lasers and Electro-Optics (2015)
Schroeder, PRSTAB 17, 101301 (2014)
Low emittance
  Drive laser needs large to form plasma wakefield, but we want low 𝐼 to avoid prematurely ionizing the gas
  Injector laser needs high 𝐼 to ionize the gas, but low to avoid disturbing the plasma
  >10x difference between the drive and injector wavelengths allows this to easily be achieved at ATF
  The large bubble driven by CO2 laser at low density simplifies alignment of the two lasers