## Slide 1
B0 Detectors
Zvi Citron for B0 team
Far-forward/ far-backward Review
Feb. 12, 2024

## Slide 2
B Detectors – Overview
Four layers of silicon tracker
EM Calorimeter

## Slide 3
B Detectors – Overview
Four layers of silicon tracker
EM Calorimeter
135 scintillating crystals
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Rails for installation & support
Readout & cable space
Credit: Jonathan Smith

## Slide 4
Forward (4.6<𝜂<5.9) charged tracking & proton tagging
Requirements:
  4 layers inside magnet bore (in the funny B0 geometry)
  Momentum resolution up to 6%
  Timing resolution sufficient to suppress background
  Radiation hard for forward environment
Detector design:
  4 layers of AC-LGAD
  27 cm spacing between layers, situated at front (IR side) of B0 magnet
B Detector – Tracking Detector

## Slide 5
Previous design called for 3 layers of MAPS (ITS3) + 1 layer AC-LGAD
Problems with MAPS
  Timing is too slow
  Covering the geometry would be difficult with default fabrication options, special geometry costly if possible
AC-LGAD
  Fast
  With charge sharing gives acceptable spatial resolution
  Technology overlap with Roman Pots, BNL expertise
Choice of AC-LGAD for Si Tracker

## Slide 6: B Detectors – Tracker Design and Status
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Note: momentum resolution (dp/p) is ~2-4%, depending on configuration.
Study by Alex Jentsch

## Slide 7: B Detectors – Tracker Design and Status
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution
Remaining Questions/optimization
Precise location/spacing still to be optimized
Previously assumed homogeneous B field in magnet bore
Reality is worse, would like all layers in “good” part of the field
Study by Alex Jentsch

## Slide 8
Forward (4.6<𝜂<5.9) photon and π0 measurement
Requirements:
  Fit inside magnet bore (in the funny B0 geometry)
  Sensitive down to 50 MeV
  Energy resolution
  Timing resolution sufficient to suppress background
  Radiation hard for forward environment
Detector design:
  135 LYSO crystals, each* 2x2x20 cm, situated 1m into magnet bore
B Detector – EM Calorimeter

## Slide 9
Considered PbWO4
  Slightly better energy containment (density = 8.3g/cm3, rad length =0.92 cm)
  Lower light yield at room T - O(10nγ/MeV), and high T sensitivity
LYSO
  Slightly worse E containment (density = 7.1g/cm3, rad length =1.12 cm)
  Better light yield O(103 nγ/MeV), stable to T
    Crucial for soft photons
  More expensive
Choice of LYSO for EM Calorimeter
Notes: Taiwan Applied Crystal has experience growing,wrapping, & preparing for CMS

## Slide 10: B Detectors – EMCal Design and Status
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM
135 scintillating crystals
Study by Michael Pitt

## Slide 11: B Detectors – EMCal Design and Status
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM
Study by Michael Pitt
Remaining Questions/optimization
Precise location still to be optimized
To make more room for tracker would like to push as far back as possible
  Outer radius crystals must be shorter to stay in mechanical envelope, lose radial acceptance

## Slide 12
B Detectors – Installation Concept
Credit: Jonathan Smith

## Slide 13
B Detectors – Installation Concept
Installation is non-trivial and staged
Detectors sit on rail for placement (and support)
Once upstream vacuum valve is closed only 10-15 cm of clearance
Crystals (20 cm long) installed before closing valve
After beam commissioning, rest of detector and electronics installed including coupling of SiPM to crystals

## Slide 14
B Detectors – Open Issues
Finalizing detector placement
Finalize cooling scheme
Tracker
  Confirming expectation of rad hardness (especially for charge sharing)
  Finalizing mechanics, cabling, etc
Calorimeter
  Finalizing readout (i.e. SiPM) and coupling
  Finalizing mechanics, cabling, etc

## Slide 15
B Detectors – Simulation Studies
Simulation of both detectors in standard ePIC framework
  Detector parameters can be adjusted
  Parameterized realistic magnetic field for tracking
Benchmarking with
  Particle gun
  Soft photons from BEAGLE, harder photons ,π0 , and protons from eSTARLIGHT (backwards DVCS mode)

## Slide 16
B Detectors – Summary
Baseline detector design and technology choice fixed
  Optimization ongoing
Basic installation/integration approach set
Simulation framework exists and simulations ongoing
Some finalization of supporting apparatus still to be done