## Slide 1
B0 Detectors
Zvi Citron for B0 team
Far-forward/ far-backward Review
Feb. 12, 2024

## Slide 2
B Detectors – Overview
Two detectors inside B0 magnet:
Four layers of silicon tracker
EM Calorimeter

## Slide 3
B Detectors – Overview
135 scintillating crystals
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Rails for installation & support
Readout & cable space
Credit: Jonathan Smith
Two detectors inside B0 magnet:
Four layers of silicon tracker
EM Calorimeter

## Slide 4
B Detectors – Simulation Status
Simulation of both detectors was developed in standard ePIC framework
  Detector parameters can be adjusted
  Parameterized realistic magnetic field for tracking
Benchmarking with
  Particle gun
  physical processes such as coherent/incoherent vector meson production, ep DVCS
Photon energy in lab frame [MeV]
Efficiency

## Slide 5
Requirements:
  Momentum resolution < 6%
  Radiation hard for forward environment
  Timing precision sufficient to deal with vertex smearing1
  Accommodate available mechanical envelope
Detector design:
  4 layers of AC-LGAD
    Use 3.2cm2 pixel sensors
    W/ charge sharing acceptable resolution
    Fast ~30 ps
  27 cm spacing between layers, situated at front (IR side) of B0 magnet
  (Serious consideration of MAPS but integration time is too slow  unacceptable background)
B Detector – Tracking Detector
Forward (4.6<𝜂<5.9) charged tracking & proton tagging
1See RP&OMD talk

## Slide 6: B Detectors – Tracker Design and Status
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Note: momentum resolution (dp/p) is ~2-4%, depending on configuration.
Study by Alex Jentsch
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution

## Slide 7: B Detectors – Tracker Design and Status
Remaining Questions/Optimization
Previously used homogeneous B field in magnet bore
Now optimizing detector positions/spacing for real B field2
Study by Alex Jentsch
Z [cm]
2More details in FF update
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution

## Slide 8
Requirements:
  Energy resolution
  Radiation hard for forward environment
  Sensitive to 50 MeV photons
  Accommodate available mechanical envelope
Detector design:
  135 Scintillating crystals , each* 2x2x20 cm, situated 1m into magnet bore
    LYSO and PbWO4 meet requirements
    Preference for LYSO for low energy measurements (and better T behavior)
B Detector – EM Calorimeter
Forward (4.6<𝜂<5.9) photon and π0 measurement

## Slide 9: B Detectors – EMCal Design and Status
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM
135 scintillating crystals
Study by Michael Pitt

## Slide 10: B Detectors – EMCal Design and Status
Study by Michael Pitt
Remaining Questions/Optimization
Precise location still to be optimized
To make more room for tracker would like to push as far back as possible
  Outer radius crystals must be shorter to stay in mechanical envelope, lose radial acceptance
Finalize coupling to readout device
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM

## Slide 11
B Detectors – Installation Concept
Credit: Jonathan Smith

## Slide 12
B Detectors – Installation Concept
Challenge: Detectors are inside magnet, with access only from the front (IR side), after vacuum valve is closed only 10-15 cm of clearance
 Installation is staged
  Crystals (20 cm long) installed before closing valve
  After beam commissioning (valve closed), rest of the detector(s) and electronics are installed including coupling of SiPM to (front of) crystals
Detectors sit on rails for installation and mechanical support

## Slide 13
B Detectors – Next Steps/Plan for 2024
Finalizing detector placement
Finalize cooling scheme (outside of vacuum – much simpler than RP)
Tracker
  Confirming expectation of rad hardness (especially for charge sharing)
  Finalizing mechanics, cabling, etc
Calorimeter
  Finalizing readout (i.e. SiPM) and coupling
  Finalizing mechanics, cabling, etc
ES&H
  No major challenges expected but full plan needs to be developed
Quality Assurance plans need to be developed
  AC-LGADs for tracker should by synchronized w/other detectors
  Testing regimen for crystals needs to be developed (possibly together with ZDC)

## Slide 14
B Detectors – Summary
Baseline detector design and technology choice fixed
  Some optimization ongoing
Basic installation/integration approach set
Simulation framework exists and simulations ongoing
Some finalization of supporting apparatus still to be done

## Slide 15
B Detectors – Backups

## Slide 16
PbWO4
  Slightly better energy containment (density = 8.3g/cm3, rad length =0.92 cm)
  Lower light yield at room T - O(10nγ/MeV), and high T sensitivity
  Read out in visible (>400 nm) with SiPM
LYSO
  Slightly worse E containment (density = 7.1g/cm3, rad length =1.12 cm)
  Better light yield O(103 nγ/MeV), stable to T
    Crucial for soft photons
  Read out in visible (>400 nm) with SiPM/APD
  More expensive
LYSO preference for EM Calorimeter
Notes: Taiwan Applied Crystal has experience growing,wrapping, & preparing for CMS