## Slide 1: B0 Detectors
EIC Preliminary Design & Safety Review of the EIC Auxiliary
Far-Forward/Far-Backward Detectors
February 12th, 2024
Zvi Citron for the B0 team

## Slide 2
B Detectors – Overview
Two detectors inside B0 magnet:
Four layers of silicon tracker
EM Calorimeter

## Slide 3
135 scintillating crystals
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Rails for installation & support
Readout & cable space
Credit: Jonathan Smith
Two detectors inside B0 magnet:
Four layers of silicon tracker
EM Calorimeter
B Detectors – Overview

## Slide 4
Simulation of both detectors was developed in standard ePIC framework
  Detector parameters can be adjusted
  Parameterized realistic magnetic field for tracking
Benchmarking with
  Particle gun
  physical processes such as coherent/incoherent vector meson production, ep DVCS
Photon energy in lab frame [MeV]
Efficiency
B Detectors – Simulation Status

## Slide 5
Requirements:
  Momentum resolution < 6%
  Radiation hard for forward environment
  Timing precision sufficient to deal with vertex smearing1
  Accommodate available mechanical envelope
Detector design:
  4 layers of AC-LGAD
    Use 3.2cm2 pixel sensors
    W/ charge sharing acceptable resolution
    Fast ~30 ps
  27 cm spacing between layers, situated at front (IR side) of B0 magnet
  (Serious consideration of MAPS but integration time is too slow  unacceptable background)
Forward (4.6<𝜂<5.9) charged tracking & proton tagging
1See RP&OMD talk
B Detectors – Tracking Detector

## Slide 6
4 Tracking layers, back-front overlapping arrangement to minimize dead area
Note: momentum resolution (dp/p) is ~2-4%, depending on configuration.
Study by Alex Jentsch
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution
B Detectors – Tracker Design & Status

## Slide 7
Remaining Questions/Optimization
Previously used homogeneous B field in magnet bore
Now optimizing detector positions/spacing for real B field2
Study by Alex Jentsch
Z [cm]
2More details in FF update
Four layers separated by 27 cm
Populated by pixilated AC-LGAD sensor with 20μm effective resolution
B Detectors – Tracker Design & Status

## Slide 8
Requirements:
  Energy resolution
  Radiation hard for forward environment
  Sensitive to 50 MeV photons
  Accommodate available mechanical envelope
Detector design:
  135 Scintillating crystals , each* 2x2x20 cm, situated 1m into magnet bore
  LYSO and PbWO4 meet requirements
  Preference for LYSO for low energy measurements (and better T behavior)
    CAVEAT: Not clear that LYSO crystals of reasonable size/cost can be obtained.
  Expect synergy w/other detectors
Forward (4.6<𝜂<5.9) photon and π0 measurement
B Detectors – EM Calorimeter

## Slide 9
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM
135 scintillating crystals
Study by Michael Pitt
B Detectors – EMCal Design & Status

## Slide 10
Study by Michael Pitt
Remaining Questions/Optimization
Precise location still to be optimized
To make more room for tracker would like to push as far back as possible
  Outer radius crystals must be shorter to stay in mechanical envelope, lose radial acceptance
Finalize coupling to readout device
135 crystals 2x2x20 cm crystals
Read out by front (IR side) coupled SiPM
B Detectors – EMCal Design & Status

## Slide 11
Credit: Jonathan Smith
B Detectors – Installation

## Slide 12
Challenge: Detectors are inside magnet, with access only from the front (IR side), after vacuum valve is closed only 10-15 cm of clearance
 Installation is staged
  Crystals (20 cm long) installed before closing valve
  After beam commissioning (valve closed), rest of the detector(s) and electronics are installed including coupling of SiPM to (front of) crystals
Detectors sit on rails for installation and mechanical support
B Detectors – Installation

## Slide 13
Finalizing detector placement
Finalize cooling scheme (outside of vacuum – much simpler than RP)
Tracker
  Confirming expectation of rad hardness (especially for charge sharing)
  Finalizing mechanics, cabling, etc
Calorimeter
  Finalizing readout (i.e. SiPM) and coupling
  Finalizing mechanics, cabling, etc
ES&H
  No major challenges expected but full plan needs to be developed
Quality Assurance plans need to be developed
  AC-LGADs for tracker should by synchronized w/other detectors
  Testing regimen for crystals needs to be developed (possibly together with ZDC)
B Detectors – Next Steps/Plan for 2024

## Slide 14
Baseline detector design and technology fixed
  Some optimization ongoing
Basic installation/integration approach set
Simulation framework exists and simulations ongoing
Some finalization of supporting apparatus still to be done
B Detectors – Summary

## Slide 15
B Detectors – Backups

## Slide 16
PbWO4
  Slightly better energy containment (density = 8.3g/cm3, rad length =0.92 cm)
  Lower light yield at room T - O(10nγ/MeV), and high T sensitivity
  Read out in visible (>400 nm) with SiPM
LYSO
  Slightly worse E containment (density = 7.1g/cm3, rad length =1.12 cm)
  Better light yield O(103 nγ/MeV), stable to T
    Crucial for soft photons
  Read out in visible (>400 nm) with SiPM/APD
  More expensive
B Detectors – LYSO vs PbWO4
Notes: Taiwan Applied Crystal has experience growing,wrapping, & preparing for CMS